PHYSICAL REVIEW D 94, 032003 (2016)
## Search for pair production of gluinos decaying via stop and sbottom in events with b-jets and large missing transverse momentum in pp collisions at ps = 13 TeV with the ATLAS detector
*
Aad et al.
(ATLAS Collaboration)
(Received 31 May 2016; published 9 August 2016)
A search for supersymmetry involving the pair production of gluinos decaying via third-generation
squarks to the lightest neutralino (p0) is reported. It uses an LHC proton-proton data set at a center-of-mass
energy P? = 13 TeV with an integrated luminosity of 3.2 fb-1 collected with the ATLAS detector in 2015.
The signal is searched for in events containing several energetic jets, of which at least three must be
identified as b jets, large missing transverse momentum, and, potentially, isolated electrons or muons.
Large-radius jets with a high mass are also used to identify highly boosted top quarks. No excess is found
above the predicted background. Forp0 masses below approximately 700 GeV, gluino masses of less than
1.78 TeV and 1.76 TeV are excluded at the 95% C.L. in simplified models of the pair production of gluinos
decaying via sbottom and stop, respectively. These results significantly extend the exclusion limits obtained
with the Ps = 8 TeV data set.
DOI: 10.1103/PhysRevD.94.032003
#### I. INTRODUCTION
Supersymmetry (SUSY) [1-6] is a generalization of
space-time symmetries that predicts new bosonic partners
to the fermions and new fermionic partners to the bosons of
the Standard Model (SM). If R parity is conserved [7],
SUSY particles are produced in pairs and the lightest
supersymmetric particle (LSP) is stable. The scalar partners
of the left- and right-handed quarks, the squarks qL and qR,
can mix to form two mass eigenstates q1 and q2, ordered by
increasing mass. SUSY can solve the hierarchy problem
[8-11] by preventing “unnatural” fine-tuning in the Higgs
sector provided that the superpartners of the top quark (stop,
t1 and ~2) have masses not too far above the weak scale.
Because of the SM weak isospin symmetry, the mass of the
left-handed bottom quark scalar partner (sbottom, bL) is tied
to the mass of the left-handed top quark scalar partner (~L),
and as a consequence the mass of the lightest sbottom b~ 1 is
also expected to be close to the weak scale. The fermionic
partners of the gluons, the gluinos (g), are also constrained
by naturalness [12,13] to have a mass around the TeV scale
to limit their contributions to the radiative corrections to the
stop masses. For these reasons, and because the gluinos are
expected to be pair produced with a high cross section at the
CERN Large Hadron Collider (LHC), the search for gluino
production with decays via stop and sbottom quarks is
highly motivated at the LHC.
*Full author list given at the end of the article.
Published by the American Physical Society under the terms of
the Creative Commons Attribution 3.0 License. Further distri-
bution of this work must maintain attribution to the author(s) and
the published article’s title, journal citation, and DOI.
This paper presents the search for gluino pair production
where both gluinos decay either to stops via g ^ tq t or to
sbottoms via g ^ b0b, using a data set of 3.2 fb-1 of
proton-proton data collected with the ATLAS detector [14]
at a center-of-mass energy of Ps = 13 TeV. Each stop
(sbottom) is then assumed to decay to a top (bottom) quark
and the LSP: t1 ^ tp0 (b0 ^ bp0). The LSP is assumed to
be the lightest neutralino p0, the lightest linear super-
position of the superpartners of the neutral electroweak and
Higgs bosons. The p0 interacts only weakly, resulting in
final states with substantial missing transverse momentum
of magnitude Em155. Diagrams of the simplified models
[15,16] considered, which are referred to as “Gbb” and
“Gtt” in the following, are shown in Figs. 1(a) and 1(b),
respectively. The sbottom and stop are assumed to be
produced off shell such that the gluinos undergo the three-
body decay g ^ bbp0 or g ^ tip0, and that the only
parameters of the simplified models are the gluino and
p0 masses.1
The Gbb experimental signature consists of four ener-
getic b jets (i.e., jets containing b hadrons) and large £miss-
In order to maintain high signal efficiency, at least three of
four required jets must be identified as b jets (b tagged).
This requirement is very effective in rejecting tt events,
which constitute the main background for both the Gbb and
Gtt signatures, and which contain only two b jets unless
they are produced with additional heavy-flavor jets. The Gtt
1Models with on-shell sbottom and stop were studied in Run 1
, and the limits on the gluino and thep0 masses were found to
be mostly independent of the stop and sbottom masses, except
when the stop is very light.
2470-0010/2016/94(3)/032003(32)
032003-1
© 2016 CERN, for the ATLAS Collaboration

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
t
### (a)
(b)
FIG. 1. The decay topologies in the (a) Gbb and (b) Gtt simplified models.
experimental signature also contains four b jets and Em“5,
but yields in addition four W bosons originating from the
top quark decays t ^ Wb. Each W boson can either decay
leptonically (W ^ 1v) or hadronically (W ^ qq0). A Gtt
event would therefore possess a high jet multiplicity, with
as many as 12 jets originating from top quark decays and,
potentially, isolated charged leptons. In this paper, pair-
produced gluinos decaying via stop and sbottom quarks are
searched for using events with high jet multiplicity, of
which at least three must be identified as b jets, large Em“8,
and either zero leptons (referred to as the Gtt 0-lepton
channel) or at least one identified charged lepton2 (referred
to as the Gtt 1-lepton channel). For both the Gbb and Gtt
models, several signal regions are designed to cover
different ranges of gluino and j0 masses. For the Gtt
models with a large mass difference (mass splitting)
between the gluino and j0, the top quarks tend to be
highly boosted and their decay products collimated. In the
corresponding signal regions, at least one large-radius,
trimmed [18] jet, which is reclustered from small-radius
jets [19], is required to have a high mass to identify
hadronically decaying boosted top quarks.
Pair production of gluinos, with subsequent decays via
sbottom quarks, was searched for in ATLAS Run 1 with a
similar analysis requiring at least three b-tagged jets [17]. It
excluded gluino masses below 1290 GeV for LSP masses
below 400 GeV at 95% confidence level (C.L.). That
analysis also searched for gluinos decaying via stop quarks
in events with at least three b-tagged jets and either zero or
at least one identified lepton and obtained the best ATLAS
limits for the Gtt models with massless and moderately
massive LSP [20]. Gluino masses below 1400 GeV were
excluded at 95% C.L. for LSP masses below 400 GeV. Pair-
produced gluinos with stop-mediated decays have also
been searched for by ATLAS in events with high jet
multiplicity [21], events with at least one lepton, many
jets, and £™ss [22], and events containing pairs of same-
sign leptons or three leptons [23], the latter obtaining the
best ATLAS limit for Gtt models with compressed mass
spectra between the gluino and the LSP in Run 1 [20] and
having since been performed in Run 2 [24].
Similar searches performed with the CMS experiment
using = 8 TeV [25-30] and = 13 TeV data [31-34]
have produced comparable results to ATLAS searches.
### II. ATLAS DETECTOR
The ATLAS detector is a multipurpose particle physics
detector with a forward-backward symmetric cylindrical
geometry and nearly 4n coverage in solid angle.3 The
inner tracking detector (ID) consists of pixel and silicon
microstrip detectors covering the pseudorapidity region
|n| < 2.5, surrounded by a transition radiation tracker,
which enhances electron identification in the region
|n| < 2.0. Before the start of Run 2, the new innermost
pixel layer, the Insertable B-Layer (IBL) [35], was inserted
at a mean sensor radius of 3.3 cm. The ID is surrounded by
a thin superconducting solenoid providing an axial 2 T
magnetic field and by a fine-granularity lead/liquid-argon
(LAr) electromagnetic calorimeter covering |n| < 3.2.
A steel/scintillator-tile calorimeter provides coverage for
hadronic showers in the central pseudorapidity range (|n| <
1.7). The end cap and forward regions (1.5 < |n| < 4.9) of
the hadronic calorimeter are made of LAr active layers with
either copper or tungsten as the absorber material. A muon
spectrometer with an air-core toroid magnet system sur-
rounds the calorimeters. Three layers of high-precision
tracking chambers provide coverage in the range |n| < 2.7,
The term “lepton” refers exclusively to an electron or a muon
in this paper.
3ATLAS uses a right-handed coordinate system with its origin
at the nominal interaction point in the center of the detector. The
positive x axis is defined by the direction from the interaction
point to the center of the LHC ring, with the positive y axis
pointing upwards, while the beam direction defines the z axis.
Cylindrical coordinates (r, <p) are used in the transverse plane, <p
being the azimuthal angle around the z axis. The pseudorapidity n
is defined in terms of the polar angle 0 by n = — lntan(0/2).
032003-2

SEARCH FOR PAIR PRODUCTION OF GLUINOS
PHYSICAL REVIEW D 94, 032003 (2016)
while dedicated fast chambers allow triggering in the region
|n| < 2.4. The ATLAS trigger system [36] consists of a
hardware-based Level-1 trigger followed by a software-
based high level trigger.
#### III. DATA AND SIMULATED EVENT SAMPLES
The data used in this analysis were collected by the
ATLAS detector from pp collisions produced by the
LHC at a center-of-mass energy of 13 TeV and 25 ns
proton bunch spacing. The full data set corresponds to an
integrated luminosity of 3.2 fb—1 with an associated uncer-
tainty of ±5%, after requiring that all detector subsystems
were operational during data recording. The measurement
of the integrated luminosity is derived, following a meth-
odology similar to that detailed in Ref. [37], from a
calibration of the luminosity scale using a pair of x-y
beam-separation scans performed in June 2015. Events are
required to pass an ETmiss trigger that is fully efficient for
events passing the preselection defined in Sec. . Each
event includes on average 14 additional inelastic pp
collisions (“pileup”) in the same bunch crossing.
Simulated event samples are used to model the signal
and background processes in this analysis. The signal
samples for the Gbb and Gtt processes are generated with
up to two additional partons using MADGRAPH5_aMC @nlo
v2.2.2 at leading order (LO) with CTEQ6L1 [39]
parton density function (PDF) sets and interfaced to PYTHIA
v8.186 [40] for the modeling of the parton showering,
hadronization, and underlying event.
The dominant background in the signal regions is the
production of tt pairs with additional high-pT jets. The
sample for the estimation of this background is generated
using the powheg-box [41,42] generator at next-to-leading
order (NLO) with CT10 [43] PDFs and interfaced to
PYTHIA v6.428 [44] for showering and hadronization. The
decays of heavy-flavor hadrons are modeled using the
evtgen [45] package. The hdamp parameter in powheg,
which controls the pT of the first additional emission
beyond the Born level and thus regulates the pT of the
recoil emission against the tt system, is set to the mass of
the top quark (mtop = 172.5 GeV). This setting was found
to give the best description of the pT of the tt system at
PS = 7 TeV [46] and Ps = 8 TeV [47]. All events with at
least one semileptonically decaying top quark are included.
Fully hadronic tt events do not contain sufficient Em188 to
contribute significantly to the background.
Smaller backgrounds in the signal region come from the
production of tt pairs in association with W/Z/h and
additional jets, single-top production, production of tftf,
W/Z + jets and WW/WZ/ZZ (diboson) events. The
production of tft pairs in association with electroweak
vector bosons and tttf production are modeled by samples
generated using madgraph [48] interfaced to pythia
v8.186, while samples to model tth production are gen-
erated using MADGRAPH5_aMC@NLO [38] v2.2.1 and show-
ered with herwig++ [49] v2.7.1. Single-top production in
the s, t, and Wt channels is generated by powheg-box
interfaced to pythia v6.428. W/Z + jets and diboson
processes are simulated using the sherpa v2.1.1 [50]
generator with CT10 PDF sets. Matrix elements for these
processes are calculated using the Comix [51] and
openLoops [52] generators and merged with the
sherpa parton shower [53] using the ME + PS@NLO
prescription [54].
All simulated event samples, with the exception of the
Gbb signals, are passed through the full ATLAS detector
simulation using GEANT4 [55,56]. The Gbb signal samples
are passed through a fast simulation that uses a para-
metrized description to simulate the response of the
calorimeter systems [57]. The simulated events are recon-
structed with the same algorithm as that used for data. All
pythia v6.428 samples use the PERUGIA2012 [58] set of
tuned parameters (tune) for the underlying event, while
pythia v8.186 and herwig++ showering are run with the
A14 [59] and UEEE5 [60] underlying-event tunes, respec-
tively. In-time and out-of-time pileup interactions from the
same or nearby bunch crossings are simulated by over-
laying additional pp collisions generated by pythia v8.186
on the hard-scattering events. Details of the sample gen-
eration and normalization are summarized in Table I.
Additional samples with different generators and settings
TABLE I. List of generators used for the different background processes. Information is given about the pQCD highest-order accuracy
used for the normalization of the different samples, the underlying-event tunes and PDF sets considered.
Process	Generator + fragmentation/hadronization	Tune	PDF set	Cross-section
if	POWHEG-BOX v2 + PYTHIA-6.428	PERUGIA2012	CT10	NNLO + NNLL [61]
Single top	POWHEG-BOX v2 + PYTHIA-6.428	PERUGIA2012	CT10	NNLO + NNLL [62-64]
tfW/ttZ/4-tops	MADGRAPH-2.2.2 + PYTHIA-8.186	A14	NNPDF2.3 [65]	NLO
tfh	MADGRAPH5_aMC @NLO- 2.2.1 + HERWIG++-2.7.1	UEEE5	CT10	NLO [66]
Dibosons / WW, WZ, ZZ	SHERPA-2.1.1	Default	CT10	NLO
W/Z+jets	SHERPA-2.1.1	Default	CT10	NNLO [67]

032003-3

G. AAD et al.
are used to estimate systematic uncertainties on the back-
grounds, as described in Sec. VI.
The signal samples are normalized using the best cross
sections calculated at NLO in the strong coupling constant,
adding the resummation of soft gluon emission at next-to-
leading-logarithmic (NLL) accuracy [68-72]. The nominal
cross section and the uncertainty are taken from an
envelope of cross-section predictions using different
PDF sets and factorization and renormalization scales, as
described in Ref. [73]. The cross section of gluino pair
production in these simplified models is approximately
325 fb for a gluino mass of 1 TeV, falling to 2.8 fb for
1.8 TeV mass gluinos. All background processes are
normalized to the best available theoretical calculation
for their respective cross sections. The order of this
calculation in perturbative QCD (pQCD) for each process
is listed in Table I.
#### IV. OBJECT RECONSTRUCTION
Interaction vertices from the proton-proton collisions are
reconstructed from at least two tracks with pT > 0.4 GeV
and are required to be consistent with the beam spot
envelope. The primary pp interaction vertex is identified
as the one with the largest sum of squares of the transverse
momenta from associated tracks (Jg |pT;track|2) [74].
Basic selection criteria are applied to define candidates
for electrons, muons, and jets in the event. An overlap
removal procedure is applied to these candidates to prevent
double counting. Further requirements are then made to
select the final signal leptons and jets from the remaining
objects. The details of the object selections and of the
overlap removal procedure are given below.
Candidate jets are reconstructed from three-dimensional
topological energy clusters [75] in the calorimeter using the
anti-kt jet algorithm [76] with a radius parameter of 0.4
(small-R jets). Each topological cluster is calibrated to the
electromagnetic scale response prior to jet reconstruction.
The reconstructed jets are then calibrated to the particle
level by the application of a jet energy scale (JES) derived
from simulation and corrections based on 8 TeV data
[77,78]. Quality criteria are imposed to reject events that
contain at least one jet arising from noncollision sources or
detector noise [79]. Further selections are applied to reject
jets that originate from pileup interactions [80]. Candidate
jets are required to have pT > 20 GeV and |n| < 2.8.
Signal jets, selected after resolving overlaps with electrons
and muons, are required to satisfy the stricter requirement
of pT > 30 GeV.
A multivariate algorithm using information about the
impact parameters of inner detector tracks matched to the
jet, the presence of displaced secondary vertices, and
the reconstructed flight paths of b and c hadrons inside
the jet [81-83] is used to tag b jets. The b tagging working
point with an 85% efficiency, as determined from a
simulated sample of tt events, was found to be optimal.
PHYSICAL REVIEW D 94, 032003 (2016)
The corresponding rejection factors against jets originating
from c quarks, from t leptons, and from light quarks and
gluons in the same sample at this working point are 2.6, 3.8,
and 27, respectively.
The candidate small-R jets are used as inputs for further
jet reclustering [19] using the anti-kt algorithm with a
radius parameter of 1.0. These reclustered jets are then
trimmed [18,19] by removing subjets whose pT falls below
fcut = 5% of the pT of the original reclustered jet. The
resulting large-R jets are used to tag high-pT boosted top
quarks in the event. Selected large-R jets are required to
have pT > 300 GeV and to have |n| < 2.0. A large-R jet is
tagged as a top candidate if it has a mass above 100 GeV.
The mass of the large-R jets is computed from the four-
momentum sum of its constituent small-R jets, and the
mass of the small-R jets are computed from the four-
momentum sum of the topological clusters that make up
the jet, which are assumed to be massless. When it is not
explicitly stated otherwise, the term “jets” in this paper
refers to small-R jets.
Electron candidates are reconstructed from energy clus-
ters in the electromagnetic calorimeter and inner detector
tracks and are required to satisfy a set of “loose” quality
criteria [84-86]. They are also required to have |n| < 2.47.
Muon candidates are reconstructed from matching tracks in
the inner detector and in the muon spectrometer. They are
required to meet “medium” quality criteria, as described in
Refs. [87,88] and to have |n| < 2.5. All electron and muon
candidates must have pT > 20 GeV and survive the over-
lap removal procedure. Signal leptons are chosen from the
candidates with the following isolation requirement—the
scalar sum of pT of additional inner detector tracks in a
cone around the lepton track is required to be < 5% of
the lepton pT. The angular separation between the lepton
and the b jet ensuing from a semileptonic top quark decay
narrows as the pT of the top quark increases. This increased
collimation is accounted for by varying the radius of
the isolation cone as max(0.2,10/pp), where pp is the
lepton pT expressed in GeV. Signal electrons are further
required to meet the “tight” quality criteria, while signal
muons are required to satisfy the same medium quality
criteria as the muon candidates. Electrons (muons) are
matched to the primary vertex by requiring the transverse
impact parameter d0 to satisfy |d0|/pd0) < 5 (3), where
pd0) is the measured uncertainty in d0, and the longi-
tudinal impact parameter z0 to satisfy |z0 sin 0| < 0.5 mm
In addition, events containing one or more muon candidates
with |d0| > 0.2 mm and |z0| > 1 mm are rejected to
suppress cosmic rays.
The overlap removal procedure between muon and jet
candidates is designed to remove those muons that are
likely to have originated from the decay of hadrons and to
retain the overlapping jet. Jets and muons may also appear
in close proximity when the jet results from high-pT muon
bremsstrahlung, and in such cases the jet should be
032003-4

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...
removed and the muon retained. Such jets are characterized
by having very few matching inner detector tracks.
Therefore, if the angular distance AR between a muon
and a jet is within min(0.4, 0.04 + 10 GeV/pT) of the axis
of a jet,4 the muon is removed only if the jet has >3
matching inner detector tracks. If the jet has fewer than
three matching tracks, the jet is removed and the muon is
kept [89]. Overlap removal between electron and jet
candidates aims to remove jets that are formed primarily
from the showering of a prompt electron and to remove
electrons that are produced in the decay chains of hadrons.
Since electron showers within the cone of a jet contribute to
the measured energy of the jet, any overlap between an
electron and the jet must be fully resolved. A pT -dependent
cone for the purpose of this overlap removal is thus
impractical. Consequently, any non-b-tagged jet whose axis
lies AR < 0.2 from an electron is discarded. If the electron is
within AR = 0.4 of the axis of any jet remaining after this
initial overlap removal procedure, the jet is retained and the
electron is removed. Finally, electron candidates that lie
AR < 0.01 from muon candidates are removed to suppress
contributions from muon bremsstrahlung.
The missing transverse momentum (ETmiss) in the event is
defined as the magnitude of the negative vector sum
transverse momentum (p>Tmiss) of all selected and calibrated
objects in the event, with an extra term added to account for
soft energy that is not associated with any of the selected
objects. This soft term is calculated from inner detector
tracks matched to the primary vertex to make it more
resilient to contamination frompileup interactions [90,91].
Corrections derived from data control samples are applied
to simulated events to account for differences between
data and simulation in the reconstruction efficiencies,
momentum scale, and resolution of leptons [85-87,92]
and in the efficiency and false positive rate for identifying
b jets [82,83].
#### V. EVENT SELECTION
The event selection criteria are defined based on kin-
ematic requirements on the objects defined in Sec. IV and
on the following event variables.
Two effective mass variables are used, which would
typically have much higher values in pair-produced gluino
events than in background events. The Gtt signal regions
employ the inclusive effective mass mfc\
incl
'eff
= 53 PTjeti+53 r/;+e™
where the first and second sums are over the signal jets
and leptons, respectively. The signal regions for the Gbb
4ar = a/ (An)2 + (A|)2 defines the distance between objects
in (n, |) space.
PHYSICAL REVIEW D 94, 032003 (2016)
models, for which four high-pT b jets are expected, are
defined using mf
# mf = 53 pTjSti + ET,
¡<4
where the sum is over the four highest-pT (leading) signal
jets in the event.
In regions with at least one signal lepton, the transverse
mass mT of the leading signal lepton (l) and E™ss is used to
discriminate between the signal and backgrounds from
semileptonic tf and W + jets events,
# y^pTErfl - costA^RT™55, l)]}.
mT =
Neglecting resolution effects, mT is bounded from above by
the W boson mass for these backgrounds and typically has
higher values for Gtt events. Another useful transverse
mass variable is mT—m^, the minimum transverse mass
formed by ETmiss and any of the three leading b-tagged jets
in the event,
m
b-jets
T,min
= mm¿<3
E™55!! - cos[A^(RTmiss,b-jet¿)]} .
It is bounded below the top quark mass for semileptonic
tft events while peaking at higher values for Gbb and Gtt
events.
The signal regions require either zero or at least one
lepton. The requirement of a signal lepton, with the
additional requirements on jets, ETmiss, and event variables
described in Sec. VA, render the multijet background
negligible for the > 1-lepton signal regions. For the
lepton signal regions, the minimum azimuthal angle
between p>Tmiss and the leading four small-R jets in the
event, A^^n, is required to be greater than 0.4,
A|min = min(||jet1 — |p~rmiss |,	||jet4	— |p'Tmiss |) > °.+
This requirement ensures that the multijet background,
which can produce large ETmiss if containing poorly mea-
sured jets or neutrinos emitted close to the axis of a jet, is
also negligible in the 0-lepton signal regions (along with
the other requirements on jets, ETmiss, and event variables
described in Sec. VA).
Figure 2 shows the kinematic distributions of ETmiss,
„incl
eff ,
b- jets
T;min,
and mT for a preselection that requires
ETmiss > 200 GeV, at least four signal jets of which at least
three must be b tagged, and A|mn > 0.4. Figure 3 shows
the multiplicity of signal jets, b-tagged signal jets, top-
tagged large-R jets, and signal leptons in the preselection.
032003-5

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
FIG. 2. Distributions of kinematic variables in the preselection region described in the text: (a) E™^, (b) mf, (c) mT-e^, and (d) mT
(for preselected events with at least one signal lepton). The statistical and experimental systematic uncertainties are included in the
uncertainty band, where the systematic uncertainties are defined in Sec. VI. The lower part of each figure shows the ratio of data to the
background prediction. All backgrounds (including tt) are normalized using the best available theoretical calculation described in
Sec. III. The background category “Others” includes tth, tttt, and diboson events. Example signal models with cross sections enhanced
by a factor of 100 are overlaid for comparison.
Good agreement between data and simulation is observed.
Example signal models with enhanced cross sections are
overlaid for comparison.
### A. Signal regions
The signal regions are designed by optimizing the
expected signal discovery reach for the 2015 data set.
They are defined in the leftmost column of Tables II, III,
and IV for the Gbb, Gtt 0-lepton, and Gtt 1-lepton channels,
respectively, and are discussed below. These tables also
contain the definition of the control regions used to
normalize the tt background, discussed in Sec. V B, and
the validation regions used to cross-check the background
estimate and which are discussed in Section V C. The
following region nomenclature is used in the remainder of
the paper. Signal, control, and validation region names start
with the prefix “SR,” “CR,” and “VR,” respectively, and
with the type of validation region specified for the Gtt
validation regions. The name of the region is completed by
the type of model targeted and a letter corresponding to
the level of mass splitting between the gluino and the LSP.
For example the validation region that cross-checks the
extrapolation over mT for the Gtt 1-lepton region A is
denoted by “VR-mT-Gtt-1L-A.”
The experimental signature for the Gbb model is
characterized by four high-pT b jets, large ETmiss, and no
leptons [Fig. 1(a)]. The following requirements are applied
to all Gbb signal regions. Events containing a candidate
lepton are vetoed and at least four signal small-R jets are
required, of which at least three must be b tagged. The
remaining multijet background is rejected by requiring
A^nlin > 0 4. The Gbb signal regions are described in the
leftmost column of Table II. The three signal regions A, B,
and C are designed to cover Gbb models with large
(>1 TeV), moderate (between «200 GeV and «1 TeV),
and small (<200 GeV) mass splittings between the gluino
032003-6

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...
PHYSICAL REVIEW D 94, 032003 (2016)
FIG. 3. Distributions of the number of (a) signal jets, (b) b-tagged jets, (c) top-tagged large-R jets, and (d) signal leptons in the
preselection region described in the text. The statistical and experimental systematic uncertainties are included in the uncertainty band,
where the systematic uncertainties are defined in Sec. VI. The lower part of each figure shows the ratio of data to the background
prediction. All backgrounds (including tt) are normalized using the best available theoretical calculation described in Sec. III. The
background category “Others” includes tth, tttt, and diboson events. Example signal models with cross sections enhanced by a factor of
100 are overlaid for comparison.
and the LSP, respectively. All regions feature stringent cuts
on Emss,	and the jet transverse momentum p-É1.
The experimental signature for the Gtt model is char-
acterized by several high-pT jets of which four are b jets,
large	and potentially leptons [Fig. 1(b)]. The Gtt
signal regions are classified into regions with a signal
lepton veto (0-lepton channel) and regions with at least one
signal lepton (1-lepton channel). The Gtt 0-lepton signal
regions are defined in the leftmost column of Table III. In
all Gtt 0-lepton signal regions at least eight signal jets,
> 0.4 and mT-m^ > 80 GeV are required. Three Gtt
lepton signal regions are defined to cover Gtt models
with decreasing mass splitting between the gluino and the
sum of the mass of the two top quarks and the LSP: A
(>1 TeV), B (between «200 GeV and «1 TeV), and C
(<200 GeV). In the large and moderate mass splitting
scenarios, the top quarks tend to have a large pT, and at
least one top-tagged large-R jet is required (Ntop > 1). The
requirements on £™ss and mef decrease with the mass
splitting between the gluino and the LSP. However, the
required number of b-tagged jets Nb-jet is tightened to four
for the lower mass splitting regions B and C in order to
maintain a high background rejection despite the softer
signal kinematics.
The Gtt 1-lepton signal regions are defined in the
leftmost column of Table I . Two signal regions A and
B are defined to cover Gtt models with decreasing
mass difference between the gluino and the LSP. In all
signal regions at least one signal lepton, at least six signal
jets (pTjet > 30 GeV), and mT > 150 GeV are required.
Region A has tighter requirements on mf (mef >
1100 GeV) and the number of top-tagged large-R jets
(Ntop > 1). Region B has a softer requirement on mf than
region A, but it features a tighter cut on Em“8 to achieve a
satisfactory background rejection without requiring a top-
tagged large-R jet.
032003-7

G. AAD et al.	PHYSICAL	REVIEW	D	94,	032003	(2016)
TABLE II. Definitions of the Gbb signal, control, and validation regions. The unit of all kinematic variables is GeV except Ai^n:
which is in radians. The jet pT requirement is also applied to b-tagged jets.
Criteria common to all Gbb regions:	> 4 signal jets, >3b-tagged jets
	Variable	Signal region	Control region	Validation region
Criteria common to all regions of the same type	^Candidate Lepton ^Signal Lepton / A^inin / b-jets / mT • / T,min / mj	= 0 > 0.4	= 1 / < 150	= 0 / >0.4 < 160
Region A / (Large mass splitting)	Pt1* / £miss / 4j / meff	90 / 350 / 1600	90 / 250 / 1200	> 90 >250 < 1400
Region B / (Moderate mass splitting)	Pt1* / £miss / T4j / meff	90 / 450 / 1400	90 / 300 / 1000	90 / 300 < 1400
Region C / (Small mass splitting)	Pt1* / £miss / T4j / meff	30 / 500 / 1400	30 / 400 / 1200	30 / 400 < 1400

#### B. Background estimation and it control regions
The largest background in all signal regions is it
produced with additional high-pT jets. The other relevant
backgrounds are itW, itZ, itit, ith, single-top, W + jets,
Z + jets, and diboson events. All of these smaller
backgrounds are estimated with the simulated event sam-
ples normalized to the best available theory calculations
described in Sec. III. The multijet background is estimated
to be negligible in all regions.
For each signal region, the ii background is normalized
in a dedicated control region. The it normalization factor
TABLE III. Definitions of the Gtt 0-lepton signal, control, and validation regions. The unit of all kinematic variables is GeV except
Aj which is in radians. The jet pT requirement is also applied to b-tagged jets.
Criteria common to all Gtt 0-lepton regions: pT^et	> 30 GeV
	Variable	Signal region	Control region	VR1L	VR0L
Criteria common to all regions of the same type	^Signal Lepton	=0	= 1	= 1	= 0
	A^m. / min	> 0.4			> 0.4
	Njet	> 8	>7	>7	>8
	b-jets / mT,min	> 80		> 80	< 80
	mT		< 150	< 150
Region A (Large mass splitting)	£miss	> 400	> 250	> 250	> 200
	mincl / meff	> 1700	> 1350	> 1350	> 1400
	Nb-tag	>3	>3	>3	>2
		>1	>1	>1	>1
Region B (Moderate mass splitting)	£miss	> 350	> 200	> 200	> 200
	mincl / meff	> 1250	> 1000	> 1000	> 1100
	Nb-tag	>4	>4	>4	>3
		>1	>1	>1	>1
Region C (Small mass splitting)	Emiss	> 350	> 200	> 200	> 200
	mincl / eff	> 1250	> 1000	> 1000	> 1250
	Nb-tag	>4	>4	>4	>3

032003-8

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...	PHYSICAL	REVIEW	D	94,	032003	(2016)
TABLE IV. Definitions of the Gtt 1-lepton signal, control, and validation regions. The unit of all kinematic variables is GeV. The jet pT
requirement is also applied to b-tagged jets.
Criteria common to all Gtt 1-lepton regions: > 1 signal lepton, pTjet > 30 GeV
	Variable	Signal region	Control region	VR-mT	b-jets / VR-mT,min
Criteria common to all regions of the same type	mT	> 150	< 150	> 150	< 150
	Njet	> 6	=6	>5	>6
	Nb-tag	> 3	>3	=3	=3
Region A (Large mass splitting)	Emiss	> 200	> 200	> 200	> 200
	mincl / meff	> 1100	> 1100	> 600	> 600
	b-jets / mT,mrn	> 160		< 160	> 140
		>1	>1	>1	>1
Region B (Moderate to small mass splitting)	Emiss	> 300	> 300	> 200	> 200
	mincl / eff	> 900	> 900	> 600	> 600
	b-jets / mT,mrn	> 160		< 160	> 160

required for the total predicted yield to match the data in
the control region is used to normalize the it background in
the signal region. The control regions are designed to be
dominated by iti events and to have negligible signal
contamination, while being kinematically as close as
possible to the corresponding signal region. The latter
requirement minimizes the systematic uncertainties asso-
ciated with extrapolating the normalization factors from the
control to the signal regions.
The definitions of the control regions are shown next to
the signal regions in Tables II, III, and IV for the Gbb, Gtt
1. lepton, and Gtt 1-lepton channels, respectively. In both
   the Gbb and Gtt 0-lepton channels, exactly one signal
   lepton is required. This is motivated by background
   composition studies using simulated events which show
   that semileptonic iti events, for which the lepton is outside
   the acceptance or is a hadronically decaying t lepton,
   dominate the it yield in the signal regions. An upper cut
   on mT is then applied to ensure orthogonality with the Gtt
2. lepton signal regions and to suppress signal contamina-
   tion. The jet multiplicity requirement is reduced to seven
   jets in the Gtt 0-lepton control regions (from eight jets in the
   signal regions), to accept more events and to obtain a
   number of jets from top quark decay and parton shower
   similar to that in the signal region. Approximately 40%-
   60% of the signal region events contain a hadronically
   decaying t lepton that is counted as a jet. Orthogonality
   between Gtt 0-lepton and Gtt 1-lepton control regions is
   ensured by requiring exactly six jets in the Gtt 1-lepton
   control regions (as opposed to the requirement of at least
   six jets in the signal regions). For all Gbb and Gtt 0-lepton
   control regions, the number of b-tagged jets and top-tagged
   large-R jets is consistent with the signal region. The
   requirements on Em“5 and meff are, however, relaxed in
   the control regions to achieve a sufficiently large iti yield
   and small signal contamination (<15%). The Gtt 1-lepton
   control regions are defined by inverting the mT cut and
removing the mT^ requirement. All other requirements
are exactly the same as for the signal regions.
#### C. Validation regions
Validation regions are defined to cross-check the back-
ground prediction in regions that are kinematically close
to the signal regions but yet have a small signal contami-
nation. They are designed primarily to cross-check the
assumption that the iti normalization extracted from the
control regions can be accurately extrapolated to the signal
regions. Their requirements are shown in the rightmost
column(s) of Tables II, III, and IV for the Gbb, Gtt 0-lepton,
and Gtt 1-lepton channels, respectively. Their signal con-
tamination is less than approximately 30% for the majority
of Gbb and Gtt model points not excluded in Run 1.
One validation region per signal region is defined for the
Gbb model. They feature the same requirements as their
corresponding signal region except that upper cuts are applied
on mT-mn and mf to reduce signal contamination and ensure
orthogonality with the signal regions. In addition, the require-
ment on Em188 is relaxed to obtain a sufficient it yield.
For the Gtt 0-lepton channel, two validation regions per
signal region are defined, one requiring exactly one signal
lepton (VR1L) and one with a signal lepton veto (VR0L).
The regions VR1L have exactly the same criteria as their
corresponding control regions except that they require
mT-mn > 80 GeV, similar to the signal regions, in order
to test the extrapolation over mT-e^ between the control
and the signal regions. Simulation studies show that the
heavy-flavor fraction of the additional jets in the it + jets
events (i.e., it + bb and it + cc), which suffers from large
theoretical uncertainties, is similar in the signal, control,
and VR1L regions. This is achieved by requiring the same
number of b-tagged jets for all three types of regions.
032003-9

G. AAD et al.
While the theoretical uncertainties in the heavy-flavor
fraction of the additional jets in the tt + jets events (i.e.,
tt + bb and tt + cc) are large, they affect signal, control,
and the 1-lepton validation regions in a similar way, and are
thus largely canceled in the semi-data-driven tt normali-
zation based on the observed control region yields.
The VR0L regions have similar requirements on their
corresponding signal regions except that the requirements
on £™ss, f and the number of b-tagged jets are
loosened to achieve sufficient event yields. Furthermore,
the criterion mT"^ < 80 GeV is applied to all VR0L
regions to ensure orthogonality with the signal regions.
The regions VR0L test the extrapolation of the tt normali-
zation from a 1-lepton to a 0-lepton region. Simulation
studies show that the VR0L regions have a composition
of semileptonic tt events (in particular of hadronically
decaying t leptons) similar to that in the signal regions,
while the control and VR1L regions are by construction
dominated by semileptonic tt events with a muon or an
electron.
Two requirements are different between Gtt 1-lepton
control regions and their corresponding signal regions: the
requirement on mT^f (absent in the control regions) and
the requirement on mT (inverted in the control regions).
Therefore, two validation regions per signal region are
defined for the Gtt 1-lepton channel, VR-mT and
VR-mj which respectively test, one at a time, the
extrapolations over mT and m"min. Exactly three b-tagged
jets are required for all 1-lepton validation regions to limit
the signal contamination and to be close to the signal
regions. For the VR-mT regions, the same requirement
mT > 150 GeV as in the signal region is applied but the
criterion on mT^f is inverted. Other requirements are
relaxed to achieve sufficiently large background yields and
small signal contamination. For the VR-mT-"mjeints regions, the
signal region requirement on mT-"mjeitns is applied (slightly
loosened to 140 GeV instead of 160 GeV in region A) and
the criterion on mT is inverted. Again, other requirements
are generally relaxed. Simulation studies show that tt
dilepton events dominate in the signal regions, in particular
due to the requirement on mT, while semileptonic tt events
dominate in the control regions. This extrapolation is cross-
checked by the VR-mT regions, which have a tt dileptonic
fraction similar to that in the signal regions.
#### VI. SYSTEMATIC UNCERTAINTIES
The largest sources of detector-related systematic uncer-
tainties in this analysis relate to the JES, jet energy resolution
(JER), and the b-tagging efficiencies and mistagging rates.
The JES uncertainties are obtained by extrapolating the
uncertainties derived from P? = 8 TeV data and simula-
tions to P? = 13 TeV [77]. The uncertainties in the energy
PHYSICAL REVIEW D 94, 032003 (2016)
scale of the small-R jets are propagated to the reclustered
large-R jets, which use them as inputs. The JES uncertainties
are especially important in the Gtt signal regions, since
these regions require high jet multiplicities. The impact of
these uncertainties on the expected background yields
in these regions is between 10% and 25%. Uncertainties
in the JER are similarly derived from dijet asymmetry
measurements in Run 1 data and extrapolated to
ps = 13 TeV. The impact of the JER uncertainties on
the background yields are in the range of 1 %—10%.
Uncertainties in the measured b-tagging efficiencies and
mistagging rates are the subleading sources of experimental
uncertainties in the Gtt 1-lepton signal regions and the
leading source in the Gtt 0-lepton and Gbb regions.
Uncertainties measured in P? = 8 TeV data are extrapo-
lated to PS = 13 TeV, with the addition of the new IBL
system in Run 2 taken into account. Uncertainties for jet pT
above 300 GeV are estimated using simulated events.
The impact of the b-tagging uncertainties on the expected
background yields in the Gbb and Gtt 0-lepton signal
regions is around 22%-30%, and around 15% in the Gtt
lepton signal regions.
The uncertainties associated with lepton reconstruction
and energy measurements have very small impact on the
final results. All lepton and jet measurement uncertainties
are propagated to the calculation of ETmiss, and additional
uncertainties are included in the scale and resolution of
the soft term. The overall impact of the ETmiss soft term
uncertainties on the expected background yields is 5%
or less.
Uncertainties in the modeling of the tf background are
evaluated using additional samples varied by each system-
atic uncertainty. Hadronization and parton showering
uncertainties are estimated using a sample generated with
powheg and showered by herwig++v2.7.1 [49] with the
UEEE5 underlying-event tune [60]. Systematic uncertain-
ties in the modeling of initial- and final-state radiation are
explored with two alternative settings of powheg, both of
which are showered by pythia v6.428 as for the nominal
sample. The first of these uses the PERUGIA2012 radHi
tune and has the renormalization and factorization scales
set to twice the nominal value, resulting in more radiation
in the final state. It also has hdamp set to 2mtop. The second
sample, using the PERUGIA2012 radLo tune, has
hdamp = mtop, and the renormalization and factorization
scales are set to half of their nominal values, resulting in
less radiation in the event. In each case, the uncertainty is
taken as the deviation in the expected yield of tft back-
ground with respect to the nominal sample. The uncertainty
due to the choice of generator is estimated by comparing
the expected yields obtained using a tf sample generated
with MADGRAPH5_aMC@NLO, and one that is generated
with powheg. Both of these samples are showered with
herwig++ v2.7.1. Finally, a 30% uncertainty is assigned to
the cross section of tft events with additional heavy-flavor
032003-10

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...
jets in the final state, in accordance with the results of the
ATLAS measurement of this cross section at y/s = 8 TeV
. Uncertainties in single-top and W/Z + jets back-
ground processes are similarly estimated by comparisons
between the nominal sample and samples with different
generators, showering models, and radiation tunes. An
additional 5% uncertainty is included in the cross section of
single-top processes [94]. A 50% constant uncertainty is
assigned to each of the remaining small backgrounds. The
variations in the expected background yields due to tt
modeling uncertainties range between 10% and 30% for the
Gbb signal regions, and between 47% and 57% in most Gtt
signal regions. The impact of the modeling uncertainties for
the smaller backgrounds on these yields is consistently
below 10% in all signal regions. The uncertainties in the
cross sections of signal processes are determined from an
envelope of different cross-section predictions, as described
in Sec. III.
The cumulative impact of the systematic uncertainties
listed above on the background yields ranges between 23%
and 63%, depending on the signal region. The typical
impact on the signal yields is in the range 10%-30%.
#### VII. RESULTS
The SM background expectation is determined sepa-
rately in each signal region with a profile likelihood fit [95],
referred to as a background-only fit. The fit uses as a
constraint the observed event yield in the associated control
region to adjust the tt normalization, assuming that a
signal does not contribute to this yield, and applies that
normalization factor to the number tt events predicted by
PHYSICAL REVIEW D 94, 032003 (2016)
simulation in the signal region. The numbers of observed
and predicted events in each control region are described
by Poisson probability density functions. The systematic
uncertainties in the expected values are included in the fit as
nuisance parameters. They are constrained by Gaussian
distributions with widths corresponding to the sizes of the
uncertainties and are treated as correlated, when appro-
priate, between the various regions. The product of the
various probability density functions forms the likelihood,
which the fit maximizes by adjusting the tt normalization
and the nuisance parameters within their constraints. The
inputs to the fit for each signal region are the number of
events observed in its associated control region and the
number of events predicted by simulation in each region for
all background processes.
Figure 4 shows the results of the background-only fit to
the control regions, extrapolated to the validation regions.
The number of events predicted by the background-only fit
is compared to the data in the upper panel. The pull, defined
by the difference between the observed number of events
(nobs) and the predicted background yield (npred) divided by
the total uncertainty (tftot), is shown for each region in the
lower panel. No evidence of significant background mis-
modeling is observed in the validation regions. There is a
certain tendency for the predicted background to be above
the data, in particular for the Gtt-0L validation regions, but
the results in the validation regions of a given channel are
not independent. The validation and control regions of
different mass splittings can overlap, with the overlap
fraction ranging from approximately 30% to 70% for
Gtt-0L. Furthermore, the uncertainties in the predicted
FIG. 4. Results of the likelihood fit extrapolated to the validation regions. The tt normalization is obtained from the fit to the control
regions. The upper panel shows the observed number of events and the predicted background yield. The background category “Others”
includes tih, titi, and diboson events. The lower panel shows the pulls in each validation region.
032003-11

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
TABLE V. Results of the likelihood fit extrapolated to the Gbb signal regions. The uncertainties shown include all
systematic uncertainties. The data in the signal regions are not included in the fit. The row “MC-only background
prediction” provides the total background prediction when the tt normalization is obtained from a theoretical
calculation [61]. The tt normalization factor pt-t obtained from the corresponding tt control region is also provided.
The background category “Others” includes tth, tttt, and diboson events. Expected yields for two example Gbb
models are also shown.
	SR-Gbb-A	SR-Gbb-B	SR-Gbb-C
Observed events	0	0	5
Fitted background events	1.3 ± 0.4	1.5 ± 0.6	7.6 ± 1.7
tt	0.63 ± 0.30	0.9 ± 0.5	4.3 ± 1.5
Z + jets	0.23 ± 0.08	0.23 ± 0.09	1.2 ± 0.5
W + jets	0.17 ± 0.06	0.13 ± 0.05	0.82 ± 0.28
Single-top	0.25 ± 0.14	0.15 ± 0.14	0.65 ± 0.33
ttW/Z	< 0.1	< 0.1	0.22 ± 0.12
Others	< 0.1	< 0.1	0.39 ± 0.22
MC-only background prediction	1.7	1.5	6.7
Pit	0.64 ± 0.33	1.0 ± 0.4	1.2 ± 0.4
Gbb (mg = 1700 GeV, 0 = 200 GeV)	3.8	3.5	4.2
Gbb (m-g = 1400 GeV, m^ = 800 GeV)	5.3	7.2	10.5

yield are dominated by the same (correlated) systematic
uncertainties.
Tables V, VI, and VII show the observed number of
events and predicted number of background events from
the background-only fit in the Gbb, Gtt 0-lepton, and Gtt
lepton signal regions, respectively. In addition, the tables
show the numbers of signal events expected for some
example values of gluino and LSP masses in the Gtt and
Gbb models. The event yields in the signal regions are also
shown in Fig. 5, where the pull is shown for each region in
the lower panel. No excess is found above the predicted
background. The background is dominated by tt events in
all Gbb and Gtt signal regions. The subdominant contri-
butions in the Gbb and Gtt 0-lepton signal regions are
Z(^ vv) +jets and W(^ 1v) +jets events, where for
W + jets events the lepton is a nonidentified electron or
muon or is a hadronically decaying t lepton. In the Gtt
lepton signal regions, the subdominant backgrounds are
single-top, ttW and ttZ.
Figure 6 shows the Emiss distributions in data and
simulated samples for SR-Gbb-B, SR-Gtt-0L-C, and SR-
Gtt-IL-A, after relaxing the E™ss threshold to 200 GeV.
TABLE VI. Results of the likelihood fit extrapolated to the Gtt 0-lepton signal regions. The uncertainties shown
include all systematic uncertainties. The data in the signal regions are not included in the fit. The row “MC-only
background prediction” provides the total background prediction when the tt normalization is obtained from a
theoretical calculation [61]. The tt normalization factor pt-t obtained from the corresponding tt control region is also
provided. The category “Others” includes tth, tttt, and diboson events. Expected yields for two example Gtt models
are also shown.
	SR-Gtt-0L-A	SR-Gtt-0L-B	SR-Gtt-0L-C
Observed events	1	1	1
Fitted background events	2.1 ± 0.5	2.9 ± 1.8	3.4 ± 1.8
tt	1.4 ± 0.4	2.4 ± 1.7	2.6 ± 1.8
Z + jets	0.22 ± 0.09	0.11 ± 0.06	0.14 ± 0.07
W + jets	0.19 ± 0.08	0.14 ± 0.06	0.18 ± 0.08
Single-top	0.17 ± 0.17	0.14 ± 0.13	0.17 ± 0.15
ttW/Z	< 0.1	<0.1	0.10 ± 0.07
Others	< 0.1	<0.1	0.20 ± 0.17
MC-only background prediction	1.8	1.9	2.5
Ptt	1.3 ± 0.4	1.8 ± 0.8	1.5 ± 0.7
Gtt (mg = 1600 GeV, mx0 = 200 GeV)	3.8	2.8	2.9
Gtt (m-g = 1400 GeV, mx0 = 800 GeV)	2.0	3.7	4.1

032003-12

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...	PHYSICAL	REVIEW	D	94,	032003	(2016)
TABLE VII. Results of the likelihood fit extrapolated to the Gtt 1-lepton signal regions. The uncertainties shown
include all systematic uncertainties. The data in the signal regions are not included in the fit. The row “MC-only
background prediction” provides the total background prediction when the tt normalization is obtained from a
theoretical calculation [61]. The tt normalization factor ^t-t obtained from the corresponding tt control region is also
provided. The category “Others” includes tth, ----, and diboson events. Expected yields for two example Gtt models
are also shown.
	SR-Gtt-IL-A	SR-Gtt-IL-B
Observed events	2	0
Fitted background events	1.2 ± 0.6	1.2 ± 0.8
tt	0.8 ± 0.6	0.8 ± 0.7
Z + jets		< 0.1
W + jets	< 0.1	<0.1
Single-top	0.18 ± 0.14	0.14 ± 0.12
ttW/Z	0.14 ± 0.08	0.15 ± 0.09
Others	< 0.1	< 0.1
MC-only background prediction	1.3	1.2
^tt	0.86 ± 0.28	1.0 ± 0.4
Gtt (mg = 1600 GeV, mx0 = 200 GeV)	3.4	3.3
Gtt (mg = 1400 GeV, mj0 = 800 GeV)	3.8	4.6

### VIII. INTERPRETATION
Since no significant excess over the expected back-
ground from SM processes is observed, the data are used
to derive one-sided upper limits at 95% C.L. Model-
independent limits on the number of beyond-the-SM
(BSM) events for each signal region are derived with
pseudoexperiments using the CLS prescription [96]. They
can be translated into upper limits on the visible BSM cross
section (tfvis), where ffvis is defined as the product of
acceptance, reconstruction efficiency, and production cross
section. The results are given in Table VIII, where the
observed (S^) and expected (S^p) 95% C.L. upper limits
on the number of BSM events are also provided.
The measurement is used to place exclusion limits on
gluino and LSP masses in the Gbb and Gtt simplified
models. The results are obtained using the CLs prescription
in the asymptotic approximation [97]. The signal contami-
nation in the control regions and the experimental
FIG. 5. Results of the likelihood fit extrapolated to the signal regions. The data in the signal regions are not included in the fit. The
upper panel shows the observed number of events and the predicted background yield. The signal regions SR-Gbb-A, SR-Gbb-B, and
SR-Gtt-1L-B have no observed events. The background category “Others” includes tth, ----, and diboson events. The lower panel shows
the pulls in each signal region.
032003-13

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
200	300	400	500	600	700	800
Efss [GeV]
(c)
FIG. 6. Distributions of for (a) SR-Gbb-B, (b) SR-Gtt-OL-C, and (c) SR-Gtt-IL-A. The threshold is set to 200 GeV for these
plots, with the red lines indicating the threshold values in the actual signal regions for SR-Gbb-B and SR-Gtt-OL-C (the E!piss threshold
in SR-Gtt-IL-A is 200 GeV). The statistical and experimental systematic uncertainties are included in the uncertainty band. Two
example signal models are overlaid.
systematic uncertainties in the signal are taken into account
for this calculation. For the Gbb models, the results are
obtained from the Gbb signal region with the best expected
sensitivity at each point of the parameter space of each
TABLE VIII. The 95% C.L. upper limits on the visible cross
section (o>is), defined as the product of acceptance,
reconstruction efficiency, and production cross section, and the
observed and expected 95% C.L. upper limits on the number of
BSM events (S^ and 5fXp).
Signal channel	ffvis [fb]	S95 / Sobs	S95 / '-’exp
SR-Gbb-A	0.94	3.0	3 9+13 3-9 07
SR-Gbb-B	0.94	3.0	o 0+1.4 3.o o 8
SR-Gbb-C	1.74	5.6	7 2+2.6 / .Z i g
SR-Gtt-IL-A	1.49	4.8	3.9+1.4 39 - 0.5
SR-Gtt-IL-B	0.91	3.0	3 . 0 + 1 . 4 3 0 0.0
SR-Gtt-0L-A	1.13	3.6	4 4+1.7 44-1.0
SR-Gtt-0L-B	1.16	3.7	4 4+1.9 / 4.4 0.9
SR-Gtt-0L-C	1.10	3.5	4.5+2.0 4.5 1.2

model. For the Gtt models, the 0- and 1-lepton channels
both contribute to the sensitivity, and they are combined in
a simultaneous fit to enhance the sensitivity of the analysis.
This is performed by considering all possible permutations
between the three Gtt 0-lepton and the two Gtt 1-lepton
signal regions for each point of the parameter space, and the
best expected combination is used. The 95% C.L. observed
and expected exclusion limits for the Gbb and Gtt models
are shown in the LSP and gluino mass plane in Figs. 7(a)
and 7(b), respectively. The ± l^SUY lines around the
observed limits are obtained by changing the SUSY cross
section by 1 standard deviation (±1+, as described in
Sec. III. The yellow band around the expected limit shows
the ±1^ uncertainty, including all statistical and systematic
uncertainties except the theoretical uncertainties in the
SUSY cross section. It has been checked that the observed
exclusion limits obtained from pseudoexperiments differ by
less than 25 GeV from the asymptotic approximation in
gluino or LSP mass in the combined limits in Fig. 7,
although the difference can be up to 50 GeV when using
032003-14

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...	PHYSICAL	REVIEW	D	94,	032003	(2016)
m(g) [GeV]	m(g)	[GeV]
(a)	(b)
FIG. 7. Exclusion limits in the and g mass plane for the (a) Gbb and (b) Gtt models. The dashed and solid bold lines show the
95% C.L. expected and observed limits, respectively. The shaded bands around the expected limits show the impact of the experimental
and background theoretical uncertainties. The dotted lines show the impact on the observed limit of the variation of the nominal signal
cross section by ±1<7 of its theoretical uncertainty. The 95% C.L. observed limits from the P? = 8 TeV ATLAS search requiring at least
three b-tagged jets [17] are also shown.
single analysis regions. The two methods of computation
produce equivalent expected limits.
For the Gbb models, gluinos with masses below
1.78 TeV are excluded at 95% C.L. for LSP masses
below 800 GeV. At high gluino masses, the exclusion
limits are driven by the SR-Gbb-A and SR-Gbb-B
signal regions. The best exclusion limit on the LSP
mass is approximately 1.0 TeV, which is reached for a
gluino mass of approximately 1.6 TeV. The exclusion
limit is dominated by SR-Gbb-C for high LSP masses.
For the Gtt models, gluino masses up to 1.8 TeV are
excluded for massless LSP. For LSP masses below
700 GeV, gluino masses below 1.76 TeV are excluded.
For large gluino masses, the exclusion limits are driven
by the combination of SR-Gtt-IL-B and SR-Gtt-OL-A.
The LSP exclusion extends up to approximately
975 GeV, corresponding to a gluino mass of approx-
imately 1.5 TeV-1.6 TeV. The best exclusion limits are
obtained by the combination of SR-Gtt-1L-B and SR-
Gtt-0L-C for high LSP masses. The ATLAS exclusion
limits obtained with the full s = 8 TeV data set are
also shown in Fig. 7. The current results largely
improve on the s = 8 TeV limits despite the lower
integrated luminosity. The exclusion limit on the gluino
mass is extended by approximately 500 GeV and
400 GeV for the Gbb and Gtt models for massless
LSP, respectively. This improvement is primarily attrib-
utable to the increased center-of-mass energy of the
LHC. The addition of the IBL pixel layer in Run 2,
which improves the capability to tag b jets [35], also
particularly benefits this analysis that employs a data
set requiring at least three b-tagged jets. The sensitivity
of the data analysis is also improved with respect to the
P? = 8 TeV analysis [17] by using top-tagged large-R
jets, lepton isolation adapted to a busy environment,
and the mT-jen variable.
#### IX. CONCLUSION
A search for pair-produced gluinos decaying via sbottom
or stop is presented. LHC proton-proton collision data from
the full 2015 data-taking period were analyzed, correspond-
ing to an integrated luminosity of 3.2 fb-1 collected at
P? = 13 TeV by the ATLAS detector. Several signal
regions are designed for different scenarios of gluino
and LSP masses. They require several high-pT jets, of
which at least three must be b tagged, large Em“5, and either
zero or at least one charged lepton. For the gluino models
with stop-mediated decays in which there is a large mass
difference between the gluino and the LSP, large-R jets
identified as originating from highly boosted top quarks are
employed. The background is dominated by tt + jets,
which is normalized in dedicated control regions. No
excess is found above the predicted background of each
signal region. Model-independent limits are set on the
visible cross section for new physics processes. Exclusion
limits are set on gluino and LSP masses in the simplified
gluino models with stop-mediated and sbottom-mediated
decays. For LSP masses below approximately 700 GeV,
gluino masses of less than 1.78 TeV and 1.76 TeV are
excluded at the 95% C.L. for the gluino models with
sbottom-mediated and stop-mediated decays, respectively.
These results significantly extend the exclusion limits
obtained with the P? = 8 TeV data set.
#### ACKNOWLEDGMENTS
We thank CERN for the very successful operation of the
LHC, as well as the support staff from our institutions
032003-15

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
without whom ATLAS could not be operated efficiently.
We acknowledge the support of ANPCyT, Argentina;
YerPhI, Armenia; ARC, Australia; BMWFW and FWF,
Austria; ANAS, Azerbaijan; SSTC, Belarus; CNPq and
FAPESP, Brazil; NSERC, NRC, and CFI, Canada; CERN;
CONICYT, Chile; CAS, MOST, and NSFC, China;
COLCIENCIAS, Colombia; MSMT CR, MPO CR, and
VSC CR, Czech Republic; DNRF and DNSRC, Denmark;
IN2P3-CNRS, CEA-DSM/IRFU, France; GNSF, Georgia;
BMBF, HGF, and MPG, Germany; GSRT, Greece; RGC,
Hong Kong SAR, China; ISF, I-CORE, and Benoziyo
Center, Israel; INFN, Italy; MEXT and JSPS, Japan;
CNRST, Morocco; FOM and NWO, Netherlands; RCN,
Norway; MNiSWand NCN, Poland; FCT, Portugal; MNE/
IFA, Romania; MES of Russia and NRC KI, Russian
Federation; JINR; MESTD, Serbia; MSSR, Slovakia;
ARRS and MIZS, Slovenia; DST/NRF, South Africa;
MINECO, Spain; SRC and Wallenberg Foundation,
Sweden; SERI, SNSF, and Cantons of Bern and Geneva,
Switzerland; MOST, Taiwan; TAEK, Turkey; STFC,
United Kingdom; DOE and NSF, United States of
America. In addition, individual groups and members have
received support from BCKDF, the Canada Council,
CANARIE, CRC, Compute Canada, FQRNT, and the
Ontario Innovation Trust, Canada; EPLANET, ERC,
FP7, Horizon 2020, and Marie Sklodowska-Curie
Actions, European Union; Investissements d’Avenir
Labex and Idex, ANR, Région Auvergne and Fondation
Partager le Savoir, France; DFG and AvH Foundation,
Germany; Herakleitos, Thales, and Aristeia programmes
cofinanced by EU-ESF and the Greek NSRF; BSF, GIF,
and Minerva, Israel; BRF, Norway; Generalitat de
Catalunya, Generalitat Valenciana, Spain; the Royal
Society and Leverhulme Trust, United Kingdom. The
crucial computing support from all WLCG partners is
acknowledged gratefully, in particular from CERN and the
ATLAS Tier-1 facilities at TRIUMF (Canada), NDGF
(Denmark, Norway, Sweden), CC-IN2P3 (France), KIT/
GridKA (Germany), INFN-CNAF (Italy), NL-T1
(Netherlands), PIC (Spain), ASGC (Taiwan), RAL (UK),
and BNL (USA) and in the Tier-2 facilities worldwide.
1. Yu. A. Golfand and E. P. Likhtman, Extension of the algebra
   of Poincare group generators and violation of p invariance,
   Pis’ma Zh. Eksp. Teor. Fiz. 13, 452 (1971) [JETP Lett. 13,
   323 (1971)].
2. D. V. Volkov and V. P. Akulov, Is the neutrino a Goldstone
   particle?, Phys. Lett. 46B, 109 (1973).
3. J. Wess and B. Zumino, Supergauge transformations in four-
   dimensions, Nucl. Phys. B70, 39 (1974).
4. J. Wess and B. Zumino, Supergauge invariant extension of
   quantum electrodynamics, Nucl. Phys. B78, 1 (1974).
5. S. Ferrara and B. Zumino, Supergauge invariant Yang-Mills
   theories, Nucl. Phys. B79, 413 (1974).
6. A. Salam and J. A. Strathdee, Supersymmetry and non-
   abelian gauges, Phys. Lett. 51B, 353 (1974).
7. G. R. Farrar and P. Fayet, Phenomenology of the produc-
   tion, decay, and detection of new hadronic states associated
   with supersymmetry, Phys. Lett. 76B, 575 (1978).
8. N. Sakai, Naturalness in supersymmetric GUTs, Z. Phys. C
   11, 153 (1981).
9. S. Dimopoulos, S. Raby, and F. Wilczek, Supersymmetry
   and the scale of unification, Phys. Rev. D 24, 1681 (1981).
10. L. E. Ibanez and G. G. Ross, Low-energy predictions in
    supersymmetric grand unified theories, Phys. Lett. 105B,
    439 (1981).
11. S. Dimopoulos and H. Georgi, Softly broken supersym-
    metry and SU(5), Nucl. Phys. B193, 150 (1981).
12. R. Barbieri and G. F. Giudice, Upper bounds on super-
    symmetric particle masses, Nucl. Phys. B306, 63 (1988).
13. B. de Carlos and J. A. Casas, One loop analysis of the
    electroweak breaking in supersymmetric models and the
    fine tuning problem, Phys. Lett. B 309, 320 (1993).
1. ATLAS Collaboration, The ATLAS experiment at the
   CERN Large Hadron Collider, J. Instrum. 3, S08003 (2008).
2. J. Alwall, P. Schuster, and N. Toro, Simplified models for a
   first characterization of new physics at the LHC, Phys. Rev.
   D 79, 075020 (2009).
3. D. Alves et al., Simplified models for LHC new physics
   searches, J. Phys. G 39, 105005 (2012).
4. ATLAS Collaboration, Search for strong production of
   supersymmetric particles in final states with missing trans-
   verse momentum and at least three b-jets at y/s = 8 TeV
   proton-proton collisions with the ATLAS detector, J. High
   Energy Phys. 10 (2014) 24.
5. D. Krohn, J. Thaler, and L.-T. Wang, Jet trimming, J. High
   Energy Phys. 02 (2010) 084.
6. B. Nachman, P. Nef, A. Schwartzman, M. Swiatlowski, and
Wanotayaroj, Jets from jets: Re-clustering as a tool for
large radius jet reconstruction and grooming at the LHC,
J. High Energy Phys. 02 (2015) 075.
ATLAS Collaboration, Summary of the searches for squarks
and gluinos using s = 8 TeV pp collisions with the
ATLAS experiment at the LHC, J. High Energy Phys. 10
054.
1. ATLAS Collaboration, Search for new phenomena in final
   states with large jet multiplicities and missing transverse
   momentum at s = 8 TeV proton-proton collisions using
   the ATLAS experiment, J. High Energy Phys. 10 (2013)
   130.
2. ATLAS Collaboration, Search for squarks and gluinos in
   events with isolated leptons, jets and missing transverse
   momentum at s = 8 TeV with the ATLAS detector,
   J. High Energy Phys. 04 (2015) 116.
032003-16

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...
1. ATLAS Collaboration, Search for supersymmetry at s =
   8 TeV in final states with jets and two same-sign leptons or
   three leptons with the ATLAS detector, J. High Energy
   Phys. 06 (2014) 035.
2. ATLAS Collaboration, Search for supersymmetry at s =
   13 TeV in final states with jets and two same-sign leptons or
   three leptons with the ATLAS detector, Eur. Phys. J. C 76,
   259 (2016).
3. CMS Collaboration, Search for gluino mediated bottom-
   and top-squark production in multijet final states in pp
   collisions at 8 TeV, Phys. Lett. B 725, 243 (2013).
4. CMS Collaboration, Search for supersymmetry in pp
   collisions at s = 8 TeV in events with a single lepton,
   large jet multiplicity, and multiple b jets, Phys. Lett. B 733,
   328 (2014).
5. CMS Collaboration, Search for supersymmetry using razor
   variables in events with b-tagged jets in pp collisions at
   pS = 8 TeV, Phys. Rev. D 91, 052018 (2015).
6. CMS Collaboration, Search for new physics in the multijet
   and missing transverse momentum final state in proton-
   proton collisions at PS = 8 TeV, J. High Energy Phys. 06
055.
1. CMS Collaboration, Search for new physics in events
   with same-sign dileptons and jets in pp collisions at
   PS = 8 TeV, J. High Energy Phys. 01 (2014) 163.
2. CMS Collaboration, Searches for supersymmetry based on
   events with b jets and four w bosons in pp collisions at
   8 TeV, Phys. Lett. B 745, 5 (2015).
3. CMS Collaboration, Search for supersymmetry
   in the multijet and missing transverse momentum final
   state in pp collisions at 13 TeV, Phys. Lett. B 758, 152
(2016).
1. CMS Collaboration, Search for new physics with the MT2
   variable in all-jets final states produced in pp collisions at
   PS = 13 TeV (to be published).
2. CMS Collaboration, Search for supersymmetry in pp
   collisions at S = 13 TeV in the single-lepton final state
   using the sum of masses of large-radius jets (to be
   published).
3. CMS Collaboration, Search for new physics in same-sign
   dilepton events in proton-proton collisions at S = 13 TeV
   (to be published).
4. ATLAS Collaboration, ATLAS Insertable B-Layer
   Technical Design Report No. CERN-LHCC-2010-013,
   ATLAS-TDR-19, 2010, https://cds.cern.ch/record/1291633.
5. ATLAS Collaboration, Performance of the ATLAS trigger
   system in 2010, Eur. Phys. J. C 72, 1849 (2012).
6. ATLAS Collaboration, Improved luminosity determination
   in pp collisions at pS = 7 TeV using the ATLAS detector
   at the LHC, Eur. Phys. J. C 73, 2518 (2013).
7. J. Alwall, R. Frederix, S. Frixione, V. Hirschi, F. Maltoni,
   O. Mattelaer, H.-S. Shao, T. Stelzer, P. Torrielli, and M.
   Zaro, The automated computation of tree-level and next-to-
   leading order differential cross sections, and their matching
   to parton shower simulations, J. High Energy Phys. 07
079.
P. M. Nadolsky, H.-L. Lai, Q.-H. Cao, J. Huston, J. Pumplin,
D. Stump, W.-K. Tung, and C.-P. Yuan, Implications of
CTEQ global analysis for collider observation, Phys. Rev. D
78, 013004 (2008).
PHYSICAL REVIEW D 94, 032003 (2016)
1. T. Sjostrand, S. Mrenna, and P. Z. Skands, A brief introduc-
   tion to PYTHIA 8.1, Comput. Phys. Commun. 178, 852
   (2008).
2. S. Alioli, P. Nason, C. Oleari, and E. Re, A general
   framework for implementing NLO calculations in shower
   Monte Carlo programs: The POWHEG BOX, J. High
   Energy Phys. 06 (2010) 043.
3. S. Frixione, P. Nason, and C. Oleari, Matching NLO QCD
   computations with parton shower simulations:	The
   POWHEG method, J. High Energy Phys. 11 (2007) 070.
4. H.-L. Lai, M. Guzzi, J. Huston, Z. Li, P. M. Nadolsky, J.
   Pumplin, and C.-P. Yuan, New parton distributions for
   collider physics, Phys. Rev. D 82, 074024 (2010).
5. T. Sjostrand, S. Mrenna, and P. Z. Skands, PYTHIA 6.4
   physics and manual, J. High Energy Phys. 05 (2006) 026.
6. D. J. Lange, The EvtGen particle decay simulation package,
   Nucl. Instrum. Methods Phys. Res., Sect. A 462, 152
   (2001).
7. ATLAS Collaboration, Comparison of Monte Carlo gen-
   erator predictions to ATLAS measurements of top pair
   production at PS = 7 TeV, Report No. ATLAS-PHYS-
   PUB-2015-002,	2015,	http://cdsweb.cern.ch/record/
1981319.
1. ATLAS Collaboration, Measurement of the differential
   cross-section of highly boosted top quarks as a function
   of their transverse momentum in S = 8 TeV proton-
   proton collisions using the ATLAS detector, Phys. Rev.
   D 93, 032009 (2016).
2. J. Alwall, M. Herquet, F. Maltoni, O. Mattelaer, and T.
   Stelzer, MadGraph 5: Going beyond, J. High Energy Phys.
   06 (2011) 128.
3. M. Bahr et al., Herwig++ physics and manual, Eur. Phys. J.
   C 58, 639 (2008).
4. T. Gleisberg, S. Hoche, F. Krauss, M. Schonherr, S.
   Schumann, F. Siegert, and J. winter, Event generation with
   SHERPA 1.1, J. High Energy Phys. 02 (2009) 007.
5. T. Gleisberg and S. Hoche, Comix, a new matrix element
   generator, J. High Energy Phys. 12 (2008) 039.
6. F. Cascioli, P. Maierhofer, and S. Pozzorini, Scattering
   amplitudes with open loops, Phys. Rev. Lett. 108, 111601
   (2012).
7. S. Schumann and F. Krauss, A Parton shower algorithm
   based on Catani-Seymour dipole factorisation, J. High
   Energy Phys. 03 (2008) 038.
8. S. Hoche, F. Krauss, M. Schonherr, and F. Siegert, QCD
   matrix elements + parton showers: The NLO case, J. High
   Energy Phys. 04 (2013) 027.
9. S. Agostinelli et al., Geant4: A simulation toolkit, Nucl.
   Instrum. Methods Phys. Res., Sect. A 506, 250 (2003).
10. ATLAS Collaboration, The ATLAS simulation infrastruc-
    ture, Eur. Phys. J. C 70, 823 (2010).
11. ATLAS Collaboration, The simulation principle and
    performance of the ATLAS fast calorimeter simulation
    fastcalosim, Report No. ATL-PHYS-PUB-2010-013,
    2010, https://cds .cern.ch/record/1300517.
12. P. Z. Skands, Tuning Monte Carlo generators: The Perugia
    tunes, Phys. Rev. D 82, 074018 (2010).
13. ATLAS Collaboration, ATLAS Run-1 Pythia8 tunes, Report
    No. ATLAS-PHYS-PUB-2014-021, 2014, http://cdsweb
    .cern.ch/record/1966419.
032003-17

G. AAD et al.
1. S. Gieseke, C. Rohr, and A. Siodmok, Colour reconnections
   in Herwig++, Eur. Phys. J. C 72, 2225 (2012).
2. M. Czakon and A. Mitov, Top++: A program for the
   calculation of the top-pair cross-section at hadron colliders,
   Comput. Phys. Commun. 185, 2930 (2014).
3. N. Kidonakis, Next-to-next-to-leading-order collinear and
   soft gluon corrections for i-channel single top quark
   production, Phys. Rev. D 83, 091503 (2011).
4. N. Kidonakis, Two-loop soft anomalous dimensions for
   single top quark associated production with a W- or H-,
   Phys. Rev. D 82, 054018 (2010).
5. N. Kidonakis, NNLL resummation for s-channel single top
   quark production, Phys. Rev. D 81, 054028 (2010).
6. R. D. Ball et al., Parton distributions with LHC data, Nucl.
   Phys. B867, 244 (2013).
7. S. Heinemeyer et al., Handbook of LHC Higgs cross
   sections: 3. Higgs properties: Report of the LHC Higgs
   Cross Section Working Group, 2013, https://cds.cern.ch/
   record/1559921.
8. S. Catani, L. Cieri, G. Ferrera, D. de Florian, and M.
   Grazzini, Vector boson production at hadron colliders: A
   fully exclusive QCD calculation at NNLO, Phys. Rev. Lett.
   103, 082001 (2009).
9. W. Beenakker, R. Höpker, M. Spira, and P. M. Zerwas,
   Squark and gluino production at hadron colliders, Nucl.
   Phys. B492, 51 (1997).
10. A. Kulesza and L. Motyka, Threshold resummation for
    squark-antisquark and gluino-pair production at the LHC,
    Phys. Rev. Lett. 102, 111802 (2009).
11. A. Kulesza and L. Motyka, Soft gluon resummation for the
    production of gluino-gluino and squark-antisquark pairs at
    the LHC, Phys. Rev. D 80, 095004 (2009).
12. W.Beenakker,S.Brensing,M.Krämer, A.Kulesza,E.Laenen,
    and I. Niessen, Soft-gluon resummation for squark and gluino
    hadroproduction, J. High Energy Phys. 12 (2009) 041.
13. W. Beenakker, S. Brensing, M. Krämer, A. Kulesza, E.
    Laenen, L. Motyka, and I. Niessen, Squark and gluino
    hadroproduction, Int. J. Mod. Phys. A 26, 2637 (2011).
14. M. Kramer et al., Supersymmetry production cross sections
    in pp collisions at PS = 7 TeV, Report No. CERN-PH-
    TH-2012-163, 2012, https://cds.cern.ch/record/1456029.
15. ATLAS Collaboration, Vertex reconstruction performance
    of the ATLAS detector at ps = 13 TeV, Report No. ATL-
    PHYS-PUB-2015-026, 2015, http://cdsweb.cern.ch/record/
    2037717.
16. W. Lampl etal., Calorimeter clustering algorithms: Description
    and performance, 2008, https://cds.cern.ch/record/1099735.
17. M. Cacciari, G. Salam, and G. Soyez, The anti-kt jet
    clustering algorithm, J. High Energy Phys. 04 (2008) 063.
18. ATLAS Collaboration, Jet calibration and systematic un-
    certainties for jets reconstructed in the ATLAS detector at
    PS = 13 TeV, Report No. ATLAS-PHYS-PUB-2015-015
, http://cdsweb.cern.ch/record/2037613.
1. ATLAS Collaboration, Monte Carlo calibration and
   combination of in-situ measurements of jet energy scale,
   jet energy resolution and jet mass in ATLAS, Report
   No. ATLAS-CONF-2015-037, 2015, http://cdsweb.cern
   .ch/record/2044941.
2. ATLAS Collaboration, Selection of jets produced in 13 TeV
   proton-proton collisions with the ATLAS detector, Report
PHYSICAL REVIEW D 94, 032003 (2016)
No. ATLAS-CONF-2015-029, 2015, http://cdsweb.cern.ch/
record/2037702.
1. ATLAS Collaboration, Performance of pile-up mitigation
   techniques for jets in pp collisions at Ps = 8 TeV using the
   ATLAS detector, Report No. CERN-PH-EP-2015-206,
   2015, https://cds.cern.ch/record/2058295.
2. ATLAS Collaboration, Commissioning of the ATLAS b-
   tagging algorithms using ttt events in early Run-2 data,
   Report No. ATLAS-PHYS-PUB-2015-039, 2015, http://
   cdsweb.cern.ch/record/2047871.
3. ATLAS Collaboration, Calibration of b-tagging using
   dileptonic top pair events in a combinatorial likelihood
   approach with the ATLAS experiment, Report No. ATLAS-
   CONF-2014-004,	2014,	http://cdsweb.cern.ch/record/
1664335.
1. ATLAS Collaboration, Calibration of the performance of
   b-tagging for c and light-flavour jets in the 2012 ATLAS
   data, Report No. ATLAS-CONF-2012-046, 2014, http://
   cdsweb.cern.ch/record/1741020.
2. ATLAS Collaboration, Electron reconstruction and iden-
   tification efficiency measurements with the ATLAS
   detector using the 2011 LHC proton-proton collision
   data, Eur. Phys. J. C 74, 2941 (2014).
3. ATLAS Collaboration, Electron and photon energy calibra-
   tion with the ATLAS detector using LHC Run 1 data, Eur.
   Phys. J. C 74, 3071 (2014).
4. ATLAS Collaboration, Electron identification measure-
   ments in ATLAS using pS = 13 TeV data with 50 ns
   bunch spacing, Report No. ATLAS-PHYS-PUB-2015-041,
   2015, http://cdsweb.cern.ch/record/2048202.
5. ATLAS Collaboration, Muon reconstruction performance of
   the ATLAS detector in proton-proton collision data at
   p = 13 TeV, Eur. Phys. J. C 76, 292 (2016).
6. ATLAS Collaboration, Measurement of the muon
   reconstruction performance of the ATLAS detector using
   2011 and 2012 LHC proton-proton collision data, Eur. Phys.
   J. C 74, 3130 (2014).
7. ATLAS Collaboration, A search for ttt resonances using
   lepton-plus-jets events in proton-proton collisions at s =
   8 TeV with the ATLAS detector, J. High Energy Phys. 08
148.
1. ATLAS Collaboration, Performance of missing transverse
   momentum reconstruction for the ATLAS detector in the
   first proton-proton collisions at s = 13 TeV, Report
   No. ATLAS-CONF-2013-082, 2013, https://cds.cern.ch/
   record/1570993.
2. ATLAS Collaboration, Performance of missing transverse
   momentum reconstruction in proton-proton collisions at
   7 TeV with ATLAS, Eur. Phys. J. C 72, 1844 (2012).
3. ATLAS Collaboration, Preliminary results on the muon
   reconstruction efficiency, momentum resolution, and mo-
   mentum scale in ATLAS 2012 pp collision data, Report
   No. ATLAS-CONF-2013-088, 2013, http://cdsweb.cern.ch/
   record/1580207.
4. ATLAS Collaboration, Measurements of fiducial cross-
   sections for ttt production with one or two additional b-jets
   in pp collisions at s = 8 TeV using the ATLAS detector,
   Eur. Phys. J. C 76, 11 (2016).
5. P. Kant, O. M. Kind, T. Kintscher, T. Lohse, T. Martini, S.
   Molbitz, P. Rieck, and P. Uwer, HatHor for single top-quark
032003-18

SEARCH FOR PAIR PRODUCTION OF GLUINOS
PHYSICAL REVIEW D 94, 032003 (2016)
production: Updated predictions and uncertainty estimates
for single top-quark production in hadronic collisions,
Comput. Phys. Commun. 191, 74 (2015).
M. Baak, G. J. Besjes, D. Côté, A. Koutsman, J. Lorenz, and
Short, HistFitter software framework for statistical data
analysis, Eur. Phys. J. C 75, 153 (2015).
1. A. L. Read, Presentation of search results: The CL(s)
   technique, J. Phys. G 28, 2693 (2002).
2. G. Cowan, K. Cranmer, E. Gross, and O. Vitells, Asymp-
   totic formulae for likelihood-based tests of new physics,
   Eur. Phys. J. C 71, 1554 (2011).
1. Aad,87 B. Abbott,114 J. Abdallah,65 O. Abdinov,12 B. Abeloos,118 R. Aben,108 O. S. AbouZeid,138 N. L. Abraham,150
2. Abramowicz,154 H. Abreu,153 R. Abreu,117 Y. Abulaiti,147a,147b B. S. Acharya,164a,164b,b L. Adamczyk,40a D. L. Adams,27
J. Adelman,109 S. Adomeit,101 T. Adye,132 A. A. Affolder,76 T. Agatonovic-Jovin,14 J. Agricola,56
J. A. Aguilar-Saavedra,127a’127f S. P. Ahlen,24 F. Ahmadov,67’c G. Aielli,134a’134b H. Akerstedt,147a’147b T. P. A. Äkesson,83
A. V. Akimov,97 G. L. Alberghi,22a’22b J. Albert,169 S. Albrand,57 M. J. Alconada Verzini,73 M. Aleksa,321. N. Aleksandrov,67
Alexa,28b G. Alexander,154 T. Alexopoulos,10 M. Alhroob,114 M. Aliev,75a’75b G. Alimonti,93a J. Alison,33 S. P. Alkire,37
M. M. Allbrooke,150 B. W. Allen,117 P. P. Allport,19 A. Aloisio,105a105b A. Alonso,38 F. Alonso,73 C. Alpigiani,139
M. Alstaty,87 B. Alvarez Gonzalez,32 D. Alvarez Piqueras,167 M. G. Alviggi,105a105b B. T. Amadio,16 K. Amako,68
Y. Amaral Coutinho,26a C. Amelung,25 D. Amidei,91 S. P. Amor Dos Santos,127a127c A. Amorim,127a127b S. Amoroso,32
Amundsen,25 C. Anastopoulos,140 L. S. Ancu,51 N. Andari,109 T. Andeen,11 C. F. Anders,60b G. Anders,32 J. K. Anders,76
K. J. Anderson,33 A. Andreazza,93a’93b V. Andrei,60a S. Angelidakis,9 I. Angelozzi,108 P. Anger,46 A. Angerami,37
Anghinolfi,32 A. V. Anisenkov,110’d N. Anjos,13 A. Annovi,125a’125b M. Antonelli,49 A. Antonov,99 F. Anulli,133a M. Aoki,68
L. Aperio Bella,19 G. Arabidze,92 Y. Arai,68 J. P. Araque,127a A. T. H. Arce,47 F. A. Arduh,73 J-F. Arguin,96
S. Argyropoulos,65 M. Arik,20a A. J. Armbruster,144 L. J. Armitage,78 O. Arnaez,32 H. Arnold,50 M. Arratia,30 O. Arslan,23
A. Artamonov,98 G. Artoni,121 S. Artz,85 S. Asai,156 N. Asbah,44 A. Ashkenazi,154 B. Äsman,147a’147b L. Asquith,150
K. Assamagan,27 R. Astalos,145a M. Atkinson,166 N. B. Atlay,142 K. Augsten,129 G. Avolio,32 B. Axen,16 M. K. Ayoub,118
Azuelos,96’e M. A. Baak,32 A. E. Baas,60a M. J. Baca,19 H. Bachacou,137 K. Bachas,75a'75b M. Backes,32 M. Backhaus,32
P. Bagiacchi,133a133b P. Bagnaia,133a133b Y. Bai,35a J. T. Baines,132 O. K. Baker,176 E. M. Baldin,110d P. Balek,130
T. Balestri,149 F. Balli,137 W. K. Balunas,123 E. Banas,41 Sw. Banerjee,173 f A. A. E. Bannoura,175 L. Barak,32 E. L. Barberio,90
Barberis,52a 52b M. Barbero,87 T. Barillari,102 T. Barklow,144 N. Barlow,30 S. L. Barnes,86 B. M. Barnett,132 R. M. Barnett,16
Z. Barnovska,5 A. Baroncelli,135a G. Barone,25 A. J. Barr,121 L. Barranco Navarro,167 F. Barreiro,84
J. Barreiro Guimaraes da Costa,35a R. Bartoldus,144 A. E. Barton,74 P. Bartos,145a A. Basalaev,124 A. Bassalat,118
R. L. Bates,55 S.J. Batista,159 J. R. Batley,30 M. Battaglia,138 M. Bauce,133a133b F. Bauer,137 H. S. Bawa,144g
J. B. Beacham,112 M. D. Beattie,74 T. Beau,82 P. H. Beauchemin,162 P. Bechtle,23 H. P. Beck,18 h K. Becker,121 M. Becker,85
M. Beckingham,170 C. Becot,111 A. J. Beddall,20e A. Beddall,20b V. A. Bednyakov,67 M. Bedognetti,108 C. P. Bee,149
L. J. Beemster,108 T. A. Beermann,32 M. Begel,27 J. K. Behr,44 C. Belanger-Champagne,89 A. S. Bell,80 G. Bella,154
L. Bellagamba,22a A. Bellerive,31 M. Bellomo,88 K. Belotskiy,99 O. Beltramello,32 N. L. Belyaev,99 O. Benary,154
D. Benchekroun,136a M. Bender,101 K. Bendtz,147a147b N. Benekos,10 Y. Benhammou,154 E. Benhar Noccioli,176 J. Benitez,65
D. P. Benjamin,47 J. R. Bensinger,25 S. Bentvelsen,108 L. Beresford,121 M. Beretta,49 D. Berge,108 E. Bergeaas Kuutmann,165
N. Berger,5 J. Beringer,16 S. Berlendis,57 N. R. Bernard,88 C. Bernius,111 F. U. Bernlochner,23 T. Berry,79 P. Berta,130
Bertella,85 G. Bertoli,147a147b F. Bertolucci,125a125b I. A. Bertram,74 C. Bertsche,44 D. Bertsche,114 G. J. Besjes,38
O.	Bessidskaia Bylund,147a’147b M. Bessner,44 N. Besson,137 C. Betancourt,50 S. Bethke,102 A. J. Bevan,78 W. Bhimji,16
R. M. Bianchi,126 L. Bianchini,25 M. Bianco,32 O. Biebel,101 D. Biedermann,17 R. Bielski,86 N. V. Biesuz,125a125b
M. Biglietti,135a J. Bilbao De Mendizabal,51 H. Bilokon,49 M. Bindi,56 S. Binet,118 A. Bingul,20b C. Bini,133a133b
S. Biondi,22a,22b D. M. Bjergaard,47 C. W. Black,151 J. E. Black,144 K. M. Black,24 D. Blackburn,139 R. E. Blair,6
J.-B. Blanchard,137 J. E. Blanco,79 T. Blazek,145a I. Bloch,44 C. Blocker,25 W. Blum,85 a U. Blumenschein,56 S. Blunier,34a
J. Bobbink,108 V. S. Bobrovnikov,110’4 S. S. Bocchetta,83 A. Bocci,47 C. Bock,101 M. Boehler,50 D. Boerner,175
J. A. Bogaerts,32 D. Bogavac,14 A. G. Bogdanchikov,110 C. Bohm,147a V. Boisvert,79 P. Bokan,14 T. Bold,40a
A. S. Boldyrev,164a,164c M. Bomben,82 M. Bona,78 M. Boonekamp,137 A. Borisov,131 G. Borissov,74 J. Bortfeldt,101
Bortoletto,121 V. Bortolotto,62a’62b’62c K. Bos,108 D. Boscherini,22a M. Bosman,13 J. D. Bossio Sola,29 J. Boudreau,126
J. Bouffard,2 E. V. Bouhova-Thacker,74 D. Boumediene,36 C. Bourdarios,118 S. K. Boutle,55 A. Boveia,32 J. Boyd,32
032003-19

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
I. R. Boyko,67 J. Bracinik,19 A. Brandt,8 G. Brandt,56 O. Brandt,60“ U. Bratzler,157 B. Brau,88 J. E. Brau,117 H. M. Braun,175’“
W. D. Breaden Madden,55 K. Brendlinger,123 A. J. Brennan,90 L. Brenner,108 R. Brenner,165 S. Bressler,172 T. M. Bristow,48
D. Britton,55 D. Britzger,44 F. M. Brochu,30 I. Brock,23 R. Brock,92 G. Brooijmans,37 T. Brooks,79 W. K. Brooks,34b
J. Brosamer,16 E. Brost,117 J. H Broughton,19 P. A. Bruckman de Renstrom,41 D. Bruncko,145b R. Bruneliere,50 A. Bruni,22a
Bruni,22a BH Brunt,30 M. Bruschi,22a N. Bruscino,23 P. Bryant,33 L. Bryngemark,83 T. Buanes,15 Q. Buat,143
P. Buchholz,142 A. G. Buckley,551. A. Budagov,67 F. Buehrer,50 M. K. Bugge,120 O. Bulekov,99 D. Bullock,8 H. Burckhart,32
S. Burdin,76 C. D. Burgard,50 B. Burghgrave,109 K. Burka,41 S. Burke,132 I. Burmeister,45 E. Busato,36 D. Büscher,50
V. Büscher,85 P. Bussey,55 J. M. Butler,24 C. M. Buttar,55 J. M. Butterworth,80 P. Butti,108 W. Buttinger,27 A. Buzatu,55
A.R. Buzykaev,110,d S. Cabrera Urban,167 D. Caforio,129 V.M. Cairo,39a,39b O. Cakir,4a N. Calace,51 P. Calafiura,16
A. Calandri,87 G. Calderini,82 P. Calfayan,101 L. P. Caloba,26a D. Calvet,36 S. Calvet,36 T. P. Calvet,87 R. Camacho Toro,33
S. Camarda,32 P. Camarri,134a134b D. Cameron,120 R. Caminal Armadans,166 C. Camincher,57 S. Campana,32
M. Campanelli,80 A. Camplani,93a,93b A. Campoverde,149 V. Canale,105a,105b A. Canepa,160a M. Cano Bret,35e J. Cantero,115
R. Cantrill,127a T. Cao,42 M. D. M. Capeans Garrido,32 I. Caprini,28b M. Caprini,28b M. Capua,39a 39b R. Caputo,85
R. M. Carbone,37 R. Cardarelli,134a F. Cardillo,50 I. Carli,130 T. Carli,32 G. Carlino,105a L. Carminati,93“’93b S. Caron,107
Carquin,34b G. D. Carrillo-Montoya,32 J. R. Carter,30 J. Carvalho,127“’127c D. Casadei,19 M. P. Casado,13 i M. Casolino,13
D. W. Casper,163 E. Castaneda-Miranda,146“ R. Castelijn,108 A. Castelli,108 V. Castillo Gimenez,167 N. F. Castro,127“’j
A. Catinaccio,32 J. R. Catmore,120 A. Cattai,32 J. Caudron,85 V. Cavaliere,166 E. Cavallaro,13 D. Cavalli,93“
M. Cavalli-Sforza,13 V. Cavasinni,125“’125b F. Ceradini,135“’135b L. Cerda Alberich,167 B. C. Cerio,47 A. S. Cerqueira,26b
A. Cerri,150 L. Cerrito,78 F. Cerutti,16 M. Cerv,32 A. Cervelli,18 S.A. Cetin,20d A. Chafaq,136a D. Chakraborty,109
S. K. Chan,59 Y. L. Chan,62a P. Chang,166 J. D. Chapman,30 D. G. Charlton,19 A. Chatterjee,51 C. C. Chau,159
A. Chavez Barajas,150 S. Che,112 S. Cheatham,74 A. Chegwidden,92 S. Chekanov,6 S. V. Chekulaev,160a G. A. Chelkov,67,k
M. A. Chelstowska,91 C. Chen,66 H. Chen,27 K. Chen,149 S. Chen,35c S. Chen,156 X. Chen,35f Y. Chen,69 H. C. Cheng,91
J Cheng,35a Y. Cheng,33 A. Cheplakov,67 E. Cheremushkina,131 R. Cherkaoui El Moursli,136e V. Chernyatin,27^ E. Cheu,7
L. Chevalier,137 V. Chiarella,49 G. Chiarelli,125a,125b G. Chiodini,75a A. S. Chisholm,19 A. Chitan,28b M. V. Chizhov,67
K. Choi,63 A. R. Chomont,36 S. Chouridou,9 B. K. B. Chow,101 V. Christodoulou,80 D. Chromek-Burckhart,32 J. Chudoba,128
J. Chuinard,89 J. J. Chwastowski,41 L. Chytka,116 G. Ciapetti,133“’133b A. K. Ciftci,4a D. Cinca,55 V. Cindro,77
A. Cioara,23 A. Ciocio,16 F. Cirotto,105a105b Z. H. Citron,172 M. Citterio,93a M. Ciubancan,28b A. Clark,51 B.L. Clark,59
M. R. Clark,37 P. J. Clark,48 R. N. Clarke,16 C. Clement,147a,147b Y. Coadou,87 M. Cobal,164a,164c A. Coccaro,51 J. Cochran,66
L. Coffey,25 L. Colasurdo,107 B. Cole,37 A. P. Colijn,108 J. Collot,57 T. Colombo,32 G. Compostella,102
P. Conde Muino,127“’127b E. Coniavitis,50 S. H. Connell,146b I. A. Connelly,79 V. Consorti,50 S. Constantinescu,28b G. Conti,32
F. Conventi,105al M. Cooke,16 B. D. Cooper,80 A.M. Cooper-Sarkar,121 K.J. R. Cormier,159 T. Cornelissen,175
M. Corradi,133a,133b F. Corriveau,89,m A. Corso-Radu,163 A. Cortes-Gonzalez,13 G. Cortiana,102 G. Costa,93a M. J. Costa,167
Costanzo,140 G. Cottin,30 G. Cowan,79 B. E. Cox,86 K. Cranmer,111 S. J. Crawley,55 G. Cree,31 S. Crepe-Renaudin,57
1. Crescioli,82 W. A. Cribbs,147M47b M. Crispin Ortuzar,121 M. Cristinziani,23 V. Croft,107 G. Crosetti,39a39b
   T. Cuhadar Donszelmann,140 J. Cummings,176 M. Curatolo,49 J. Cuth,85 C. Cuthbert,151 H. Czirr,142 P. Czodrowski,3
2. D’amen,22“’22b S. D’Auria,55 M. D’Onofrio,76 M. J. Da Cunha Sargedas De Sousa,127“’127b C. Da Via,86 W. Dabrowski,40a
   T. Dado,145a T. Dai,91 O. Dale,15 F. Dallaire,96 C. Dallapiccola,88 M. Dam,38 J. R. Dandoy,33 N. P. Dang,50 A. C. Daniells,19
   N. S. Dann,86 M. Danninger,168 M. Dano Hoffmann,137 V. Dao,50 G. Darbo,52a S. Darmora,8 J. Dassoulas,3 A. Dattagupta,63
   W. Davey,23 C. David,169 T. Davidek,130 M. Davies,154 P. Davison,80 E. Dawe,90 I. Dawson,140
   R. K. Daya-Ishmukhametova,88 K. De,8 R. de Asmundis,105a A. De Benedetti,114 S. De Castro,22“’22b S. De Cecco,82
   N. De Groot,107 P. de Jong,108 H. De la Torre,84 F. De Lorenzi,66 A. De Maria,56 D. De Pedis,133a A. De Salvo,133a
   U. De Sanctis,150 A. De Santo,150 J. B. De Vivie De Regie,118 W. J. Dearnaley,74 R. Debbe,27 C. Debenedetti,138
V. Dedovich,67 N. Dehghanian,31. Deigaard,108 M. Del Gaudio,39“’39b J. Del Peso,84 T. Del Prete,125a125b D. Delgove,118
Deliot,137 C. M. Delitzsch,51 M. Deliyergiyev,77 A. Dell’Acqua,32 L. Dell’Asta,24 M. Dell’Orso,125“’125b
M. Della Pietra,105“’l D. della Volpe,51 M. Delmastro,5 P. A. Delsart,57 C. Deluca,108 D. A. DeMarco,159 S. Demers,176
M. Demichev,67 A. Demilly,82 S. P. Denisov,131 D. Denysiuk,137 D. Derendarz,41 J. E. Derkaoui,136d F. Derue,82 P. Dervan,76
K. Desch,23 C. Deterre,44 K. Dette,45 P. O. Deviveiros,32 A. Dewhurst,132 S. Dhaliwal,25 A. Di Ciaccio,134“’134b
L. Di Ciaccio,5 W. K. Di Clemente,123 C. Di Donato,133a,133b A. Di Girolamo,32 B. Di Girolamo,32 B. Di Micco,135a,135b
R. Di Nardo,32 A. Di Simone,50 R. Di Sipio,159 D. Di Valentino,31 C. Diaconu,87 M. Diamond,159 F. A. Dias,48 M. A. Diaz,34a
032003-20

SEARCH FOR PAIR PRODUCTION OF GLUINOS
PHYSICAL REVIEW D 94, 032003 (2016)
B. Diehl,91 J. Dietrich,17 S. Diglio,87 A. Dimitrievska,14 J. Dingfelder,23 P. Dita,28b S. Dita,28b F. Dittus,32 F. Djama,87
T. Djobava,53b J. I. Djuvsland,60a M. A. B. do Vale,26c D. Dobos,32 M. Dobre,28b C. Doglioni,83 T. Dohmae,156 J. Dolejsi,130
Z. Dolezal,130 B. A. Dolgoshein,99a M. Donadelli,26d S. Donati,125a125b P. Dondero,122a122b J. Donini,36 J. Dopke,132
A. Doria,105a M. T. Dova,73 A. T. Doyle,55 E. Drechsler,56 M. Dris,10 Y. Du,35d J. Duarte-Campderros,154 E. Duchovni,172
Duckeck,101 O. A. Ducu,96 n D. Duda,108 A. Dudarev,32 E. M. Duffield,16 L. Duflot,118 L. Duguid,79 M. Dührssen,32
M. Dumancic,172 M. Dunford,60a H. Duran Yildiz,4a M. Düren,54 A. Durglishvili,53b D. Duschinger,46 B. Dutta,44
M. Dyndal,44 C. Eckardt,44 K. M. Ecker,102 R. C. Edgar,91 N. C. Edwards,48 T. Eifert,32 G. Eigen,15 K. Einsweiler,16
T. Ekelof,165 M. El Kacimi,136c V. Ellajosyula,87 M. Ellert,165 S. Elles,5 F. Ellinghaus,175 A. A. Elliot,169 N. Ellis,32
J. Elmsheuser,27 M. Elsing,32 D. Emeliyanov,132 Y. Enari,156 O. C. Endner,85 M. Endo,119 J. S. Ennis,170 J. Erdmann,45
A. Ereditato,18 G. Ernis,175 J. Ernst,2 M. Ernst,27 S. Errede,166 E. Ertel,85 M. Escalier,118 H. Esch,45 C. Escobar,126
1. Esposito,49 A.I. Etienvre,137 E. Etzion,154 H. Evans,63 A. Ezhilov,124 F. Fabbri,22a22b L. Fabbri,22a22b G. Facini,33
   R.M. Fakhrutdinov,131 S. Falciano,133a R.J. Falla,80 J. Faltova,130 Y. Fang,35a M. Fanti,93a93b A. Farbin,8 A. Farilla,135a
2. Farina,126 T. Farooque,13 S. Farrell,16 S. M. Farrington,170 P. Farthouat,32 F. Fassi,136e P. Fassnacht,32 D. Fassouliotis,9
   M. Faucci Giannelli,79 A. Favareto,52a52b W. J. Fawcett,121 L. Fayard,118 O. L. Fedin,124’“ W. Fedorko,168 S. Feigl,120
L. Feligioni,87 C. Feng,35d E. J. Feng,32 H. Feng,91 A. B. Fenyuk,131 L. Feremenga,8 P. Fernandez Martinez,167
S. Fernandez Perez,13 J. Ferrando,55 A. Ferrari,165 P. Ferrari,108 R. Ferrari,122a D. E. Ferreira de Lima,60b A. Ferrer,167
Ferrere,51 C. Ferretti,91 A. Ferretto Parodi,52a52b F. Fiedler,85 A. Filipcic,77 M. Filipuzzi,44 F. Filthaut,107
M. Fincke-Keeler,169 K. D. Finelli,151 M. C. N. Fiolhais,127a127c L. Fiorini,167 A. Firan,42 A. Fischer,2 C. Fischer,13
J. Fischer,175 W. C. Fisher,92 N. Flaschel,44 I. Fleck,142 P. Fleischmann,91 G. T. Fletcher,140 R. R. M. Fletcher,123 T. Flick,175
A. Floderus,83 L. R. Flores Castillo,62a M. J. Flowerdew,102 G. T. Forcolin,86 A. Formica,137 A. Forti,86 A. G. Foster,19
Fournier,118 H. Fox,74 S. Fracchia,13 P. Francavilla,82 M. Franchini,22a22b D. Francis,32 L. Franconi,120 M. Franklin,59
M. Frate,163 M. Fraternali,122a122b D. Freeborn,80 S. M. Fressard-Batraneanu,32 F. Friedrich,46 D. Froidevaux,32
J. A. Frost,121 C. Fukunaga,157 E. Fullana Torregrosa,85 T. Fusayasu,103 J. Fuster,167 C. Gabaldon,57 O. Gabizon,175
A. Gabrielli,22a22b A. Gabrielli,16 G. P. Gach,40a S. Gadatsch,32 S. Gadomski,51 G. Gagliardi,52a52b L. G. Gagnon,96
P. Gagnon,63 C. Galea,107 B. Galhardo,127a127c E. J. Gallas,121 B.J. Gallop,132 P. Gallus,129 G. Galster,38 K.K. Gan,112
J. Gao,35b’87 Y. Gao,48 Y. S. Gao,144,g F. M. Garay Walls,48 C. García,167 J. E. García Navarro,167 M. Garcia-Sciveres,16
R. W. Gardner,33 N. Garelli,144 V. Garonne,120 A. Gascon Bravo,44 C. Gatti,49 A. Gaudiello,52a52b G. Gaudio,122a B. Gaur,142
L. Gauthier,96 I. L. Gavrilenko,97 C. Gay,168 G. Gaycken,23 E. N. Gazis,10 Z. Gecse,168 C. N. P. Gee,132 Ch. Geich-Gimbel,23
M. P. Geisler,60a C. Gemme,52a M. H. Genest,57 C. Geng,35bp S. Gentile,133a133b S. George,79 D. Gerbaudo,13 A. Gershon,154
S. Ghasemi,142 H. Ghazlane,136b M. Ghneimat,23 B. Giacobbe,22a S. Giagu,133a133b P. Giannetti,125a125b B. Gibbard,27
S. M. Gibson,79 M. Gignac,168 M. Gilchriese,16 T. P. S. Gillam,30 D. Gillberg,31 G. Gilles,175 D. M. Gingrich,3 e N. Giokaris,9
M. P. Giordani,164a164c F. M. Giorgi,22a F. M. Giorgi,17 P. F. Giraud,137 P. Giromini,59 D. Giugni,93a F. Giuli,121 C. Giuliani,102
M. Giulini,60b B. K. Gjelsten,120 S. Gkaitatzis,155 I. Gkialas,155 E. L. Gkougkousis,118 L. K. Gladilin,100 C. Glasman,84
J. Glatzer,32 P. C. F. Glaysher,48 A. Glazov,44 M. Goblirsch-Kolb,102 J. Godlewski,41 S. Goldfarb,91 T. Golling,51
Golubkov,131 A. Gomes,127a127b127d R. Gonpalo,127a J. Goncalves Pinto Firmino Da Costa,137 L. Gonella,19
A. Gongadze,67 S. González de la Hoz,167 G. Gonzalez Parra,13 S. Gonzalez-Sevilla,51 L. Goossens,32 P. A. Gorbounov,98
1. A. Gordon,27 I. Gorelov,106 B. Gorini,32 E. Gorini,75a75b A. Gorisek,77 E. Gornicki,41 A. T. Goshaw,47 C. Gössling,45
   M. I. Gostkin,67 C. R. Goudet,118 D. Goujdami,136c A. G. Goussiou,139 N. Govender,146b q E. Gozani,153 L. Graber,56
2. Grabowska-Bold,40a P.O.J. Gradin,57 P. Grafström,22a22b J. Gramling,51 E. Gramstad,120 S. Grancagnolo,17
V. Gratchev,124 P. M. Gravila,28e H. M. Gray,32 E. Graziani,135a Z. D. Greenwood,81,r C. Grefe,23 K. Gregersen,80
M. Gregor,44 P. Grenier,144 K. Grevtsov,5 J. Griffiths,8 A. A. Grillo,138 K. Grimm,74 S. Grinstein,13,s Ph. Gris,36
J.-F. Grivaz,118 S. Groh,85 J. P. Grohs,46 E. Gross,172 J. Grosse-Knetter,56 G. C. Grossi,81 Z. J. Grout,150 L. Guan,91
W. Guan,173 J. Guenther,129 F. Guescini,51 D. Guest,163 O. Gueta,154 E. Guido,52a52b T. Guillemin,5 S. Guindon,2 U. Gul,55
Gumpert,32 J. Guo,35e Y. Guo,35bp S. Gupta,121 G. Gustavino,133a133b P. Gutierrez,114 N. G. Gutierrez Ortiz,80
Gutschow,46 C. Guyot,137 C. Gwenlan,121 C. B. Gwilliam,76 A. Haas,111 C. Haber,16 H. K. Hadavand,8 N. Haddad,136e
Hadef,87 P. Haefner,23 S. Hageböck,23 Z. Hajduk,41 H. Hakobyan,177a M. Haleem,44 J. Haley,115 G. Halladjian,92
D. Hallewell,87 K. Hamacher,175 P. Hamal,116 K. Hamano,169 A. Hamilton,146a G. N. Hamity,140 P. G. Hamnett,44
L. Han,35b K. Hanagaki,68,t K. Hanawa,156 M. Hance,138 B. Haney,123 P. Hanke,60a R. Hanna,137 J. B. Hansen,38
J. D. Hansen,38 M. C. Hansen,23 P. H. Hansen,38 K. Hara,161 A. S. Hard,173 T. Harenberg,175 F. Hariri,118 S. Harkusha,94
032003-21

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
R. D. Harrington,48 P. F. Harrison,170 F. Hartjes,108 N. M. Hartmann,101 M. Hasegawa,69 Y. Hasegawa,141 A. Hasib,114
S. Hassani,137 S. Haug,18 R. Hauser,92 L. Hauswald,46 M. Havranek,128 C. M. Hawkes,19 R. J. Hawkings,32 D. Hayden,92
P. Hays,121 J. M. Hays,78 H. S. Hayward,76 S.J. Haywood,132 S.J. Head,19 T. Heck,85 V. Hedberg,83 L. Heelan,8
S. Heim,123 T. Heim,16 B. Heinemann,16 J. J. Heinrich,101 L. Heinrich,111 C. Heinz,54 J. Hejbal,128 L. Helary,24
S. Hellman,147a147b C. Helsens,32 J. Henderson,121 R. C. W. Henderson,74 Y. Heng,173 S. Henkelmann,168
A. M. Henriques Correia,32 S. Henrot-Versille,118 G. H. Herbert,17 Y. Hernández Jiménez,167 G. Herten,50
R. Hertenberger,101 L. Hervas,32 G. G. Hesketh,80 N. P. Hessey,108 J. W. Hetherly,42 R. Hickling,78 E. Higón-Rodriguez,167
Hill,169 J. C. Hill,30 K. H. Hiller,44 S. J. Hillier,19 I. Hinchliffe,16 E. Hines,123 R. R. Hinman,16 M. Hirose,158
Hirschbuehl,175 J. Hobbs,149 N. Hod,160a M. C. Hodgkinson,140 P. Hodgson,140 A. Hoecker,32 M. R. Hoeferkamp,106
F. Hoenig,101 D. Hohn,23 T. R. Holmes,16 M. Homann,45 T. M. Hong,126 B. H. Hooberman,166 W. H. Hopkins,117 Y. Horii,104
A. J. Horton,143 J-Y. Hostachy,57 S. Hou,152 A. Hoummada,136a J. Howarth,44 M. Hrabovsky,116 I. Hristova,17 J. Hrivnac,118
T. Hryn’ova,5 A. Hrynevich,95 C. Hsu,146c P. J. Hsu,152u S.-C. Hsu,139 D. Hu,37 Q. Hu,35b Y. Huang,44 Z. Hubacek,129
Hubaut,87 F. Huegging,23 T. B. Huffman,121 E. W. Hughes,37 G. Hughes,74 M. Huhtinen,32 T. A. Hülsing,85 P. Huo,149
N. Huseynov,67 c J. Huston,92 J. Huth,59 G. Iacobucci,51 G. Iakovidis,27 I. Ibragimov,142 L. Iconomidou-Fayard,118
Ideal,176 Z. Idrissi,136e P. Iengo,32 O. Igonkina,108 v T. Iizawa,171 Y. Ikegami,68 M. Ikeno,68 Y. Ilchenko,11w D. Iliadis,155
N. Ilic,144 T. Ince,102 G. Introzzi,122a122b P. Ioannou,9 a M. Iodice,135a K. Iordanidou,37 V. Ippolito,59 M. Ishino,70
M. Ishitsuka,158 R. Ishmukhametov,112 C. Issever,121 S. Istin,20a F. Ito,161 J. M. Iturbe Ponce,86 R. Iuppa,134a134b
W. Iwanski,41 H. Iwasaki,68 J. M. Izen,43 V. Izzo,105a S. Jabbar,3 B. Jackson,123 M. Jackson,76 P. Jackson,1 V. Jain,2
K. B. Jakobi,85 K. Jakobs,50 S. Jakobsen,32 T. Jakoubek,128 D. O. Jamin,115 D. K. Jana,81 E. Jansen,80 R. Jansky,64
J. Janssen,23 M. Janus,56 G. Jarlskog,83 N. Javadov,67’c T. Javurek,50 F. Jeanneau,137 L. Jeanty,16 J. Jejelava,53a’x G.-Y. Jeng,151
Jennens,90 P. Jenni,50’y J. Jentzsch,45 C. Jeske,170 S. Jézéquel,5 H. Ji,173 J. Jia,149 H. Jiang,66 Y. Jiang,35b S. Jiggins,80
J. Jimenez Pena,167 S. Jin,35a A. Jinaru,28b O. Jinnouchi,158 P. Johansson,140 K. A. Johns,7 W. J. Johnson,139
K. Jon-And,147a,147b G. Jones,170 R. W. L. Jones,74 S. Jones,7 T. J. Jones,76 J. Jongmanns,60a P. M. Jorge,127a,127b
J. Jovicevic,160a X. Ju,173 A. Juste Rozas,13’s M. K. Köhler,172 A. Kaczmarska,41 M. Kado,118 H. Kagan,112 M. Kagan,144
S. J. Kahn,87 E. Kajomovitz,47 C. W. Kalderon,121 A. Kaluza,85 S. Kama,42 A. Kamenshchikov,131 N. Kanaya,156 S. Kaneti,30
L. Kanjir,77 V. A. Kantserov,99 J. Kanzaki,68 B. Kaplan,111 L. S. Kaplan,173 A. Kapliy,33 D. Kar,146c K. Karakostas,10
A. Karamaoun,3 N. Karastathis,10 M. J. Kareem,56 E. Karentzos,10 M. Karnevskiy,85 S. N. Karpov,67 Z. M. Karpova,67
K. Karthik,111 V. Kartvelishvili,74 A. N. Karyukhin,131 K. Kasahara,161 L. Kashif,173 R. D. Kass,112 A. Kastanas,15
Y. Kataoka,156 C. Kato,156 A. Katre,51 J. Katzy,44 K. Kawagoe,72 T. Kawamoto,156 G. Kawamura,56 S. Kazama,156
V. F. Kazanin,110d R. Keeler,169 R. Kehoe,42 J. S. Keller,44 J. J. Kempster,79 K Kentaro,104 H. Keoshkerian,159 O. Kepka,128
P. Kersevan,77 S. Kersten,175 R. A. Keyes,89 F. Khalil-zada,12 A. Khanov,115 A. G. Kharlamov,110 d T. J. Khoo,51
V. Khovanskiy,98 E. Khramov,67 J. Khubua,53b z S. Kido,69 H. Y. Kim,8 S. H. Kim,161 Y. K. Kim,33 N. Kimura,155
M. Kind,17 B. T. King,76 M. King,167 S. B. King,168 J. Kirk,132 A. E. Kiryunin,102 T. Kishimoto,69 D. Kisielewska,40a
Kiss,50 K. Kiuchi,161 O. Kivernyk,137 E. Kladiva,145b M. H. Klein,37 M. Klein,76 U. Klein,76 K. Kleinknecht,85
P. Klimek,147a147b A. Klimentov,27 R. Klingenberg,45 J. A. Klinger,140 T. Klioutchnikova,32 E.-E. Kluge,60a P. Kluit,108
S. Kluth,102 J. Knapik,41 E. Kneringer,64 E. B. F. G. Knoops,87 A. Knue,55 A. Kobayashi,156 D. Kobayashi,158
T. Kobayashi,156 M. Kobel,46 M. Kocian,144 P. Kodys,130 T. Koffas,31 E. Koffeman,108 T. Koi,144 H. Kolanoski,17 M. Kolb,60b
Koletsou,5 A. A. Komar,97 a Y. Komori,156 T. Kondo,68 N. Kondrashova,44 K. Köneke,50 A. C. König,107 T. Kono,68 aa
R. Konoplich,111bb N. Konstantinidis,80 R. Kopeliansky,63 S. Koperny,40a L. Köpke,85 A. K. Kopp,50 K. Korcyl,41
K. Kordas,155 A. Korn,80 A.A. Korol,110d I. Korolkov,13 E.V. Korolkova,140 O. Kortner,102 S. Kortner,102 T. Kosek,130
V. V. Kostyukhin,23 A. Kotwal,47 A. Kourkoumeli-Charalampidi,155 C. Kourkoumelis,9 V. Kouskoura,27
A. B. Kowalewska,41 R. Kowalewski,169 T. Z. Kowalski,40a C. Kozakai,156 W. Kozanecki,137 A. S. Kozhin,131
V. A. Kramarenko,100 G. Kramberger,77 D. Krasnopevtsev,99 M. W. Krasny,82 A. Krasznahorkay,32 J. K. Kraus,23
Kravchenko,27 M. Kretz,60c J. Kretzschmar,76 K. Kreutzfeldt,54 P. Krieger,159 K. Krizka,33 K. Kroeninger,45 H. Kroha,102
J. Kroll,123 J. Kroseberg,23 J. Krstic,14 U. Kruchonak,67 H. Krüger,23 N. Krumnack,66 A. Kruse,173 M. C. Kruse,47
M. Kruskal,24 T. Kubota,90 H. Kucuk,80 S. Kuday,4b J. T. Kuechler,175 S. Kuehn,50 A. Kugel,60c F. Kuger,174 A. Kuhl,138
T. Kuhl,44 V. Kukhtin,67 R. Kukla,137 Y. Kulchitsky,94 S. Kuleshov,34b M. Kuna,133a133b T. Kunigo,70 A. Kupco,128
Kurashige,69 Y. A. Kurochkin,94 V. Kus,128 E. S. Kuwertz,169 M. Kuze,158 J. Kvita,116 T. Kwan,169 D. Kyriazopoulos,140
032003-22

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...	PHYSICAL	REVIEW	D	94,	032003 (2016)
A. La Rosa,102 J. L. La Rosa Navarro,26d L. La Rotonda,39a’39b C. Lacasta,167 F. Lacava,133a’133b J. Lacey,31 H. Lacker,17
1. Lacour,82 V. R. Lacuesta,167 E. Ladygin,67 R. Lafaye,5 B. Laforge,82 T. Lagouri,176 S. Lai,56 S. Lammers,63 W. Lampl,7
2. Lançon,137 U. Landgraf,50 M. P. J. Landon,78 V. S. Lang,60a J. C. Lange,13 A. J. Lankford,163 F. Lanni,27 K. Lantzsch,23
   A. Lanza,122a S. Laplace,82 C. Lapoire,32 J. F. Laporte,137 T. Lari,93a F. Lasagni Manghi,22a22b M. Lassnig,32 P. Laurelli,49
   W. Lavrijsen,16 A. T. Law,138 P. Laycock,76 T. Lazovich,59 M. Lazzaroni,93a93b B. Le,90 O. Le Dortz,82 E. Le Guirriec,87
P. Le Quilleuc,137 M. LeBlanc,169 T. LeCompte,6 F. Ledroit-Guillon,57 C. A. Lee,27 S. C. Lee,152 L. Lee,1 G. Lefebvre,82
M. Lefebvre,169 F. Legger,101 C. Leggett,16 A. Lehan,76 G. Lehmann Miotto,32 X. Lei,7 W. A. Leight,31 A. Leisos,155 cc
G. Leister,176 M. A. L. Leite,26d R. Leitner,130 D. Lellouch,172 B. Lemmer,56 K.J. C. Leney,80 T. Lenz,23 B. Lenzi,32
R. Leone,7 S. Leone,125a125b C. Leonidopoulos,48 S. Leontsinis,10 G. Lerner,150 C. Leroy,96 A. A. J. Lesage,137 C. G. Lester,30
M. Levchenko,124 J. Levêque,5 D. Levin,91 L. J. Levinson,172 M. Levy,19 D. Lewis,78 A. M. Leyko,23 M. Leyton,43 B. Li,35bp
Li,149 H. L. Li,33 L. Li,47 L. Li,35e Q. Li,35a S. Li,47 X. Li,86 Y. Li,142 Z. Liang,35a B. Liberti,134a A. Liblong,159 P. Lichard,32
K. Lie,166 J. Liebal,23 W. Liebig,15 A. Limosani,151 S. C. Lin,152 dd T. H. Lin,85 B. E. Lindquist,149 A. E. Lionti,51
Lipeles,123 A. Lipniacka,15 M. Lisovyi,60b T. M. Liss,166 A. Lister,168 A. M. Litke,138 B. Liu,152 ee D. Liu,152 H. Liu,91
Liu,27 J. Liu,87 J. B. Liu,35b K. Liu,87 L. Liu,166 M. Liu,47 M. Liu,35b Y. L. Liu,35b Y. Liu,35b M. Livan,122a122b A. Lleres,57
J. Llorente Merino,35a S. L. Lloyd,78 F. Lo Sterzo,152 E. Lobodzinska,44 P. Loch,7 W. S. Lockman,138 F. K. Loebinger,86
A. E. Loevschall-Jensen,38 K. M. Loew,25 A. Loginov,176 T. Lohse,17 K. Lohwasser,44 M. Lokajicek,128 B. A. Long,24
J. D. Long,166 R. E. Long,74 L. Longo,75a75b K. A. Looper,112 L. Lopes,127a D. Lopez Mateos,59 B. Lopez Paredes,140
Lopez Paz,13 A. Lopez Solis,82 J. Lorenz,101 N. Lorenzo Martinez,63 M. Losada,21 P. J. Lösel,101 X. Lou,35a A. Lounis,118
J. Love,6 P. A. Love,74 H. Lu,62a N. Lu,91 H. J. Lubatti,139 C. Luci,133a133b A. Lucotte,57 C. Luedtke,50 F. Luehring,63
W. Lukas,64 L. Luminari,133a O. Lundberg,147a147b B. Lund-Jensen,148 D. Lynn,27 R. Lysak,128 E. Lytken,83 V. Lyubushkin,67
Ma,27 L.L. Ma,35d Y. Ma,35d G. Maccarrone,49 A. Macchiolo,102 C. M. Macdonald,140 B. Macek,77
J. Machado Miguens,123’127b D. Madaffari,87 R. Madar,36 H. J. Maddocks,165 W. F. Mader,46 A. Madsen,44 J. Maeda,69
S. Maeland,15 T. Maeno,27 A. Maevskiy,100 E. Magradze,56 J. Mahlstedt,108 C. Maiani,118 C. Maidantchik,26a A. A. Maier,102
T. Maier,101 A. Maio,127a’127b’127d S. Majewski,117 Y. Makida,68 N. Makovec,118 B. Malaescu,82 Pa. Malecki,41
V. P. Maleev,124 F. Malek,57 U. Mallik,65 D. Malon,6 C. Malone,144 S. Maltezos,10 S. Malyukov,32 J. Mamuzic,167
Mancini,49 B. Mandelli,32 L. Mandelli,93a I. Mandic,77 J. Maneira,127a127b L. Manhaes de Andrade Filho,26b
J. Manjarres Ramos,160b A. Mann,101 B. Mansoulie,137 J. D. Mansour,35a R. Mantifel,89 M. Mantoani,56 S. Manzoni,93a’93b
L. Mapelli,32 G. Marceca,29 L. March,51 G. Marchiori,82 M. Marcisovsky,128 M. Marjanovic,14 D. E. Marley,91
Marroquim,26a S. P. Marsden,86 Z. Marshall,16 S. Marti-Garcia,167 B. Martin,92 T. A. Martin,170 V. J. Martin,48
Martin dit Latour,15 M. Martinez,13s S. Martin-Haugh,132 V. S. Martoiu,28b A. C. Martyniuk,80 M. Marx,139 A. Marzin,32
L. Masetti,85 T. Mashimo,156 R. Mashinistov,97 J. Masik,86 A. L. Maslennikov,110’4 I. Massa,22a’22b L. Massa,22a’22b
P. Mastrandrea,5 A. Mastroberardino,39a’39b T. Masubuchi,156 P. Mättig,175 J. Mattmann,85 J. Maurer,28b S.J. Maxfield,76
A. Maximov,1104 R. Mazini,152 S. M. Mazza,93a,93b N. C. Mc Fadden,106 G. Mc Goldrick,159 S. P. Mc Kee,91 A. McCarn,91
R. L. McCarthy,149 T. G. McCarthy,31 L. I. McClymont,80 E. F. McDonald,90 K. W. McFarlane,58,a J. A. Mcfayden,80
Mchedlidze,56 S.J. McMahon,132 R. A. McPherson,169“ M. Medinnis,44 S. Meehan,139 S. Mehlhase,101 A. Mehta,76
K. Meier,60a C. Meineck,101 B. Meirose,43 D. Melini,167 B. R. Mellado Garcia,146c M. Melo,145a F. Meloni,18
Mengarelli,22a,22b S. Menke,102 E. Meoni,162 S. Mergelmeyer,17 P. Mermod,51 L. Merola,105a,105b C. Meroni,93a
S. Merritt,33 A. Messina,133a,133b J. Metcalfe,6 A. S. Mete,163 C. Meyer,85 C. Meyer,123 J-P. Meyer,137 J. Meyer,108
Meyer Zu Theenhausen,60“ F. Miano,150 R. P. Middleton,132 S. Miglioranzi,52a52b L. Mijovic,23 G. Mikenberg,172
M. Mikestikova,128 M. Mikuz,77 M. Milesi,90 A. Milic,64 D. W. Miller,33 C. Mills,48 A. Milov,172 D. A. Milstead,147a,147b
A. Minaenko,131 Y. Minami,156 I. A. Minashvili,67 A. I. Mincer,111 B. Mindur,40a M. Mineev,67 Y. Ming,173 L. M. Mir,13
K. P. Mistry,123 T. Mitani,171 J. Mitrevski,101 V. A. Mitsou,167 A. Miucci,51 P. S. Miyagawa,140 J. U. Mjörnmark,83
T. Moa,147a,147b K. Mochizuki,96 S. Mohapatra,37 S. Molander,147a,147b R. Moles-Valls,23 R. Monden,70 M. C. Mondragon,92
K. Mönig,44 J. Monk,38 E. Monnier,87 A. Montalbano,149 J. Montejo Berlingen,32 F. Monticelli,73 S. Monzani,93a93b
R. W. Moore,3 N. Morange,118 D. Moreno,21 M. Moreno Llacer,56 P. Morettini,52a D. Mori,143 T. Mori,156 M. Morii,59
M. Morinaga,156 V. Morisbak,120 S. Moritz,85 A. K. Morley,151 G. Mornacchi,32 J. D. Morris,78 S.S. Mortensen,38
L. Morvaj,149 M. Mosidze,53b J. Moss,144 K. Motohashi,158 R. Mount,144 E. Mountricha,27 S. V. Mouraviev,97,a
J. W. Moyse,88 S. Muanza,87 R. D. Mudd,19 F. Mueller,102 J. Mueller,126 R. S. P. Mueller,101 T. Mueller,30
032003-23

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
D. Muenstermann,74 P. Mullen,55 G. A. Mullier,18 F. J. Munoz Sanchez,86 J. A. Murillo Quijada,19 W. J. Murray,170132
Musheghyan,56 M. Muskinja,77 A. G. Myagkov,131,ff M. Myska,129 B. P. Nachman,144 O. Nackenhorst,51 K. Nagai,121
R. Nagai,68,aa K. Nagano,68 Y. Nagasaka,61 K. Nagata,161 M. Nagel,50 E. Nagy,87 A. M. Nairz,32 Y. Nakahama,32
K. Nakamura,68 T. Nakamura,156 I. Nakano,113 H. Namasivayam,43 R. F. Naranjo Garcia,44 R. Narayan,11
D. I. Narrias Villar,60a I. Naryshkin,124 T. Naumann,44 G. Navarro,21 R. Nayyar,7 H. A. Neal,91 P. Yu. Nechaeva,97
T. J. Neep,86 P. D. Nef,144 A. Negri,122a,122b M. Negrini,22a S. Nektarijevic,107 C. Nellist,118 A. Nelson,163 S. Nemecek,128
P. Nemethy,111 A. A. Nepomuceno,26a M. Nessi,32,gg M. S. Neubauer,166 M. Neumann,175 R. M. Neves,111 P. Nevski,27
P. R. Newman,19 D. H. Nguyen,6 T. Nguyen Manh,96 R. B. Nickerson,121 R. Nicolaidou,137 J. Nielsen,138 A. Nikiforov,17
V. Nikolaenko,131^ I. Nikolic-Audit,82 K. Nikolopoulos,19 J. K. Nilsen,120 P. Nilsson,27 Y. Ninomiya,156 A. Nisati,133a
R. Nisius,102 T. Nobe,156 L. Nodulman,6 M. Nomachi,119 I. Nomidis,31 T. Nooney,78 S. Norberg,114 M. Nordberg,32
N. Norjoharuddeen,121 O. Novgorodova,46 S. Nowak,102 M. Nozaki,68 L. Nozka,116 K. Ntekas,10 E. Nurse,80 F. Nuti,90
O’grady,7 D. C. O’Neil,143 A. A. O’Rourke,44 V. O’Shea,55 F. G. Oakham,31e H. Oberlack,102 T. Obermann,23 J. Ocariz,82
A. Ochi,69 I. Ochoa,37 J. P. Ochoa-Ricoux,34a S. Oda,72 S. Odaka,68 H. Ogren,63 A. Oh,86 S. H. Oh,47 C. C. Ohm,16
Ohman,165 H. Oide,32 H. Okawa,161 Y. Okumura,33 T. Okuyama,68 A. Olariu,28b L. F. Oleiro Seabra,127a
S. A. Olivares Pino,48 D. Oliveira Damazio,27 A. Olszewski,41 J. Olszowska,41 A. Onofre,127a127e K. Onogi,104
P. U. E. Onyisi,11,w M. J. Oreglia,33 Y. Oren,154 D. Orestano,135a,135b N. Orlando,62b R. S. Orr,159 B. Osculati,52a,52b
R. Ospanov,86 G. Otero y Garzon,29 H. Otono,72 M. Ouchrif,136d F. Ould-Saada,120 A. Ouraou,137 K. P. Oussoren,108
Q. Ouyang,35a M. Owen,55 R. E. Owen,19 V. E. Ozcan,20a N. Ozturk,8 K. Pachal,143 A. Pacheco Pages,13 C. Padilla Aranda,13
M. Pagäcovä,50 S. Pagan Griso,16 F. Paige,27 P. Pais,88 K. Pajchel,120 G. Palacino,160b S. Palestini,32 M. Palka,40b D. Pallin,36
Palma,127a127b E. St. Panagiotopoulou,10 C. E. Pandini,82 J. G. Panduro Vazquez,79 P. Pani,147a147b S. Panitkin,27
Pantea,28b L. Paolozzi,51 Th. D. Papadopoulou,10 K. Papageorgiou,155 A. Paramonov,6 D. Paredes Hernandez,176
A. J. Parker,74 M. A. Parker,30 K. A. Parker,140 F. Parodi,52a,52b J. A. Parsons,37 U. Parzefall,50 V. R. Pascuzzi,159
Pasqualucci,133a S. Passaggio,52a Fr. Pastore,79 G. Päsztor,31hh S. Pataraia,175 J. R. Pater,86 T. Pauly,32 J. Pearce,169
Pearson,114 L. E. Pedersen,38 M. Pedersen,120 S. Pedraza Lopez,167 R. Pedro,127a127b S. V. Peleganchuk,110 d D. Pelikan,165
O.	Penc,128 C. Peng,35a H. Peng,35b J. Penwell,63 B. S. Peralva,26b M. M. Perego,137 D. V. Perepelitsa,27 E. Perez Codina,160a
L. Perini,93a93b H. Pernegger,32 S. Perrella,105a105b R. Peschke,44 V. D. Peshekhonov,67 K. Peters,44 R. F. Y. Peters,86
A. Petersen,32 T. C. Petersen,38 E. Petit,57 A. Petridis,1 C. Petridou,155 P. Petroff,118 E. Petrolo,133a M. Petrov,121
Petrucci,135a135b N. E. Pettersson,88 A. Peyaud,137 R. Pezoa,34b P. W. Phillips,132 G. Piacquadio,144 E. Pianori,170
Picazio,88 E. Piccaro,78 M. Piccinini,22a,22b M. A. Pickering,121 R. Piegaia,29 J. E. Pilcher,33 A. D. Pilkington,86
W. J. Pin,86 M. Pinamonti,164a164cii J. L. Pinfold,3 A. Pingel,38 S. Pires,82 H. Pirumov,44 M. Pitt,172 L. Plazak,145a
M.-A. Pleier,27 V. Pleskot,85 E. Plotnikova,67 P. Plucinski,92 D. Pluth,66 R. Poettgen,147a147b L. Poggioli,118 D. Pohl,23
Polesello,122a A. Poley,44 A. Policicchio,39a,39b R. Polifka,159 A. Polini,22a C. S. Pollard,55 V. Polychronakos,27
K. Pommes,32 L. Pontecorvo,133a B. G. Pope,92 G. A. Popeneciu,28c D. S. Popovic,14 A. Poppleton,32 S. Pospisil,129
K. Potamianos,16 I. N. Potrap,67 C. J. Potter,30 C. T. Potter,117 G. Poulard,32 J. Poveda,32 V. Pozdnyakov,67
M. E. Pozo Astigarraga,32 P. Pralavorio,87 A. Pranko,16 S. Prell,66 D. Price,86 L. E. Price,6 M. Primavera,75a S. Prince,89
M. Proissl,48 K. Prokofiev,62c F. Prokoshin,34b S. Protopopescu,27 J. Proudfoot,6 M. Przybycien,40a D. Puddu,135a135b
D. Puldon,149 M. Purohit,27 jj P. Puzo,118 J. Qian,91 G. Qin,55 Y. Qin,86 A. Quadt,56 W. B. Quayle,164a164b
M. Queitsch-Maitland,86 D. Quilty,55 S. Raddum,120 V. Radeka,27 V. Radescu,60b S. K. Radhakrishnan,149 P. Radloff,117
P. Rados,90 F. Ragusa,93a 93b G. Rahal,178 J. A. Raine,86 S. Rajagopalan,27 M. Rammensee,32 C. Rangel-Smith,165
M. G. Ratti,93a93b F. Rauscher,101 S. Rave,85 T. Ravenscroft,55 I. Ravinovich,172 M. Raymond,32 A. L. Read,120
N. P. Readioff,76 M. Reale,75a75b D. M. Rebuzzi,122a122b A. Redelbach,174 G. Redlinger,27 R. Reece,138 K. Reeves,43
L. Rehnisch,17 J. Reichert,123 H. Reisin,29 C. Rembser,32 H. Ren,35a M. Rescigno,133a S. Resconi,93a O. L. Rezanova,110 d
P. Reznicek,130 R. Rezvani,96 R. Richter,102 S. Richter,80 E. Richter-Was,40b O. Ricken,23 M. Ridel,82 P. Rieck,17
J. Riegel,175 J. Rieger,56 O. Rifki,114 M. Rijssenbeek,149 A. Rimoldi,122a122b M. Rimoldi,18 L. Rinaldi,22a B. Ristic,51
Ritsch,32 I. Riu,13 F. Rizatdinova,115 E. Rizvi,78 C. Rizzi,13 S. H. Robertson,89,m A. Robichaud-Veronneau,89
D. Robinson,30 J. E. M. Robinson,44 A. Robson,55 C. Roda,125a,125b Y. Rodina,87 A. Rodriguez Perez,13
Rodriguez Rodriguez,167 S. Roe,32 C. S. Rogan,59 O. R0hne,120 A. Romaniouk,99 M. Romano,22a22b
S. M. Romano Saez,36 E. Romero Adam,167 N. Rompotis,139 M. Ronzani,50 L. Roos,82 E. Ros,167 S. Rosati,133a
K. Rosbach,50 P. Rose,138 O. Rosenthal,142 N.-A. Rosien,56 V. Rossetti,147a,147b E. Rossi,105a,105b L. P. Rossi,52a
032003-24

SEARCH FOR PAIR PRODUCTION OF GLUINOS
PHYSICAL REVIEW D 94, 032003 (2016)
J. H. N. Rosten,30 R. Rosten,139 M. Rotaru,28b I. Roth,172 J. Rothberg,139 D. Rousseau,118 C. R. Royon,137 A. Rozanov,87
Y. Rozen,153 X. Ruan,146c F. Rubbo,144 M. S. Rudolph,159 F. Rühr,50 A. Ruiz-Martinez,31 Z. Rurikova,50 N. A. Rusakovich,67
Ruschke,101 H. L. Russell,139 J. P. Rutherfoord,7 N. Ruthmann,32 Y. F. Ryabov,124 M. Rybar,166 G. Rybkin,118 S. Ryu,6
A. Ryzhov,131 G. F. Rzehorz,56 A. F. Saavedra,151 G. Sabato,108 S. Sacerdoti,29 H. F-W. Sadrozinski,138 R. Sadykov,67
1. Safai Tehrani,133a P. Saha,109 M. Sahinsoy,60a M. Saimpert,137 T. Saito,156 H. Sakamoto,156 Y. Sakurai,171
2. Salamanna,135a135b A. Salamon,134a134b J. E. Salazar Loyola,34b D. Salek,108 P. H. Sales De Bruin,139 D. Salihagic,102
Salnikov,144 J. Salt,167 D. Salvatore,39a’39b F. Salvatore,150 A. Salvucci,62a A. Salzburger,32 D. Sammel,50
D. Sampsonidis,155 A. Sanchez,105a105b J. Sánchez,167 V. Sanchez Martinez,167 H. Sandaker,120 R. L. Sandbach,78
G. Sander,85 M. Sandhoff,175 C. Sandoval,21 R. Sandstroem,102 D. P. C. Sankey,132 M. Sannino,52a 52b A. Sansoni,49
Santoni,36 R. Santonico,134a’134b H. Santos,127“ I. Santoyo Castillo,150 K. Sapp,126 A. Sapronov,67 J. G. Saraiva,127a’127d
Sarrazin,23 O. Sasaki,68 Y. Sasaki,156 K. Sato,161 G. Sauvage,5’a E. Sauvan,5 G. Savage,79 P. Savard,159’e C. Sawyer,132
L. Sawyer,81’r J. Saxon,33 C. Sbarra,22a A. Sbrizzi,22a’22b T. Scanlon,80 D. A. Scannicchio,163 M. Scarcella,151
V. Scarfone,39a39b J. Schaarschmidt,172 P. Schacht,102 B. M. Schachtner,101 D. Schaefer,32 R. Schaefer,44 J. Schaeffer,85
S. Schaepe,23 S. Schaetzel,60b U. Schäfer,85 A.C. Schaffer,118 D. Schaile,101 R. D. Schamberger,149 V. Scharf,60a
V. A. Schegelsky,124 D. Scheirich,130 M. Schernau,163 C. Schiavi,52a’52b S. Schier,138 C. Schillo,50 M. Schioppa,39a’39b
S. Schlenker,32 K. R. Schmidt-Sommerfeld,102 K. Schmieden,32 C. Schmitt,85 S. Schmitt,44 S. Schmitz,85 B. Schneider,160a
U. Schnoor,50 L. Schoeffel,137 A. Schoening,60b B. D. Schoenrock,92 E. Schopf,23 M. Schott,85 J. Schovancova,8
S. Schramm,51 M. Schreyer,174 N. Schuh,85 M. J. Schultens,23 H.-C. Schultz-Coulon,60a H. Schulz,17 M. Schumacher,50
A. Schumm,138 Ph. Schune,137 A. Schwartzman,144 T. A. Schwarz,91 Ph. Schwegler,102 H. Schweiger,86
Ph. Schwemling,137 R. Schwienhorst,92 J. Schwindling,137 T. Schwindt,23 G. Sciolla,25 F. Scuri,125a125b F. Scutti,90
J. Searcy,91 P. Seema,23 S. C. Seidel,106 A. Seiden,138 F. Seifert,129 J. M. Seixas,26a G. Sekhniaidze,105a K. Sekhon,91
S. J. Sekula,42 D. M. Seliverstov,124’a N. Semprini-Cesari,22a’22b C. Serfon,120 L. Serin,118 L. Serkin,164a’164b M. Sessa,135a’135b
R. Seuster,169 H. Severini,114 T. Sfiligoj,77 F. Sforza,32 A. Sfyrla,51 E. Shabalina,56 N. W. Shaikh,147a’147b L. Y. Shan,35a
R. Shang,166 J. T. Shank,24 M. Shapiro,16 P. B. Shatalov,98 K. Shaw,164a’164b S. M. Shaw,86 A. Shcherbakova,147a'147b
1. Y. Shehu,150 P. Sherwood,80 L. Shi,152,kk S. Shimizu,69 C. O. Shimmin,163 M. Shimojima,103 M. Shiyakova,67,ll
   A. Shmeleva,97 D. Shoaleh Saadi,96 M. J. Shochet,33 S. Shojaii,93a’93b S. Shrestha,112 E. Shulga,99 M. A. Shupe,7 P. Sicho,128
   A.M. Sickles,166 P.E. Sidebo,148 O. Sidiropoulou,174 D. Sidorov,115 A. Sidoti,22a22b F. Siegert,46 Dj. Sijacki,14
   J. Silva,127a127d S.B. Silverstein,147a V. Simak,129 O. Simard,5 Lj. Simic,14 S. Simion,118 E. Simioni,85 B. Simmons,80
2. Simon,36 M. Simon,85 P. Sinervo,159 N. B. Sinev,117 M. Sioli,22a’22b G. Siragusa,174 S. Yu. Sivoklokov,100 J. Sjölin,147a’147b
   T. B. Sjursen,15 M. B. Skinner,74 H. P. Skottowe,59 P. Skubic,114 M. Slater,19 T. Slavicek,129 M. Slawinska,108 K. Sliwa,162
R. Slovak,130 V. Smakhtin,172 B. H. Smart,5 L. Smestad,15 J. Smiesko,145a S. Yu. Smirnov,99 Y. Smirnov,99
L. N. Smirnova,100’™“ O. Smirnova,83 M. N. K. Smith,37 R. W. Smith,37 M. Smizanska,74 K. Smolek,129 A. A. Snesarev,97
S. Snyder,27 R. Sobie,169m F. Socher,46 A. Soffer,154 D. A. Soh,152 G. Sokhrannyi,77 C. A. Solans Sanchez,32 M. Solar,129
Yu. Soldatov,99 U. Soldevila,167 A. A. Solodkov,131 A. Soloshenko,67 O. V. Solovyanov,131 V. Solovyev,124 P. Sommer,50
Son,162 H. Y. Song,35b,nn A. Sood,16 A. Sopczak,129 V. Sopko,129 V. Sorin,13 D. Sosa,60b C. L. Sotiropoulou,125a,125b
R. Soualah,164a,164c A. M. Soukharev,110,d D. South,44 B. C. Sowden,79 S. Spagnolo,75a,75b M. Spalla,125a,125b
M. Spangenberg,170 F. Spano,79 D. Sperlich,17 F. Spettel,102 R. Spighi,22a G. Spigo,32 L. A. Spiller,90 M. Spousta,130
R. D. St. Denis,55 a A. Stabile,93a R. Stamen,60a S. Stamm,17 E. Stanecka,41 R. W. Stanek,6 C. Stanescu,135a
M. Stanescu-Bellu,44 M. M. Stanitzki,44 S. Stapnes,120 E. A. Starchenko,131 G. H. Stark,33 J. Stark,57 P. Staroba,128
P. Starovoitov,60a S. Stärz,32 R. Staszewski,41 P. Steinberg,27 B. Stelzer,143 H. J. Stelzer,32 O. Stelzer-Chilton,160a
Stenzel,54 G. A. Stewart,55 J. A. Stillings,23 M. C. Stockton,89 M. Stoebe,89 G. Stoicea,28b P. Stolte,56 S. Stonjek,102
R. Stradling,8 A. Straessner,46 M. E. Stramaglia,18 J. Strandberg,148 S. Strandberg,147a,147b A. Strandlie,120 M. Strauss,114
P. Strizenec,145b R. Ströhmer,174 D. M. Strom,117 R. Stroynowski,42 A. Strubig,107 S. A. Stucci,18 B. Stugu,15 N. A. Styles,44
Su,144 J. Su,126 R. Subramaniam,81 S. Suchek,60a Y. Sugaya,119 M. Suk,129 V. V. Sulin,97 S. Sultansoy,4c T. Sumida,70
S. Sun,59 X. Sun,35a J. E. Sundermann,50 K. Suruliz,150 G. Susinno,39a,39b M. R. Sutton,150 S. Suzuki,68 M. Svatos,128
M. Swiatlowski,33 I. Sykora,145a T. Sykora,130 D. Ta,50 C. Taccini,135a,135b K. Tackmann,44 J. Taenzer,159 A. Taffard,163
R. Tafirout,160a N. Taiblum,154 H. Takai,27 R. Takashima,71 T. Takeshita,141 Y. Takubo,68 M. Talby,87 A. A. Talyshev,110 d
K. G. Tan,90 J. Tanaka,156 R. Tanaka,118 S. Tanaka,68 B. B. Tannenwald,112 S. Tapia Araya,34b S. Tapprogge,85 S. Tarem,153
032003-25

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
F. Tartarelli,93a P. Tas,130 M. Tasevsky,128 T. Tashiro,70 E. Tassi,39a’39b A. Tavares Delgado,127a’127b Y. Tayalati,136d
A. C. Taylor,106 G. N. Taylor,90 P. T. E. Taylor,90 W. Taylor,160b F. A. Teischinger,32 P. Teixeira-Dias,79 K. K. Temming,50
Temple,143 H. Ten Kate,32 P. K. Teng,152 J. J. Teoh,119 F. Tepel,175 S. Terada,68 K. Terashi,156 J. Terron,84 S. Terzo,102
M. Testa,49 R. J. Teuscher,159m T. Theveneaux-Pelzer,87 J. P. Thomas,19 J. Thomas-Wilsker,79 E. N. Thompson,37
P. D. Thompson,19 A. S. Thompson,55 L. A. Thomsen,176 E. Thomson,123 M. Thomson,30 M. J. Tibbetts,16
R. E. Ticse Torres,87 V. O. Tikhomirov,97’°° Yu. A. Tikhonov,110,6 S. Timoshenko,99 P. Tipton,176 S. Tisserant,87
K. Todome,158 T. Todorov,5a S. Todorova-Nova,130 J. Tojo,72 S. Tokär,145a K. Tokushuku,68 E. Tolley,59 L. Tomlinson,86
M. Tomoto,104 L. Tompkins,144pp K. Toms,106 B. Tong,59 E. Torrence,117 H. Torres,143 E. Torro Pastor,139 J. Toth,87 qq
Touchard,87 D. R. Tovey,140 T. Trefzger,174 A. Tricoli,27 I. M. Trigger,160a S. Trincaz-Duvoid,82 M. F. Tripiana,13
W. Trischuk,159 B. Trocme,57 A. Trofymov,44 C. Troncon,93a M. Trottier-McDonald,16 M. Trovatelli,169 L. Truong,164a164c
M. Trzebinski,41 A. Trzupek,41 J. C-L. Tseng,121 P. V. Tsiareshka,94 G. Tsipolitis,10 N. Tsirintanis,9 S. Tsiskaridze,13
V. Tsiskaridze,50 E. G. Tskhadadze,53a K. M. Tsui,62a I. I. Tsukerman,98 V. Tsulaia,16 S. Tsuno,68 D. Tsybychev,149
A. Tudorache,28b V. Tudorache,28b A. N. Tuna,59 S. A. Tupputi,22a22b S. Turchikhin,100mm D. Turecek,129 D. Turgeman,172
R. Turra,93a’93b A. J. Turvey,42 P. M. Tuts,37 M. Tyndel,132 G. Ucchielli,22a’22b I. Ueda,156 R. Ueno,31 M. Ughetto,147a’147b
Ukegawa,161 G. Unal,32 A. Undrus,27 G. Unel,163 F. C. Ungaro,90 Y. Unno,68 C. Unverdorben,101 J. Urban,145b
P. Urquijo,90 P. Urrejola,85 G. Usai,8 A. Usanova,64 L. Vacavant,87 V. Vacek,129 B. Vachon,89 C. Valderanis,101
Valdes Santurio,147a'147b N. Valencic,108 S. Valentinetti,22a'22b A. Valero,167 L. Valery,13 S. Valkar,130 S. Vallecorsa,51
J. A. Valls Ferrer,167 W. Van Den Wollenberg,108 P. C. Van Der Deijl,108 R. van der Geer,108 H. van der Graaf,108
N. van Eldik,153 P. van Gemmeren,6 J. Van Nieuwkoop,143 I. van Vulpen,108 M. C. van Woerden,32 M. Vanadia,133a’133b
W. Vandelli,32 R. Vanguri,123 A. Vaniachine,6 P. Vankov,108 G. Vardanyan,177 R. Vari,133a E. W. Varnes,7 T. Varol,42
Varouchas,82 A. Vartapetian,8 K. E. Varvell,151 J. G. Vasquez,176 F. Vazeille,36 T. Vazquez Schroeder,89 J. Veatch,56
L. M. Veloce,159 F. Veloso,127a’127c S. Veneziano,133a A. Ventura,75a’75b M. Venturi,169 N. Venturi,159 A. Venturini,25
Vercesi,122a M. Verducci,133a’133b W. Verkerke,108 J. C. Vermeulen,108 A. Vest,46’11 M. C. Vetterli,143’e O. Viazlo,83
Vichou,166 T. Vickey,140 O. E. Vickey Boeriu,140 G. H. A. Viehhauser,121 S. Viel,16 L. Vigani,121 R. Vigne,64 M. Villa,22a22b
M. Villaplana Perez,93a,93b E. Vilucchi,49 M. G. Vincter,31 V. B. Vinogradov,67 C. Vittori,22a,22b I. Vivarelli,150 S. Vlachos,10
M. Vlasak,129 M. Vogel,175 P. Vokac,129 G. Volpi,125a’125b M. Volpi,90 H. von der Schmitt,102 E. von Toerne,23 V. Vorobel,130
K. Vorobev,99 M. Vos,167 R. Voss,32 J. H. Vossebeld,76 N. Vranjes,14 M. Vranjes Milosavljevic,14 V. Vrba,128
M. Vreeswijk,108 R. Vuillermet,32 I. Vukotic,33 Z. Vykydal,129 P. Wagner,23 W. Wagner,175 H. Wahlberg,73 S. Wahrmund,46
J. Wakabayashi,104 J. Walder,74 R. Walker,101 W. Walkowiak,142 V. Wallangen,147a,147b C. Wang,35c C. Wang,356,87
Wang,173 H. Wang,16 H. Wang,42 J. Wang,44 J. Wang,151 K. Wang,89 R. Wang,6 S. M. Wang,152 T. Wang,23 T. Wang,37
X. Wang,176 C. Wanotayaroj,117 A. Warburton,89 C. P. Ward,30 D. R. Wardrope,80 A. Washbrook,48 P. M. Watkins,19
A. T. Watson,19 M. F. Watson,19 G. Watts,139 S. Watts,86 B. M. Waugh,80 S. Webb,85 M. S. Weber,18 S. W. Weber,174
J. S. Webster,6 A. R. Weidberg,121 B. Weinert,63 J. Weingarten,56 C. Weiser,50 H. Weits,108 P. S. Wells,32 T. Wenaus,27
T. Wengler,32 S. Wenig,32 N. Wermes,23 M. Werner,50 P. Werner,32 M. Wessels,60a J. Wetter,162 K. Whalen,117
N. L. Whallon,139 A. M. Wharton,74 A. White,8 M. J. White,1 R. White,34b D. Whiteson,163 F. J. Wickens,132
W. Wiedenmann,173 M. Wielers,132 P. Wienemann,23 C. Wiglesworth,38 L. A. M. Wiik-Fuchs,23 A. Wildauer,102 F. Wilk,86
G. Wilkens,32 H. H. Williams,123 S. Williams,108 C. Willis,92 S. Willocq,88 J. A. Wilson,19 I. Wingerter-Seez,5
Winklmeier,117 O. J. Winston,150 B.T. Winter,23 M. Wittgen,144 J. Wittkowski,101 S. J. Wollstadt,85 M. W. Wolter,41
Wolters,127a,127c B. K. Wosiek,41 J. Wotschack,32 M. J. Woudstra,86 K. W. Wozniak,41 M. Wu,57 M. Wu,33 S. L. Wu,173
X. Wu,51 Y. Wu,91 T. R. Wyatt,86 B. M. Wynne,48 S. Xella,38 D. Xu,35a L. Xu,27 B. Yabsley,151 S. Yacoob,146a R. Yakabe,69
Yamaguchi,158 Y. Yamaguchi,119 A. Yamamoto,68 S. Yamamoto,156 T. Yamanaka,156 K. Yamauchi,104 Y. Yamazaki,69
Z. Yan,24 H. Yang,35e H. Yang,173 Y. Yang,152 Z. Yang,15 W-M. Yao,16 Y. C. Yap,82 Y. Yasu,68 E. Yatsenko,5
K. H. Yau Wong,23 J. Ye,42 S. Ye,271. Yeletskikh,67 A. L. Yen,59 E. Yildirim,85 K. Yorita,171 R. Yoshida,6 K. Yoshihara,123
Young,144 C. J. S. Young,32 S. Youssef,24 D. R. Yu,16 J. Yu,8 J. M. Yu,91 J. Yu,66 L. Yuan,69 S. P. Y. Yuen,231. Yusuff,30,ss
Zabinski,41 R. Zaidan,35d A. M. Zaitsev,131ff N. Zakharchuk,44 J. Zalieckas,15 A. Zaman,149 S. Zambito,59
L. Zanello,133a133b D. Zanzi,90 C. Zeitnitz,175 M. Zeman,129 A. Zemla,40a J. C. Zeng,166 Q. Zeng,144 K. Zengel,25 O. Zenin,131
T. Zenis,145a D. Zerwas,118 D. Zhang,91 F. Zhang,173 G. Zhang,35bnn H. Zhang,35c J. Zhang,6 L. Zhang,50 R. Zhang,23
R. Zhang,35b,tt X. Zhang,35d Z. Zhang,118 X. Zhao,42 Y. Zhao,35d Z. Zhao,35b A. Zhemchugov,67 J. Zhong,121 B. Zhou,91
032003-26

SEARCH FOR PAIR PRODUCTION OF GLUINOS ...	PHYSICAL	REVIEW	D	94,	032003 (2016)
Zhou,47 L. Zhou,37 L. Zhou,42 M. Zhou,149 N. Zhou,35f C. G. Zhu,35d H. Zhu,35a J. Zhu,91 Y. Zhu,35b X. Zhuang,35a
K. Zhukov,97 A. Zibell,174 D. Zieminska,63 N. I. Zimine,67 C. Zimmermann,85 S. Zimmermann,50 Z. Zinonos,56 M. Zinser,85
M. Ziolkowski,142 L. Zivkovic,14 G. Zobernig,173 A. Zoccoli,22a’22b M. zur Nedden,17 G. Zurzolo,105a’105b and L. Zwalinski32
(ATLAS Collaboration)
1 Department of Physics, University of Adelaide, Adelaide, Australia
2Physics Department, SUNY Albany, Albany, New York, USA
3Department of Physics, University of Alberta, Edmonton, Alberta, Canada
4aDepartment of Physics, Ankara University, Ankara, Turkey
4bIstanbul Aydin University, Istanbul, Turkey
4cDivision of Physics, TOBB University of Economics and Technology, Ankara, Turkey
5LAPP, CNRS/IN2P3 and Université Savoie Mont Blanc, Annecy-le-Vieux, France
6High Energy Physics Division, Argonne National Laboratory, Argonne, Illinois, USA
1 Department of Physics, University of Arizona, Tucson, Arizona, USA
8Department of Physics, The University of Texas at Arlington, Arlington, Texas, USA
9Physics Department, University of Athens, Athens, Greece
10Physics Department, National Technical University of Athens, Zografou, Greece
11 Department of Physics, The University of Texas at Austin, Austin, Texas, USA
12Institute of Physics, Azerbaijan Academy of Sciences, Baku, Azerbaijan
13Institut de Física d’Altes Energies (IFAE), The Barcelona Institute of Science and Technology,
Barcelona, Spain, Spain
14Institute of Physics, University of Belgrade, Belgrade, Serbia
15Department for Physics and Technology, University of Bergen, Bergen, Norway
16Physics Division, Lawrence Berkeley National Laboratory and University of California, Berkeley,
California, USA
11Department of Physics, Humboldt University, Berlin, Germany
18Albert Einstein Center for Fundamental Physics and Laboratory for High Energy Physics,
University of Bern, Bern, Switzerland
19School of Physics and Astronomy, University of Birmingham, Birmingham, United Kingdom
20aDepartment of Physics, Bogazici University, Istanbul, Turkey
20bDepartment of Physics Engineering, Gaziantep University, Gaziantep, Turkey
20dIstanbul Bilgi University, Faculty of Engineering and Natural Sciences, Istanbul, Turkey, Turkey
20eBahcesehir University, Faculty of Engineering and Natural Sciences, Istanbul, Turkey, Turkey
21Centro de Investigaciones, Universidad Antonio Narino, Bogota, Colombia
22aINFN Sezione di Bologna, Italy
22bDipartimento di Fisica e Astronomia, Università di Bologna, Bologna, Italy
23Physikalisches Institut, University of Bonn, Bonn, Germany
24Department of Physics, Boston University, Boston, Massachusetts, USA
25
Department of Physics, Brandeis University, Waltham, Massachusetts, USA
26aUniversidade Federal do Rio De Janeiro COPPE/EE/IF, Rio de Janeiro, Brazil
26bElectrical Circuits Department, Federal University of Juiz de Fora (UFJF), Juiz de Fora, Brazil
26cFederal University of Sao Joao del Rei (UFSJ), Sao Joao del Rei, Brazil
26dInstituto de Fisica, Universidade de Sao Paulo, Sao Paulo, Brazil
21Physics Department, Brookhaven National Laboratory, Upton, New York, USA
28aTransilvania University of Brasov, Brasov, Romania, Romania
28bNational Institute of Physics and Nuclear Engineering, Bucharest, Romania
28cNational Institute for Research and Development of Isotopic and Molecular Technologies,
Physics Department, Cluj Napoca, Romania
28dUniversity Politehnica Bucharest, Bucharest, Romania
28eWest University in Timisoara, Timisoara, Romania
29Departamento de Física, Universidad de Buenos Aires, Buenos Aires, Argentina
30Cavendish Laboratory, University of Cambridge, Cambridge, United Kingdom
31 Department of Physics, Carleton University, Ottawa, Ontario, Canada
32CERN, Geneva, Switzerland
33Enrico Fermi Institute, University of Chicago, Chicago, Illinois, USA
34aDepartamento de Física, Pontificia Universidad Católica de Chile, Santiago, Chile
34bDepartamento de Física, Universidad Técnica Federico Santa María, Valparaíso, Chile
032003-27

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
35aInstitute of High Energy Physics, Chinese Academy of Sciences, Beijing, China
35bDepartment of Modern Physics, University of Science and Technology of China, Anhui, China
35cDepartment of Physics, Nanjing University, Jiangsu, China
35dSchool of Physics, Shandong University, Shandong, China
35eDepartment of Physics and Astronomy, Shanghai Key Laboratory for Particle Physics and Cosmology,
Shanghai Jiao Tong University, Shanghai; (also affiliated with PKU-CHEP), China
35f
Physics Department, Tsinghua University, Beijing 100084, China
36Laboratoire de Physique Corpusculaire, Clermont Université and Université Blaise Pascal and
CNRS/IN2P3, Clermont-Ferrand, France
37Nevis Laboratory, Columbia University, Irvington, New York, USA
38Niels Bohr Institute, University of Copenhagen, Kobenhavn, Denmark
39aINFN Gruppo Collegato di Cosenza, Laboratori Nazionali di Frascati, Italy
39b Dipartimento di Fisica, Università della Calabria, Rende, Italy
40aAGH University of Science and Technology, Faculty of Physics and Applied Computer Science,
Krakow, Poland
40bMarian Smoluchowski Institute of Physics, Jagiellonian University, Krakow, Poland
41Institute of Nuclear Physics Polish Academy of Sciences, Krakow, Poland
42Physics Department, Southern Methodist University, Dallas, Texas, USA
43Physics Department, University of Texas at Dallas, Richardson, Texas, USA
44DESY, Hamburg and Zeuthen, Germany
45Institut für Experimentelle Physik IV, Technische Universität Dortmund, Dortmund, Germany
46Institut für Kern- und Teilchenphysik, Technische Universität Dresden, Dresden, Germany
47Department of Physics, Duke University, Durham, North Carolina, USA
48SUPA - School of Physics and Astronomy, University of Edinburgh, Edinburgh, United Kingdom
49INFN Laboratori Nazionali di Frascati, Frascati, Italy
50Fakultät für Mathematik und Physik, Albert-Ludwigs-Universität, Freiburg, Germany
51Section de Physique, Université de Genève, Geneva, Switzerland
52aINFN Sezione di Genova, Italy
52bDipartimento di Fisica, Università di Genova, Genova, Italy
53aE. Andronikashvili Institute of Physics, Iv. Javakhishvili Tbilisi State University, Tbilisi, Georgia
53bHigh Energy Physics Institute, Tbilisi State University, Tbilisi, Georgia
54II Physikalisches Institut, Justus-Liebig-Universität Giessen, Giessen, Germany
55SUPA - School of Physics and Astronomy, University of Glasgow, Glasgow, United Kingdom
56II Physikalisches Institut, Georg-August-Universität, Göttingen, Germany
57
Laboratoire de Physique Subatomique et de Cosmologie, Université Grenoble-Alpes, CNRS/IN2P3,
Grenoble, France
58
Department of Physics, Hampton University, Hampton, Virginia, USA
59Laboratory for Particle Physics and Cosmology, Harvard University, Cambridge, Massachusetts, USA
60aKirchhoff-Institut für Physik, Ruprecht-Karls-Universität Heidelberg, Heidelberg, Germany
60bPhysikalisches Institut, Ruprecht-Karls-Universität Heidelberg, Heidelberg, Germany
60cZITI Institut für technische Informatik, Ruprecht-Karls-Universität Heidelberg, Mannheim, Germany
61Faculty of Applied Information Science, Hiroshima Institute of Technology, Hiroshima, Japan
62aDepartment of Physics, The Chinese University of Hong Kong, Shatin, N.T., Hong Kong, China
62bDepartment of Physics, The University of Hong Kong, Hong Kong, China
62cDepartment of Physics, The Hong Kong University of Science and Technology, Clear Water Bay,
Kowloon, Hong Kong, China
63Department of Physics, Indiana University, Bloomington, Indiana, USA
^Institut für Astro- und Teilchenphysik, Leopold-Franzens-Universität, Innsbruck, Austria
65University of Iowa, Iowa City, Iowa, USA
66Department of Physics and Astronomy, Iowa State University, Ames, Iowa, USA
67Joint Institute for Nuclear Research, JINR Dubna, Dubna, Russia
68KEK, High Energy Accelerator Research Organization, Tsukuba, Japan
69Graduate School of Science, Kobe University, Kobe, Japan
10Faculty of Science, Kyoto University, Kyoto, Japan
71Kyoto University of Education, Kyoto, Japan
72Department of Physics, Kyushu University, Fukuoka, Japan
73Instituto de Física La Plata, Universidad Nacional de La Plata and CONICET, La Plata, Argentina
14Physics Department, Lancaster University, Lancaster, United Kingdom
75aINFN Sezione di Lecce, Italy
75bDipartimento di Matematica e Fisica, Università del Salento, Lecce, Italy
032003-28

SEARCH FOR PAIR PRODUCTION OF GLUINOS
PHYSICAL REVIEW D 94, 032003 (2016)
16Oliver Lodge Laboratory, University of Liverpool, Liverpool, United Kingdom
11 Department of Physics, Jozef Stefan Institute and University of Ljubljana, Ljubljana, Slovenia
18School of Physics and Astronomy, Queen Mary University of London, London, United Kingdom
19Department of Physics, Royal Holloway University of London, Surrey, United Kingdom
80Department of Physics and Astronomy, University College London, London, United Kingdom
81Louisiana Tech University, Ruston, Louisiana, USA
82Laboratoire de Physique Nucléaire et de Hautes Energies, UPMC and Université Paris-Diderot and
CNRS/IN2P3, Paris, France
83Fysiska institutionen, Lunds universitet, Lund, Sweden
84Departamento de Fisica Teorica C-15, Universidad Autonoma de Madrid, Madrid, Spain
85
Institut für Physik, Universität Mainz, Mainz, Germany
86School of Physics and Astronomy, University of Manchester, Manchester, United Kingdom
81CPPM, Aix-Marseille Université and CNRS/IN2P3, Marseille, France
88Department of Physics, University of Massachusetts, Amherst, Massachusetts, USA
89Department of Physics, McGill University, Montreal, Québec, Canada
90School of Physics, University of Melbourne, Victoria, Australia
91 Department of Physics, The University of Michigan, Ann Arbor, Michigan, USA
92Department of Physics and Astronomy, Michigan State University, East Lansing, Michigan, USA
93aINFN Sezione di Milano, Italy
93b'Dipartimento di Fisica, Universita di Milano, Milano, Italy
94B.I. Stepanov Institute of Physics, National Academy of Sciences of Belarus, Minsk, Republic of Belarus
95National Scientific and Educational Centre for Particle and High Energy Physics,
Minsk, Republic of Belarus
96Group of Particle Physics, University of Montreal, Montreal, Québec, Canada
91P.N. Lebedev Physical Institute of the Russian Academy of Sciences, Moscow, Russia
98Institute for Theoretical and Experimental Physics (ITEP), Moscow, Russia
99National Research Nuclear University MEPhI, Moscow, Russia
100D.V. Skobeltsyn Institute of Nuclear Physics, M.V. Lomonosov Moscow State University,
Moscow, Russia
101 Fakultät für Physik, Ludwig-Maximilians-Universität München, München, Germany
102Max-Planck-Institut für Physik (Werner-Heisenberg-Institut), München, Germany
103Nagasaki Institute of Applied Science, Nagasaki, Japan
104Graduate School of Science and Kobayashi-Maskawa Institute, Nagoya University, Nagoya, Japan
105aINFN Sezione di Napoli, Italy
105bDipartimento di Fisica, Universita di Napoli, Napoli, Italy
106Department of Physics and Astronomy, University of New Mexico, Albuquerque, New Mexico, USA
101Institute for Mathematics, Astrophysics and Particle Physics, Radboud University Nijmegen/Nikhef
Nijmegen, Netherlands
108Nikhef National Institute for Subatomic Physics and University ofAmsterdam, Amsterdam, Netherlands
109Department of Physics, Northern Illinois University, DeKalb, Illinois, USA
110Budker Institute of Nuclear Physics, SB RAS, Novosibirsk, Russia
111 Department of Physics, New York University, New York, New York, USA
112Ohio State University, Columbus, Ohio, USA
113Faculty of Science, Okayama University, Okayama, Japan
114Homer L. Dodge Department of Physics and Astronomy, University of Oklahoma,
Norman, Oklahoma, USA
115Department of Physics, Oklahoma State University, Stillwater, Oklahoma, USA
116Palacky University, RCPTM, Olomouc, Czech Republic
111Center for High Energy Physics, University of Oregon, Eugene, Oregon, USA
118LAL, Univ. Paris-Sud, CNRS/IN2P3, Université Paris-Saclay, Orsay, France
119Graduate School of Science, Osaka University, Osaka, Japan
120Department of Physics, University of Oslo, Oslo, Norway
121Department of Physics, Oxford University, Oxford, United Kingdom
122aINFN Sezione di Pavia, Italy
122bDipartimento di Fisica, Universita di Pavia, Pavia, Italy
123Department of Physics, University of Pennsylvania, Philadelphia, Pennsylvania, USA
124National Research Centre “Kurchatov Institute” B.P.Konstantinov Petersburg Nuclear Physics
Institute, St. Petersburg, Russia
125aINFN Sezione di Pisa, Italy
125bDipartimento di Fisica E. Fermi, Universita di Pisa, Pisa, Italy
032003-29

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
126Department of Physics and Astronomy, University of Pittsburgh, Pittsburgh, Pennsylvania, USA
121aLaboratârio de Instrumentaçâo e Física Experimental de Partículas - LIP, Lisboa, Portugal
127bFaculdade de Ciencias, Universidade de Lisboa, Lisboa, Portugal
nlcDepartment of Physics, University of Coimbra, Coimbra, Portugal
121dCentro de Física Nuclear da Universidade de Lisboa, Lisboa, Portugal
127eDepartamento de Fisica, Universidade do Minho, Braga, Portugal
121tDepartamento de Fisica Teorica y del Cosmos and CAFPE, Universidad de Granada, Granada, Spain
127gDep Fisica and CEFITEC of Faculdade de Ciencias e Tecnologia, Universidade Nova de Lisboa,
Caparica, Portugal
128Institute of Physics, Academy of Sciences of the Czech Republic, Praha, Czech Republic
129Czech Technical University in Prague, Praha, Czech Republic
130Faculty of Mathematics and Physics, Charles University in Prague, Praha, Czech Republic
131State Research Center Institute for High Energy Physics (Protvino), NRC KI, Russia
132Particle Physics Department, Rutherford Appleton Laboratory, Didcot, United Kingdom
133aINFN Sezione di Roma, Italy
133bDipartimento di Fisica, Sapienza Università di Roma, Roma, Italy
134aINFN Sezione di Roma Tor Vergata, Italy
134b'Dipartimento di Fisica, Università di Roma Tor Vergata, Roma, Italy
135aINFN Sezione di Roma Tre, Italy
135bDipartimento di Matematica e Fisica, Università Roma Tre, Roma, Italy
136aFaculté des Sciences Ain Chock, Réseau Universitaire de Physique des Hautes Energies - Université
Hassan II, Casablanca, Morocco
136bCentre National de l’Energie des Sciences Techniques Nucleaires, Rabat, Morocco
136cFaculté des Sciences Semlalia, Université Cadi Ayyad, LPHEA-Marrakech, Morocco
136dFaculté des Sciences, Université Mohamed Premier and LPTPM, Oujda, Morocco
136eFaculté des sciences, Université Mohammed V, Rabat, Morocco
137DSM/IRFU (Institut de Recherches sur les Lois Fondamentales de l’Univers), CEA Saclay
(Commissariat à l’Energie Atomique et aux Energies Alternatives), Gif-sur-Yvette, France
138Santa Cruz Institute for Particle Physics, University of California Santa Cruz,
Santa Cruz, California, USA
139Department of Physics, University of Washington, Seattle, Washington, USA
140Department of Physics and Astronomy, University of Sheffield, Sheffield, United Kingdom
141 Department of Physics, Shinshu University, Nagano, Japan
142Fachbereich Physik, Universität Siegen, Siegen, Germany
143Department of Physics, Simon Fraser University, Burnaby, British Columbia, Canada
144SLAC National Accelerator Laboratory, Stanford, California, USA
145aFaculty of Mathematics, Physics & Informatics, Comenius University, Bratislava, Slovak Republic
145bDepartment of Subnuclear Physics, Institute of Experimental Physics of the Slovak Academy of
Sciences, Kosice, Slovak Republic
146aDepartment of Physics, University of Cape Town, Cape Town, South Africa
146bDepartment of Physics, University of Johannesburg, Johannesburg, South Africa
146cSchool of Physics, University of the Witwatersrand, Johannesburg, South Africa
147aDepartment of Physics, Stockholm University, Sweden
147bThe Oskar Klein Centre, Stockholm, Sweden
148Physics Department, Royal Institute of Technology, Stockholm, Sweden
149Departments of Physics & Astronomy and Chemistry, Stony Brook University,
Stony Brook, New York, USA
150Department of Physics and Astronomy, University of Sussex, Brighton, United Kingdom
151School of Physics, University of Sydney, Sydney, Australia
152Institute of Physics, Academia Sinica, Taipei, Taiwan
153Department of Physics, Technion: Israel Institute of Technology, Haifa, Israel
154Raymond and Beverly Sackler School of Physics and Astronomy, Tel Aviv University, Tel Aviv, Israel
155Department of Physics, Aristotle University of Thessaloniki, Thessaloniki, Greece
156International Center for Elementary Particle Physics and Department of Physics,
The University of Tokyo, Tokyo, Japan
157Graduate School of Science and Technology, Tokyo Metropolitan University, Tokyo, Japan
158Department of Physics, Tokyo Institute of Technology, Tokyo, Japan
159Department of Physics, University of Toronto, Toronto, Ontario, Canada
160aTRIUMF, Vancouver, British Columbia, Canada
160bDepartment of Physics and Astronomy, York University, Toronto, Ontario, Canada
032003-30

SEARCH FOR PAIR PRODUCTION OF GLUINOS
PHYSICAL REVIEW D 94, 032003 (2016)
161 Faculty of Pure and Applied Sciences, and Center for Integrated Research in Fundamental Science and
Engineering, University of Tsukuba, Tsukuba, Japan
162Department of Physics and Astronomy, Tufts University, Medford, Massachusetts, USA
163Department of Physics and Astronomy, University of California Irvine, Irvine, California, USA
164aINFN Gruppo Collegato di Udine, Sezione di Trieste, Udine, Italy
164bICTP, Trieste, Italy
164cDipartimento di Chimica, Fisica e Ambiente, Universita di Udine, Udine, Italy
165'Department of Physics and Astronomy, University of Uppsala, Uppsala, Sweden
166Department of Physics, University of Illinois, Urbana, Illinois, USA
161 Instituto de Fisica Corpuscular (IFIC) and Departamento de Fisica Atomica, Molecular y Nuclear and
Departamento de Ingeniería Electrónica and Instituto de Microelectrónica de Barcelona (IMB-CNM),
University of Valencia and CSIC, Valencia, Spain
168Department of Physics, University of British Columbia, Vancouver, British Columbia, Canada
169Department of Physics and Astronomy, University of Victoria, Victoria, British Columbia, Canada
110Department of Physics, University of Warwick, Coventry, United Kingdom
111Waseda University, Tokyo, Japan
112Department of Particle Physics, The Weizmann Institute of Science, Rehovot, Israel
173Department of Physics, University of Wisconsin, Madison, Wisconsin, USA
174Fakultätfür Physik und Astronomie, Julius-Maximilians-Universität, Würzburg, Germany
Fakultät für Mathematik und Naturwissenschaften, Fachgruppe Physik,
Bergische Universität Wuppertal, Wuppertal, Germany
116Department of Physics, Yale University, New Haven, Connecticut, USA
177Yerevan Physics Institute, Yerevan, Armenia
178Centre de Calcul de l’Institut National de Physique Nucléaire et de Physique des Particules (IN2P3),
Villeurbanne, France
aDeceased.
bAlso at Department of Physics, King’s College London, London, United Kingdom.
cAlso at Institute of Physics, Azerbaijan Academy of Sciences, Baku, Azerbaijan.
dAlso at Novosibirsk State University, Novosibirsk, Russia.
eAlso at TRIUMF, Vancouver BC, Canada.
fAlso at Department of Physics & Astronomy, University of Louisville, Louisville, KY, USA.
gAlso at Department	of	Physics,	California State University, Fresno CA, USA.
hAlso at Department	of	Physics,	University of Fribourg, Fribourg, Switzerland.
'Also at Departament de Fisica de la Universitat Autonoma de Barcelona, Barcelona, Spain.
jAlso at Departamento de Fisica e Astronomia, Faculdade de Ciencias, Universidade do Porto, Portugal.
kAlso at Tomsk State University, Tomsk, Russia.
l Also at Universita di Napoli Parthenope, Napoli, Italy.
mAlso at Institute of Particle Physics (IPP), Canada.
nAlso at National Institute of Physics and Nuclear Engineering, Bucharest, Romania.
oAlso at Department	of	Physics,	St. Petersburg State Polytechnical University, St.	Petersburg, Russia.
pAlso at Department	of	Physics,	The University of Michigan, Ann Arbor MI, USA.
qAlso at Centre for High Performance Computing, CSIR Campus, Rosebank, Cape Town, South Africa.
rAlso at Louisiana Tech University, Ruston LA, USA.
sAlso at Institucio Catalana de Recerca i Estudis Avancats, ICREA, Barcelona, Spain.
tAlso at Graduate School of Science, Osaka University, Osaka, Japan.
uAlso at Department of Physics, National Tsing Hua University, Taiwan.
vAlso at Institute for Mathematics, Astrophysics and Particle Physics, Radboud University Nijmegen/Nikhef, Nijmegen,
Netherlands.
wAlso at Department of Physics, The University of Texas at Austin, Austin TX, USA.
xAlso at Institute of Theoretical Physics, Ilia State University, Tbilisi, Georgia.
yAlso at CERN, Geneva, Switzerland.
zAlso at Georgian Technical University (GTU),Tbilisi, Georgia.
aaAlso at Ochadai Academic Production, Ochanomizu University, Tokyo, Japan.
bbAlso at Manhattan College, New York NY, USA.
cc Also at Hellenic Open University, Patras, Greece.
ddAlso at Academia Sinica Grid Computing, Institute of Physics, Academia Sinica, Taipei, Taiwan.
eeAlso at School of Physics, Shandong University, Shandong, China.
ffAlso at Moscow Institute of Physics and Technology State University, Dolgoprudny, Russia.
ggAlso at Section de Physique, Université de Genève, Geneva, Switzerland.
032003-31

G. AAD et al.
PHYSICAL REVIEW D 94, 032003 (2016)
hhAlso at Eotvos Lorand University, Budapest, Hungary.
“Also at International School for Advanced Studies (SISSA), Trieste, Italy.
JJAlso at Department of Physics and Astronomy, University of South Carolina, Columbia SC, USA.
^Also at School of Physics and Engineering, Sun Yat-sen University, Guangzhou, China.
llAlso at Institute for Nuclear Research and Nuclear Energy (INRNE) of the Bulgarian Academy of Sciences, Sofia, Bulgaria.
mmAlso at Faculty of Physics, M.V.Lomonosov Moscow State University, Moscow, Russia.
mAlso at Institute of Physics, Academia Sinica, Taipei, Taiwan.
ooAlso at National Research Nuclear University MEPhI, Moscow, Russia.
ppAlso at Department of Physics, Stanford University, Stanford CA, USA.
qqAlso at Institute for Particle and Nuclear Physics, Wigner Research Centre for Physics, Budapest, Hungary.
r Also at Flensburg University of Applied Sciences, Flensburg, Germany.
ssAlso at University of Malaya, Department of Physics, Kuala Lumpur, Malaysia.
“Also at CPPM, Aix-Marseille Université and CNRS/IN2P3, Marseille, France.
032003-32