THE INFLUENCE OF SELECTED FIRE-FIGHTING
SUBSTANCES ON THE DETECTION AND
IDENTIFICATION OF TRACES OF FLAMMABLE LIQUIDS
IN FIRE DEBRIS SAMPLES
Rafal BORUSIEWICZ
The Faculty of Chemistry, Jagiellonian University, Cracow
ABSTRACT: A series of experiments was carried out in order to study whether vari-
ous fire-fighting substances influenced the detection of traces of accelerants in sam-
ples taken from a fire scene. The experiments consisted in the following: piles made
up of typical flat furnishing materials were set on fire by means of a specific flamma-
ble liquid and then extinguished by a defined fire-fighting agent. Samples recovered
from the fire scene were then subjected to chromatographic analysis. The obtained
results suggest that the application of extinguishing foam is linked to the introduc-
tion of substances into the samples which might be detected in the process of analy-
sis. The presence of these compounds does not hinder the identification of the
accelerant, provided the person conducting the analysis knows how to interpret the
obtained results correctly.
KEY WORDS: Fire debris; Accelerants; Chromatography; Passive adsorption.
Problems of Forensic Sciences, vol. LII, 2002, 100-107
Received 13 November 2002; accepted 20 December 2002
INTRODUCTION
After a fire has been extinguished, the fire scene is subjected to careful
analysis, and in cases where arson is suspected, samples for laboratory anal-
ysis are recovered from the place that is considered to be the probable source
of the fire. Usually, such examinations are limited to a search for traces of
flammable liquids which are commonly used as accelerants [6]. Although
the problem of analysis of fire debris is not a new issue [1], the detection and
identification of flammable liquids still remains a challenge. Difficulties
arise because there are many different commercially available agents that
can be used to light fires, most of which are multi-component mixtures. In
the course of a fire, compounds contained in those mixtures evaporate to
a different extent, and some of them undergo thermal decomposition [3, 5, 6, 7].
Burnt materials may also undergo pyrolysis, which results in the presence of
numerous interferents in the sample, making analysis more difficult. An ad-

The influence of selected fire-fighting
101
ditional factor that may influence the effectiveness of detection of
accelerants is the use of various fire-fighting agents, and thus introduction
of additional substances to the analysed material [4]. The aim of the pre-
sented research was to determine the influence of fire-fighting agents on the
possibility of detection and identification of potential accelerants.
EXPERIMENTAL
# Apparatus
Equipment by Perkin Elmer was used in the research:
- an Auto System XL gas chromatograph coupled with a Turbo Mass
  Gold mass spectrometer and equipped with an Elite 1 capillary column
  with an inner diameter of 0.25 mm, film of the stationary phase of 1|tm
  thickness, and a length of 30 metres;
- automated thermal desorber - ATD Turbo Matrix with a module en-
  abling focusing of analytes on a “cold trap” and a set of suitable pipes
  made of stainless steel, containing a Tenax TA (poly-oxide 2.6 diphe-
  nylo- -phenylene).
Helium was used as a carrier gas, regulating its pressure in order to
achieve the following flow values: the flow of carrier gas during thermo-
desorption - 30 cm3/min, the flow of gas diluting the carrier gas after
thermodesorption from the cold trap (outlet split) - 30 cm3/min, the flow of
gas diluting the carrier gas after thermodesorption from the adsorbent (inlet
split) - 7.8 cm3/min. The temperature of the transfer line was 250oC, and the
temperature of the detector was 300oC.
The chromatographic analysis was conducted according to the following
temperature programme: initial temperature: 30oC maintained for three
minutes; increase 5oC/min to 120oC, increase 15oC/min to 270oC; final tem-
perature: 270oC maintained for 7.5 min.
# Materials and methods
During the research, a universal solvent made by Dragon (accelerants
class 3 according to ASTM) and diesel oil (class 5 according to ASTM) from
the local petrol station were used as accelerants. Piles were set on fire, con-
sisting of typical materials used for flat furnishings, including wood, var-
nished wood, chipboard, plastics (polystyrene, polyethylene, polypropy-
lene), carpet, and PVC linoleum. The content of the burnt piles was the
same. The conditions of burning were also the same. The piles were extin-
guished when the fire started going out by itself. The influence of the most
frequently used fire extinguishing agents was studied: extinguishing foam

102
R. Borusiewicz
obtained by the application of Deteor foam agent, a powder extinguisher and
a snow extinguisher. Reference samples were obtained by taking material
from piles where the fire was extinguished by cutting off the supply of oxy-
gen. In order to assess the influence of a given fire extinguishing agent, two
piles were set on fire: one by means of a solvent and the other by means of
diesel oil, and were extinguished by a specific fire extinguishing agent. After
the fire was extinguished, 3 samples were collected from each pile, and
placed into appropriate, clean, airtight jars. Information about the influence
of a given fire-fighting agent in relation to a specific accelerant could thus be
gained from analysis of the three samples. The samples were analysed in ac-
cordance with a previously established and routinely used procedure, which
involves concentrating analytes that are passing into the head-space, by
passive adsorption on the Tenax TA [5].
The procedure is as follows: steel pipes containing the adsorbent are in-
serted into jars containing the samples; the jars are tightly closed and
thermostated for 16 hours at a temperature of 60oC. After cooling off, the
pipes are placed on the thermodesorber, in which the adsorbent is subjected
to a temperature of 325oC. The analytes, released by thermo-desorption,
pass to the chromatographic column, where they are separated and, as sepa-
rate compounds, reach the mass spectrometer, which functions as a detec-
tor. Identification of particular substances is achieved on the basis of analy-
sis of the obtained mass spectrum, and the accelerant (which is usually
a multi-component mixture) is identified through comparison of the ob-
tained chromatogram with standard chromatograms, previously registered
and stored in the computer database.
RESULTS
The obtained results showed that, among the studied extinguishing
agents, only the use of extinguishing foam causes the introduction (into the
sample) of organic compounds which can be detected in the process of analy-
sis. This is illustrated by chromatograms presented in Figure 1: a standard
chromatogram of diesel oil, a chromatogram obtained as a result of the analy-
sis of a sample originating from a pile ignited by diesel oil and put out by extin-
guishing foam, and a standard chromatogram of Deteor foam generating
agent.
The compounds comprising the foam generating agent yield characteris-
tic, distinct peaks on the chromatogram.

The influence of selected fire-fighting
103
Standard chromatogram of diesel oil
^.2-methyl 1-propanol
1-butanol
(2-butoksyetoksy) ei
1-dodekanol
13.75	18.75	23.75	28.75
Fig. 1. A standard chromatogram of diesel oil; chromatogram obtained as a result of
the analysis of a sample originating from a pile ignited by means of diesel oil and put
out by means of extinguishing foam, and a standard chromatogram of Deteor® foam
agent.
CONCLUSIONS
Analysis of samples originating from the simulated fires, which were put
out by various fire-fighting agents, shows that only one of the examined
agents - the foam produced by Deteor foam agent - causes the introduction
of substances into the sample which can be detected in the process of analy-
sis. Their presence does not hinder the identification of the accelerant, pro-
vided that the person responsible for the analysis is aware of the fact that
the use of foam is linked to the introduction of these additional substances,
and that s/he can identify the signals coming from them on the chromato-
gram. Otherwise identification of the accelerant might prove to be difficult,
especially if the characteristic chromatogram picture for a given accelerant
has been distorted by complete evaporation of more volatile components of
the accelerant and by the presence of the products of pyrolysis. A wrong

104
R. Borusiewicz
identification might be made, or the accelerant might be correctly identified
but the compounds originating from the fire-fighting agent might be
wrongly identified as the accelerant’s impurities or admixtures. In the latter
case, a comparative analysis with liquid secured from the suspect will lead
to the wrong conclusion that they are two different mixtures. The research
carried out showed that the kind of agent used to extinguish a fire was not
the decisive factor in the detection of traces of accelerants. Observations
made in the course ofthe described experiments and analyses indicate, how-
ever, that the speed of the fire-fighting action, i.e. the time between igniting
and putting out the fire, certainly constitutes such a factor. This factor is
particularly important in the case of a mixture of volatile compounds (sol-
vents, petrol), but sufficiently speedy fire-fighting action is also a prerequi-
site for successful analysis in the case of mixtures of compounds with high
boiling points (kerosene, diesel oil or engine oils).
Acknowledgements:
The author extends his sincere thanks to the management and employees of the In-
stitute of Forensic Research in Cracow for making available equipment and mate-
rials, and for help given, without which these examinations would not have been
possible.
References:
1. Borusiewicz R., Fire debris analysis - A survey of techniques used for
   accelerants isolation and concentration, Problems of Forensic Sciences 2002,
   vol. 50, pp. 44-63.
2. Borusiewicz R., Zi^ba-Palus J., Zadora G., Application of head-space
   analysis with passive adsorption to the chromatographic detection and identi-
   fication of accelerants in the ATD-GC-FID system, Problems of Forensic Sci-
   ences 2002, vol. 51, pp. 87-105.
3. Cavanagh K., du Pasquier E., Lennard C., Background interference
   from car carpets - the evidental value of petrol residues in cases of suspected
   vehicle arson, Forensic Science International 2002, vol. 125, pp. 22-36.
4. Coulson S. A., Morgan-Smith R. K., Noble D., The effect of com-
   pressed air foam on the detection of hydrocarbon fuels in fire debris samples,
   Science & Justice 2000, vol. 40, pp. 257-260.
5. Dehaan J. D., Bonarrius K., Pyrolysis product of structure fires, Journal
   of the Forensic Science Society 1998, vol. 28, pp. 299-309.
6. Forensic science, handbook of analytical separations, vol. 2, Bogusz M. J. [ed.],
   Elsevier Science B.V., Amsterdam 2000.
7. Lennard C. J., Rochaix T., Margot P., A GC-MS database of target
   compound chromatograms for the identification of arson accelerants, Science &
   Justice 1995, vol. 35, pp. 19-30.

# WPŁYW WYBRANYCH ŚRODKÓW GAŚNICZYCH NA MOŻLIWOŚĆ DETEKCJI I IDENTYFIKACJI ŚLADÓW PŁYNÓW ŁATWOPALNYCH W PRÓBKACH POPOŻAROWYCH
Rafał BORUSIEWICZ
WPROWADZENIE
Po ugaszeniu pożaru pogorzelisko poddaje się dokładnym oględzinom, a w przy-
padkach, kiedy istnieje podejrzenie, że pożar był następstwem podpalenia, z miejsca
wytypowanego jako prawdopodobne ognisko pożaru pobiera się próbki do badań
laboratoryjnych. Badania te zwykle ograniczają się do poszukiwania śladów płynów
łatwopalnych, które są najczęściej używanymi środkami podpalającymi [6]. Chociaż
problem analizy pozostałości po pożarach nie jest zagadnieniem nowym [1], to
wykrycie i identyfikacja płynów łatwopalnych wciąż stanowi niełatwe wyzwanie.
Trudności wynikają z faktu, że w sprzedaży dostępnych jest wiele różnych środków,
którymi można się posłużyć do rozniecenia ognia, przy czym większość z nich to
wieloskładnikowe mieszaniny. Podczas pożaru związki wchodzące w skład tych
mieszanin odparowują w różnym stopniu, a niektóre z nich ulegają rozkładowi
termicznemu [3, 5, 6, 7]. Pirolizie podlegać mogą także spalane materiały, czego
efektem jest obecność w próbce licznych interferentów utrudniających analizę.
Dodatkowym czynnikiem mogącym wpływać na efektywność detekcji środków pod-
palających jest stosowanie różnego rodzaju środków gaśniczych, a przez to wprowa-
dzanie dodatkowych substancji do analizowanego materiału [4]. Celem prezentowa-
nych badań było określenie wpływu środków gaśniczych stosowanych do gaszenia
pożaru na możliwość detekcji i identyfikacji potencjalnych środków zapalających.
CZĘŚĆ DOŚWIADCZALNA
## Aparatura
W badaniach wykorzystano sprzęt firmy Perkin Elmer:
chromatograf gazowy AutoSystem XL sprzężony ze spektrometrem mas Tur-
boMass Gold i wyposażony w kolumnę kapilarną Elite 1 o średnicy wewnętrz-
nej 0,25 mm, grubości filmu fazy stacjonarnej 1 pm i długości 30 m;
automatyczny desorber termiczny (ang. automated thermal desorber - ATD)
TurboMatrix z modułem umożliwiającym ogniskowanie analitów na „zimnej
pułapce” i zestawem odpowiednich rurek ze stali nierdzewnej zawierających
złoże adsorbentu Tenax TA (politlenek 2,6-difenylo- -fenylenowy).
Jako gazu nośnego używano helu, regulując jego ciśnienie tak, by uzyskać
następujące wartości przepływów: przepływ gazu nośnego podczas termodesorpcji -
30cm3/min, przepływ gazu rozcieńczającego gaz nośny po termodesorpcji z „zimnej
pułapki” (ang. outlet split) - 30 cm3/min, przepływ gazu rozcieńczającego gaz nośny

Wpływ wybranych środków gaśniczych
106
po termodesorpcji ze złoża adsorbentu (ang. inlet split) — 7,8 cm3/min. Temperatura
linii transferowej wynosiła 250oC, a temperatura detektora 300oC.
Analizę chromatograficzną prowadzono z wykorzystaniem następującego pro-
gramu temperaturowego: temperatura początkowa 30oC utrzymywana przez 3 min;
przyrost 5oC/min do 120oC; przyrost 15oC/min do 270oC; temperatura końcowa 270oC
utrzymywana przez 7,5 min.
## Materiały i metodyka badań
W badaniach jako środków podpalających używano rozpuszczalnika uniwersal-
nego firmy Dragon (3 klasa środków podpalających wg American Society for Testing
and Materials - ASTM) i oleju napędowego (klasa 5 wg ASTM) pochodzącego
z lokalnej stacji benzynowej. Podpalano stosy składające się z materiałów typowych
dla wyposażenia mieszkań, a więc z drewna, drewna lakierowanego, płyty meblowej,
tworzyw sztucznych (polistyren, polietylen, polipropylen), dywanowej wykładziny
podłogowej i wykładziny PCV. Skład podpalanych stosów był jednakowy. Jednakowe
były także warunki spalania. Stosy dogaszano, kiedy ogień zaczynał samorzutnie
przygasać. Badano wpływ najczęściej stosowanych środków gaśniczych: piany gaśni-
czej uzyskanej z zastosowaniem środka pianotwórczego Deteor, gaśnicy proszkowej
oraz gaśnicy śniegowej. Próbki odniesienia uzyskano, pobierając materiał ze stosów
dogaszonych przez odcięcie dopływu powietrza. Aby zbadać wpływ danego środka
gaśniczego, podpalano dwa stosy - jeden przy pomocy rozpuszczalnika, a drugi
używając oleju napędowego i dogaszano je określonym środkiem gaśniczym. Po
ugaszeniu ognia z każdego ze stosów pobierano po 3 próbki do odpowiednio oczysz-
czonych, szczelnych słojów typu „twist”. Informacje o wpływie danego środka gaśni-
czego w odniesieniu do określonego płynu łatwopalnego pochodzą zatem z analizy
trzech próbek. Próbki analizowano zgodnie z opracowaną wcześniej i rutynowo
używaną procedurą, stosując zatężanie analitów przechodzących do fazy nadpo-
wierzchniowej na adsorbencie Tenax TA [5].
Sposób postępowania przedstawia się zatem następująco: do słojów zawiera-
jących próbki wkłada się stalowe rurki zawierające złoże adsorbentu, słoje szczelnie
zamyka i termostatuje przez 16 godzin w temperaturze 60oC. Po ostygnięciu rurki
umieszcza się w podajniku termodesorbera, w którym adsorbent jest poddawany
działaniu temperatury 325oC. Uwolnione w wyniku termodesorpcji anality trafiają
na kolumnę chromatograficzną, gdzie rozdzielają się i jako pojedyncze związki
osiągają pełniący funkcję detektora spektrometr mas. Identyfikacji poszczególnych
substancji dokonuje się na podstawie analizy uzyskanego widma masowego, a śro-
dek łatwopalny (który jest zwykle wieloskładnikową mieszaniną) jest identyfiko-
wany poprzez porównanie otrzymanego chromatogramu z zarejestrowanymi wcześ-
niej i zgromadzonymi w komputerowej bazie danych chromatogramami wzorco-
wymi.
WYNIKI
Uzyskane wyniki dowiodły, że spośród badanych środków gaśniczych jedynie
użycie piany gaśniczej powoduje wprowadzenie do próbki związków organicznych,
które mogąbyć wykryte w procesie analizy. Świadczą o tym przykładowe chromato-

Wpływ wybranych środków gaśniczych
107
gramy przedstawione na rycinie 1: chromatogram wzorcowy oleju napędowego,
chromatogram uzyskany w wyniku analizy próbki pochodzącej ze stosu podpalonego
olejem napędowym i ugaszonego pianą gaśniczą oraz chromatogram wzorcowy
środka pianotwórczego Deteor.
Związki wchodzące w skład środka pianotwórczego dają na chromatogramie
wyraźne, charakterystyczne piki.
WNIOSKI
Analiza próbek pochodzących z symulowanych pożarów, które gaszono różnymi
środkami gaśniczymi wskazuje, że tylko jeden z badanych środków gaśniczych — pia-
na gaśnicza uzyskiwana przy pomocy środka pianotwórczego Deteor - powoduje
wprowadzenie do próbek substancji, które mogąbyć wykryte w procesie analizy. Ich
obecność nie utrudnia identyfikacji środka łatwopalnego, jeśli tylko osoba prowa-
dząca analizę ma świadomość, że użycie piany gaśniczej wiąże się z wprowadzeniem
tych dodatkowych substancji i potrafi zidentyfikować na chromatogramie pocho-
dzące od nich sygnały. W przeciwnym wypadku identyfikacja środka podpalającego
może być trudna, szczególnie jeśli charakterystyczny dla danego środka zapa-
lającego wygląd chromatogramu zostanie zniekształcony przez całkowite odparowa-
nie bardziej lotnych składników płynu łatwopalnego i obecność produktów pirolizy.
Prowadzący analizę może dokonać błędnej identyfikacji lub też właściwie zidentyfi-
kować płyn łatwopalny, a pochodzące ze środka gaśniczego związki uznać za jego za-
nieczyszczenia lub domieszki. W tym drugim przypadku analiza porównawcza
z płynem zabezpieczonym u podejrzanego prowadzić będzie do błędnego wniosku, że
są to dwie różne mieszaniny.
Prowadzone badania wykazały, że rodzaj środka użytego do ugaszenia pożaru nie
jest czynnikiem decydującym o możliwości wykrycia śladów środków zapalających.
Obserwacje zebrane podczas prowadzenia opisanych eksperymentów i analiz wska-
zują natomiast, że czynnikiem takim jest z całą pewnością szybkość akcji gaśniczej,
tj. czas, jaki upływa od momentu podpalenia do ugaszenia pożaru. Czynnik ten jest
szczególnie istotny w przypadku mieszanin związków lotnych (rozpuszczalniki,
benzyna), ale dostatecznie szybka akcja gaśnicza warunkuje powodzenie analizy
również w przypadku mieszaniny związków wysokowrzących (nafta, olej napędowy
czy oleje silnikowe).
Podziękowania:
Autor serdecznie dziękuje kierownictwu i pracownikom Instytutu Ekspertyz Sądo-
wych w Krakowie za udostępnienie sprzętu, materiałów oraz pomoc, dzięki której
możliwe było przeprowadzenie zaprezentowanych badań.