Acta Poloniae Pharmaceutica ñ Drug Research, Vol. 69 No. 6 pp. 1023ñ1029, 2012
ISSN 0001-6837
Polish Pharmaceutical Society
CAPILLARY ELECTROPHORESIS SCREENING METHOD FOR SIX TRI- CYCLIC ANTIDEPRESSANTS IN HUMAN SERUM
KATARZYNA MADEJ*, MICHA£ WOèNIAKIEWICZ and KINGA KARABINOWSKA
Jagiellonian University, Faculty of Chemistry, Department of Analytical Chemistry, Laboratory for Forensic Chemistry, 3 Ingardena St., KrakÛw, Poland
Abstract: A capillary electrophoretic (CE) method for screening of six tricyclic antidepressants: amitriptyline, nortriptyline, imipramine, desipramine, doxepin and nordoxepin, in human serum, has been developed. The drugs were separated in a bare fused silica capillary (50 µm i.d.) using the background electrolyte: 50 mM CAPSO (pH 9.54) in methanol/water with KCl addition. For increasing the method sensitivity, the sample con- centration in the capillary (sample stacking) using pressure and electrokinetic injection has been applied. The standard addition method was used for calibration of the developed analytical procedure. The precision of the identification parameter (the relative migration time) and the quantitative parameter (the relative peak area) was within the range of 0.05ñ1.65 and 0.73ñ6.7 (RSD %), respectively. The detection limits were found to be 30 ng/mL for desipramine, 62.5 ng/mL for nortriptyline, and 50 ng/mL for remaining analytes.
Keywords: capillary electrophoresis, stacking, standard addition calibration, tricyclic antidepressants, human serum
Tricyclic antidepressant drugs (TCADs) belong to the first generation of psychotropic drugs which are still used for treatment of depression and other mental disorders. These drugs are efficacious but they are also dangerous with regard to their nar- row therapeutic window.
In biological material (plasma, serum, urine or hair), TCADs are mainly determined by chromato- graphic methods such as gas (1ñ3) or liquid (4ñ6) chromatography. For the last decade of the 20th cen- tury, capillary electrophoresis (CE) has been play- ing a significant role in the drug analysis field. However, generally, CE technique with the most commonly used spectrophotometric detection, shows relatively low sensitivity. It is caused by a short optical path, as well as by injection of very small sample volumes (i.e., nanoliters). Several approaches have been taken in order to solve this problem such as: modification of optical cell shapes (7), application of high sensitive detectors (laser induced fluorescence detector (8), mass spectrome- try detector (9) or electrochemical detector (10)), using effective on- and off-line preconcentration procedures, as well as analyte stacking techniques in the capillary (11). The last approach of lowering the analyte detection limit is especially convenient
and suitable for the capillary electrophoresis tech- nique. Under stacking conditions, a larger sample volume (5ñ50% of total capillary volume) may be injected into the capillary without disrupting peaks and loosing their resolution (12). The possibility of analyte stacking and other advantages of CE tech- nique, such as high separation potential and small sample and reagents consumption, makes CE nowa- days interesting tool for drug analysis in biological samples.
Generally, there is relatively a small number of CE procedures for determination of TCADs in bio- logical fluids employing preconcentration of these drugs in the capillary with the universal UV spec- trophotometry detection (13, 14). Chen et al. (13) proposed a sensitive CE method for determination of two tricyclic antidepressants: amitriptyline and its metabolite nortriptyline in human plasma using field-amplified sample stacking (FASS). Extracts of plasma samples (1 mL) were reconstituted with water and then electrokinetically injected (3 kV,
99.9 s) into a capillary after insertion of a 6 s water plug at pressure 10 psi. Detection of the drugs was
2.0 ng/mL for both amitriptyline and nortriptyline. The sensitive stacking-based CE method for the analysis of eight tricyclic antidepressants in human
* Corresponding author: e-mail: madejk@chemia.uj.edu.pl
1023

1024
KATARZYNA MADEJ et al.
Figure 1. Chemical structures of the examined tricyclic antidepressant drugs: a. amitriptyline (Ami), b. nortriptyline (Nort), c. imipramine (Imi), d. desipramine (Des), e. doxepin (Dox), f. nordoxepin (Nordox) and g. clomipramine (IS)

1025
Capillary electrophoresis screening method for six tricyclic antidepressants in human serum
serum has also been described (14). Stacking was caused by use of acetonitrile in the presence of sodi- um chloride as a sample medium. For analysis, 400
µL of spiked serum sample was mixed with acetoni- trile (600 µL) and sodium chloride, and then cen- trifuged. The supernatant was introduced in the CE system. Using a bubble-shaped capillary, the limits of detection were in the order of 5 ng/nL.
This paper focuses on development of a simple CE method for screening analysis of six tricyclic
Louis, USA). Spiking solutions were prepared by appropriate dilution of these stock solutions with water. Drug-free serum (control serum) was obtained from the blood bank in KrakÛw, Poland. Reference human serum (Medidrugô TCA S, MEDICHEM, Steinenbronn, Germany) containing six examined tricyclic antidepressants was supplied by Promochem (£omianki, Poland).
Reagents
CAPSO (3-[cyclohexylamino]-2-hydroxy-1- propanesulfonic acid) (Sigma Ultra) was purchased from Sigma-Aldrich (Stainheim, Germany). Methanol (HPLC gradient grade) was supplied by Merck (Darmstadt, Germany). Sodium hydroxide and potassium chloride, both of analytical grade, were obtained from POCh (Gliwice, Poland). Deionized water was used throughout.
antidepressants:
amitriptyline,
nortriptyline,
imipramine, desipramine, doxepin, and nordoxepin (Fig. 1) in human serum. For experimental condi- tions, the capillary zone electrophoresis (CZE) tech- nique was chosen and the sample was stacked by injecting it into the capillary by hydrodynamic or electrokinetic mode, in an organic (acetonitrile) or water-organic (0.01% H3PO4-methanol) medium. In order to find the optimal composition of the back- ground electrolyte, a 32 factorial design was used. A three point standard addition method was applied for calibration of the proposed analytical procedure. This approach was found to be effective for simulta- neous reduction of sample volume and time con- sumption.
Apparatus
The Prince 550 air thermostated capillary elec- trophoresis system (Prince Technologies, Emmen, The Netherlands) was used with a Lambda 1010 spectrophotometer (Bischoff, Leonberg, Germany) as a detector. Electrophoretic separation was con- ducted at 30 kV in a bare fused silica capillary of 50
µm i.d and 375 µm o.d. (Polymicro Technologies, Phoenix, USA), 100 cm long (66 cm to the detector). Drugs were detected by UV-light absorption at 210 nm. The initial background electrolyte was prepared by dissolving CAPSO (50 mM) in mixture of methanol/water (3:7, v/v), adjusted to pH 9.54 with 5 M NaOH. This mixture was then modified during optimization of the experimental conditions.
EXPERIMENTAL
Examined drugs and materials
Stock drug solutions of: amitriptyline, nor- triptyline, imipramine, desipramine, doxepin, nor- doxepin and clomipramine (IS) in methanol (1 mg/mL) were used for examination. All standard drugs were purchased from Sigma-Aldrich (St.
Table 1. Enhancement factors of the examined tricyclic antidepressants obtained in CE analysis under the stacking conditions.
a) ñ calculated as the ratio of the drug peak area obtained by sample stacking (sample injecting time was lengthened till all peaks remained baseline separated) and the drug peak area obtained by usual injection (we assumed 12 s as the injection time, which corresponded to a hydrodynamically injected sample size, equivalent to 1% of capillary volume).

Drug

Enhancement factorsa
Sample injection
Hydrodynamic mode
Electrokinetic mode
Sample medium
CH3CN
0.01% H3PO4/MeOH
CH3CN
0.01 % H3PO4/MeOH
Amitriptyline
3.9
5.4
4.1
3.7
Nortiptyline
3.3
6.0
6.0
3.4
Imipramine
3.3
5.8
4.0
3.4
Desipramine
3.2
5.9
5.3
3.8
Doxepin
3.2
4.8
3.8
3.6
Nordoxepin
4.2
6.5
4.6
3.7

1026
KATARZYNA MADEJ et al.
Figure 2. Optimization of separation conditions of the drugs (1 ñ Des, 2 ñ Nort, 3. ñ Nordox, 4 ñ Imi, 5 ñ Dox, 6 ñ IS, and 7 ñ Ami) by modification of the background electrolyte (50 mM CAPSO (pH 9.54) in methanol/water) composition: a. 30% (w/v) of methanol, b. 60% (w/v) of methanol, and c. 60% (w/v) of methanol and 0.143 mM of KCl. The concentrations of the drugs were as follows: 240 ng (Des), 400 ng (Dox), 500 ng (Ami, Nort, Imi and Nordox) and 2000 ng (IS). EOF ñ methanol

1027
Capillary electrophoresis screening method for six tricyclic antidepressants in human serum
Preparation of drug standard solutions and serum samples
Drug standard solutions were prepared in ace- tonitrile or in a mixture of 0.01% H3PO4 and methanol (1:1, v/v) by adding the drug stock solu- tions to obtain concentration of 20 µg/mL in appro- priate medium.
Lyophilized reference serum was prepared for analysis according to the procedure given by the manufacturer. After reconstitution, three (1ñ3) serum samples (0.5 mL) were pipetted and prepared in the following way: sample 1 remained untouched, sample 2 and 3 were spiked with standard drugs, respectively doubling and triplicating in drug con- centration compared to the certificated concentra- tions in the reference material. For estimation of the detection limits of the analytes examined, the con- trol serum samples were spiked with appropriate amounts of the drugs tested.
All samples were subjected to liquid-liquid extraction according to the following procedure. First, all samples were diluted with water (1:1, v/v) and spiked with the internal standard (2 µg of clomipramine). To each sample, 3 mL of 0.6 M NaOH and then 5 mL of n-hexane with isoamyl alcohol (99:1, v/v) were added and mixed. Then, the whole content was agitated for 10 min and cen- trifuged (4000 rpm) for 10 min. The organic layer (4 mL) was transferred successively into a 0.5 mL con- ical tube, and evaporated in a nitrogen stream mild- ly heated to 42OC. The residue was dissolved with 120 µL of the extracting mixture (n-hexane/isoamyl alcohol, 99:1; v/v) and vortexed for 0.5 min. The analytes were then re-extracted into 25 µL of 0.01%
H3PO4. Twenty µL of the aqueous layer was mixed with 20 µL of methanol, and injected into the capil- lary.
Measurement procedure
A new capillary was conditioned by flushing with 1 M NaOH (30 min), 0.5 M NaOH (5 min), deionized water (5 min) and the background elec- trolyte (15 min) in sequence. The measurement pro- cedure consisted of three main steps: 1) washing the capillary with freshly prepared background elec- trolyte (2 min), 2) sample injection in hydrodynam- ic (50 mbar) or electrokinetic mode (5 kV) from 12 to 96 s, and 3) separation of analytes under 30 kV. Between measurements the capillary was purged using the following sequence of reagents: 0.5 M NaOH (2 min), water (3 min) and the background electrolyte (3 min).
RESULTS AND DISCUSSION
This study covered the most important classic antidepressants including their metabolites: ami- triptyline, nortriptyline, imipramine, desipramine, doxepin and nordoxepin. Clomipramine, a drug from the same pharmaceutical group, was chosen as the internal standard.
The enhancement in the sensitivity of CE analysis was achieved by use of stacking conditions, i.e., a standard drug mixture was dissolved in a low conductivity medium (acetonitrile or mixture 0.01% H3PO4/methanol, 1:1, v/v) and then injected hydro- dynamically or electrokinetically into the capillary. Enhancement (stacking) factors, for all examined
Table 2. Optimization of the background electrolyte (50 mM CAPSO (pH 9.54) in methanol/water with salt addition) composition.
a) the global sum of peak resolutions was calculated as the median from three repeated measurements (in calculations, peak areas were taken into account). b) no salt was added.
Point No.
MeOH/water (%, w/v)
Salt cation
Salt concentration (mM)
Ra (n = 3)
0
30
ñb
0
7.19
1
30
Na
0.143
8.21
2
30
Na
0.072
8.17
3
30
K
0.072
7.74
4
30
K
0.143
8.17
5
60
Na
0.143
8.77
6
60
Na
0.072
8.29
7
60
K
0.072
8.64
8
60
K
0.143
9.00
9
60
ñb
0
7.73

1028
KATARZYNA MADEJ et al.
drugs were calculated by dividing the drug peak areas obtained by means of sample stacking (sample injecting time was lengthened from 24 to 96 s till all peaks remained baseline separated) and by usual injection (we assumed 12 s as the initial injection time, as it corresponds to the hydrodynamically injected sample size equivalent to 1% of the capil- lary volume). The best stacking conditions (the highest values of enhancement factors) for the stan- dard drug solutions were: hydrodynamic injection mode and sample medium ñ mixture of 0.01% H3PO4 and methanol (1:1, v/v) (Table 1).
In order to improve the separation efficiency of the drugs, the initial composition of the background electrolyte was optimized taking into account three factors: 1. ratio of methanol to water in the back- ground electrolyte, 2. kind of salt cation (Na+ or K+) added to the electrolyte, 3. concentration of salt added to this electrolyte. Each factor was examined on two value levels and the analyses were performed according to a 32 factorial design. As the optimum criterion, the global sum of peaks resolutions (R) between all adjacent drugs (iñj), including internal standard were selected. A significant increase in res- olution was predicted after some preliminary research, thus the injection time was prolonged to 1 min.
R =  Ri-j
where:
tj ñ ti
obtained from the experiments, the following com- position of the separation electrolyte was chosen as the optimum one (Table 2; experimental point N 8, response R = 9.00): 0.143 mM KCl in methanol/water (60:40; w/v). The protonation degree of the drugs was lowered by increasing the amount of methanol in the background electrolyte, but there was only a little improvement in separation of two desmethyl amine compounds (nortriptyline and nordoxepin), however, the rest of the tested drugs were not baseline separated (compare Figs. 2a and 2b). The substantial improvement of separation efficiency was achieved by addition of KCl salt into the background electrolyte. This was caused by adsorption ability of cation K+ on the capillary sur- face, which resulted in reduction of the electroos- motic flow and also by increasing the electric field
(15) (Fig. 2c).
Comparing the findings in the performed examinations with the results obtained by other authors, it may be stated that the developed method requires comparable (14) or even smaller amounts of the examined body fluid (13) (taking into account requirement of at least two samples analysis). The sample preparation method used by Galeano-Diaz et al. (14) was simpler (only enrichment of a serum sample with sodium chloride and then precipitation with acetonitrile was required) and CE measurement was faster (ca. 6 min) but not all examined drugs were completely separated and for lowering detec- tion limits appropriate bubble shape cell (bubble capillary) was required. The detection limits in the proposed procedure are higher than those reported in (13, 14) but they are low enough to apply this method for determination of the studied drugs in human serum at therapeutic concentrations.
Riñj = 2 ñññññññññ
wi + wj
ti and wi ñ retention time and peak width of peak I; tj and wj ñ retention time and peak width of peak j; If Ri-j = 1.5 then Ri-j was assumed to be 1.5.
At optimal conditions, the response R should be a maximum one. On the basis of the results
Table 3. Validation parameters of the developed CE method.
a) ñ ratio of the examined drug migration time and the internal standard migration time. b ñ ratio of the examined drug peak area and the internal standard peak area. c ñ lower concentration drug level (120, 200 and 250 ng/mL for desipramine, doxepin and the rest of examined drugs, respectively). d ñ higher concentration drug level (360, 600 and 750 ng/mL for desipramine, doxepin and the rest of examined drugs, respectively).

Drug

Repeatability of

Limit of detection [ng/mL]

Linearity correlation coefficient (r2)

Accuracy RE [%]

(TMD/TMIS)a
(AD/ AIS)b
[RSD, %]
[RSD, %]
C c
1
C d
2
C c	C d
1	2
Amitriptyline
0.24
0.05
2.31	5.38
50.0
0.999
4.0
Nortriptyline
1.04
1.74
1.03	4.32
62.5
0.980
4.0
Imipramine
0.24
0.55
1.96	6.70
50.0
0.999
4.4
Desipramine
1.11
1.90
0.76	1.19
30.0
0.975
5.1
Doxepin
0.36
0.20
0.78	4.76
50.0
0.999
4.1
Nordoxepin
1.16
1.65
0.73	1.10
50.0
0.979
4.4

1029
Capillary electrophoresis screening method for six tricyclic antidepressants in human serum
For validation of the analytical procedure, sev- eral analytical parameters of the developed method were determined. The precision was assessed by four times repeated analyses of serum specimens containing known concentrations (two concentra- tion levels, Table 3) of the drugs investigated. By these means, the repeatability of both qualitative (relative migration time) and quantitative (relative peak area) parameters were estimated. The detection limits (LODs) for all drugs tested in the serum were determined by estimation of the minimum concen- tration equivalent to five times of the background noise signal. The linearity of the method was stud- ied for each examined drug in serum samples in the following concentration ranges: 120ñ360 ng/mL for desipramine, 200ñ600 ng/mL for doxepin and nor- doxepin, and 250ñ750 ng/mL for amitriptyline, nor- triptyline and imipramine, and the correlation coef- ficient (r2) was calculated on the basis of three con- centrations (points) for each drug. The accuracy of the method was calculated as the relative error RE = [(desired value ñ obtained value) /desired value] ◊ 100%. The obtained values of the analytical param- eters are presented in Table 3.
of (3 ◊ 0.5 mL) serum samples, containing the examined drugs at therapeutic concentration levels. The proposed CE procedure may be an alternative for the chromatographic methods commonly used for examination of these antidepressants in clinical and forensic laboratories.
REFERENCES
1.
Winecker R.E.: Meth. Mol. Biol. 603, 45 (2010).
Yazdi A.S., Razavi N., Yazdinejad S.R.: Talanta 75, 1293 (2008).
Rana S., Urlats V.P., Ross W.: J. Anal. Toxicol. 32, 355 (2008).
Mercolini L., Mandrioli G., Finizio G., Boncompagni G., Raggi M.A.: J. Sep. Sci. 33, 23 (2010).
Breaud A.R., Harlan R., Di Bussolo J.M., McMillin G.A., Clarke W.: Clin. Chim. Acta 411, 825 (2010).
Woüniakiewicz M., Wietecha-Pos≥uszny R., Garbacik A., Koúcielniak P.: J. Chromatogr. A 1190, 52 (2008).
El-Hady D.A., El-Maali N.A.: Talanta 76, 138 (2008).
Deng Y.-H., Wang H., Zhong L., Zhang H.-S.: Talanta 77, 1337 (2009).
Boatto G., Nieddu M., Dessi G., Manconi P., Cerri R.: J. Chromatogr. A 1159, 198 (2007). Sun X., Niu Y., Bi S., Zhang S.: J. Chromatogr. B 870, 46 (2008).
Dawid M., Breadmore M.C., Guijt R.M., Haddad P.R.: J. Chromatogr. A 1217, 386 (2010).
Shihabi Z.K.: J. Chromatogr. A 902, 107 (2000).
Chen C.-C., Wu S.-M., Huang Y.-H., Ko W.-
K., Kou H.-S., Wu H.-L.: Anal. Chim. Acta 517, 103 (2004).
Galeano-DÌaz T., Acedo-Valenzuela M.-I.,
2.
3.
4.
5.
6.
7.
CONCLUSIONS
8.
A simple and sensitive CE screening method for six tricyclic psychotropic drugs in human serum has been developed. An experimental design (32 fac- torial) was used to find optimal composition of the separation electrolyte. As the optimum criterion, the global sum of peaks resolutions (R) between all adjacent drugs (iñj), including the internal standard has been selected. In order to calibrate the proposed analytical procedure, the standard addition method was used instead of the method of the set of stan- dards, which is commonly used in analysis of bio- logical fluids for drug determination. The reason for choosing the standard addition method was that this method (in contrast to the latter one) was hoped to compensate the matrix effects, which could be expected in the case of analysis of biological mate- rial, especially in the case of decomposed forensic samples.
The combination of sample preconcentration in the capillary with a three point standard addition method enables analysis of relatively small volumes
9.
10.
11.
12.
13.
14.
Mora-
DÌez
N.,
Silva-RodrÌguez
A.:
Electrophoresis 26, 3518 (2005).
Porras S.P., ValkÛ I.E., Jyske P., Riekkola M.- L.: J. Biochem. Biophys. Methods 38, 89 (1999).
15.
Received: 02. 09. 2011